STATEWIDE EMS OPERATIONS AND COMMUNICATIONS RESOURCE MANUAL

Revisions Prepared by:

The California Emergency Medical Services Authority

Tonya Thomas, EMT-B

EMS Communications Coordinator

California EMS Authority

((

Donna Nicolaus, Manager

EMS Systems Division

California EMS Authority

((

Bonnie Sinz, RN

EMS Systems Division Chief

California EMS Authority

((

Daniel R. Smiley

Chief Deputy Director

California EMS Authority

((

Steven Tharratt, MD, MPVM

Director

California EMS Authority

((

Kimberly Belshé

Secretary

California Health and Human Services Agency

((

Arnold Schwarzenegger

Governor

Table of Contents

INTRODUCTION	3

PURPOSE	3

SUMMARY	3

OPERATIONAL INFORMATION	3

FCC RULES AND REGULATIONS	3

1.   General Requirements	4

2.   Station Identification	4

3.   Operator Requirements	4

OPERATING PRACTICES	5

1.   Equipment Familiarization	5

2.   Communications Skills	5

RADIO THEORY	7

1.   Land Mobile Radio Frequency Bands	7

2.   VHF Low Band	7

3.   VHF High Band	8

4.   UHF BAND	8

5.	 700 MHz Band	8

6.   800 MHz Band	9

RADIO FREQUENCY INTERFERENCE	9

1.   Co-Channel Interference	9

2.   Receiver Desensitization	9

3.   Transmitter Noise	10

4.   Intermodulation Interference	10

5.   Equipment and Interference Rejection	10

CONCEPTS OF EMS COMMUNICATIONS	11

1.   General	11

2.   Citizen Access	11

3.   Vehicle Dispatch and Response (VDR)	11

4.   Automatic Vehicle Location	11

5.   Crew Alert Paging	11

6.	Local Medical Coordination (LMC)	12

7.	Statewide Medical Coordination (SMC)	12

8.	On-Scene Coordination (OSC)	12

9.	Medical Resource Coordination (MRC)	12

CALIFORNIA EMS ALLOCATIONS	13

GENERAL	13

INTRODUCTION TO TABLES	13

1.  Radio Channel Information	13

2.	 Emergency Department Information	15

3.   EMS Provider	15

Alameda County EMS Agency	16

Contra Costa County EMS Agency	19

El Dorado County EMS Agency	22

Central California EMS Agency	24

Coastal Valleys EMS Agency	29

Imperial County EMS Agency	33

Inland County EMS Agency	35

Kern County EMS Agency	Error! Bookmark not defined.

Los Angeles County EMS Agency	44

Marin County EMS Agency	55

Merced County EMS Agency	57

Monterey County EMS Agency	59

Mountain Valley EMS Agency	63

North Coast EMS Agency	71

Northern California EMS Agency	75

Orange County EMS Agency	83

Riverside County EMS Agency	88

Sacramento County EMS Agency	92

San Benito County EMS Agency	Error! Bookmark not defined.

San Diego County EMS Agency	98

San Francisco City and County EMS Agency	103

San Joaquin County EMS Agency	107

San Luis Obispo County EMS Agency	110

San Mateo County EMS Agency	112

Santa Barbara County EMS Agency	115

Santa Clara County EMS Agency	118

Santa Cruz County EMS Agency	122

Sierra-Sacramento Valley EMS Agency	124

Solano County EMS Agency	129

Tuolumne County EMS Agency	131

Ventura County EMS Agency	133

GENERAL ACRONYMS	135

FCC CODES AND NAMES OF RADIO SERVICES	139

GLOSSARY	140

ADDENDUM	170

This document was supported by the Preventive Health and Health Services Block Grant from the Centers of Disease Control and Prevention (CDC) and a grant from the Department of Commerce.  Points of view or opinions expressed in this document are those of the authors and do not necessarily represent the official views of CDC or policies of the Department of Commerce.

# INTRODUCTION

## PURPOSE

This Emergency Medical Services (EMS) Operations and Communications Resource Manual has been developed by the State of California Emergency Medical Services Authority (EMS Authority) primarily as an operational manual to be available to all local EMS agencies. It contains useful information for EMS operations, as well as provides the data necessary to enable radio communications during transport operations within the state.

The manual is also intended to be useful for instructional purposes in training programs for Emergency Medical Technicians (Basic, Intermediate, and Paramedics) through its operational approach and sections on radio frequency communications.

## SUMMARY

The Operational Information section of this manual contains requirements of the Federal Communications Commission (FCC) rules relating to communications operations, information on standard operating practices, discussion of the various radio frequency bands, and an explanation of primary sources of interference which can disrupt normal communications, as well as a definition of the concepts involved in EMS communications.

The California EMS Allocations section contains an alphabetical listing, by local EMS agency, of all radio frequencies for EMS operations within the state, as well as hospital emergency department addresses, telephone information, and helipad coordinates. Radio dial codes are shown for those counties using selective addressing for radio communications with hospitals. In addition, the telephone number of each ground and air ambulance provider is included showing the quantity of ALS, BLS, and air transport permitted vehicles licensed to each. The most recent information added to this manual for each local agency are coordinates for commonly used helispots for ground to air transfers that may be designated as an emergency landing zone.

# OPERATIONAL INFORMATION

## FCC RULES AND REGULATIONS

The Federal Communications Commission (FCC) prescribes a framework of rules to govern the transmission of radio signals. Under these rules, each user of the radio spectrum must be eligible to operate on given frequencies and be authorized to do so. The FCC rules and regulations are organized into various parts and subparts which address the FCC’s practice and procedure as well as the particulars of the radio services into which the frequency spectrum is allocated, including frequency assignment policy and operating requirements. Public Safety communications including the Special Emergency Radio Service is governed by Part 90 of the FCC Rules.

1.   General Requirements.

Licensees of radio systems have direct responsibility for the proper operation of each transmitter licensed. They must ensure that radios are used in accordance with the FCC rules and for purposes directly related to the particular activities for which they are licensed. Priority is to be given to communications involving the imminent safety of life and property, but licensees are required to keep transmission times to a minimum and employ efficient operating procedures to maximize the utilization of the frequency spectrum.

With the exception of those frequencies assigned for the exclusive use of a licensee in the frequency bands 470-512 MHz and 806-824/851-869 MHz, frequency assignments are considered to be available on a shared basis only. All licensees, and applicants for new licenses, are required to cooperate in the selection and use of frequencies in order to reduce interference and make the most effective use of the authorized radio facilities.

Licensees are required to take reasonable precautions to avoid causing harmful interference to other radio users. This includes monitoring the operating frequency for communications in progress and other such necessary measures to minimize the potential for interference.

### 2.   Station Identification

For public safety communications systems, each station or system of stations must be identified by the transmission of the assigned FCC call sign during each exchange of transmissions, or once every 30 minutes if operation is continuous. Identification must be made by voice in the English language or, alternatively, may be made by automatic means using the International Morse Code. In addition to the call sign, station or unit identifiers may be transmitted as necessary or desirable for system operation.

### 3.   Operator Requirements

No operator license or permit is required for the individual personnel operating radio equipment. Any person having the consent of the system licensee may provide authorized communications on behalf of the licensee. Cooperating users of other’s radio systems should maintain a written agreement of use for such systems.

The licensee will at all times exercise responsibility for operations and is expected to provide observation, servicing and maintenance as often as necessary to ensure compliance with all applicable rules. Operators should be trained initially and recurrently regarding the complex nature of EMS communication systems utilized, as well as those local systems granting and expecting access.

## OPERATING PRACTICES

In the course of providing emergency health care to the public, many of the individual participants practicing in the EMS system are required to communicate with one another via two-way radio facilities. Good operator practice is essential to the effectiveness and efficiency of any public safety communications system. For EMS, good practice followed by EMTs/paramedics, dispatchers, physicians and emergency department nursing personnel relates directly to a reduction in response time which in turn saves lives, reduces further injuries and minimizes suffering.

### 1.   Equipment Familiarization

A first step in proper communications techniques is a familiarization with the radio equipment to be used by the operator. There are many different brands and types of radio equipment items that EMS personnel will encounter in their work, and manufacturers are continually introducing new products which will always present new educational challenges. As a minimum, communications systems are comprised of mobile and portable radios, base/repeater stations and various radio control devices. Additionally, they may include more complex aspects such as telemetry, satellite receiver voting systems, vehicular repeaters and trunked operations.

EMS personnel should take sufficient time to learn the correct operation of each item of communications equipment that they use. They should fully investigate the various features of that equipment in order to maximize the extent to which the equipment assists in delivery of emergency services. Operators are encouraged to ask questions of their colleagues, equipment maintenance technicians and manufacturers’ representatives to ensure understanding.

Most EMS radio systems provide the flexibility to communicate to various hospitals and dispatch centers via the use of selectable channels, tones, and codes. EMS personnel must understand the procedures for such selections which are normally based on patient destination, status, local area, or combination of similar factors. EMS providers should include quick-reference documentation for use by field personal that is designed to be utilized during emergent circumstances. Hospital providers should also keep similar reference materials readily available at their radio positions.

### 2.   Communications Skills

The objective of radio communications in EMS is to convey information in a concise and accurate manner. The communications skills exhibited by operator personnel can have a positive influence on the outcome of a particular event.

A.   Operating

For most EMS providers there is generally a protocol (written or unwritten) to govern radio communications. If unwritten, such procedures are probably defined by tradition. No attempt is made here to establish a particular mode of operation however; certain key points are highlighted for the benefit of operator personnel.

Follow standard protocol established by the EMS service. It may address the manner in which calls are to be placed from one unit of the service to another and govern the manner in which messages are formatted.

Maintain channel discipline. Courtesy and respect for the communications of others sharing the radio channel go a long way in preserving order, especially in congested geographic areas with much radio traffic. Monitor the channel before transmitting to prevent interference to other users. Think ahead and keep transmissions short and to the point to maximize airtime.

Practice verbal communications skills. Speak distinctly, at a moderate rate, and directly into the microphone or handset to maximize intelligibility. Keeping the microphone close to the mouth overcomes background noise and permits the operator to speak in a normal tone of voice. Shouting is to be avoided as it results in audio distortion.

Use plain language to describe a particular condition or event when in doubt of the appropriate aural brevity code which might otherwise be used. Individuals under stress may find it easier to relate clear and simple descriptions.

B.   Technical Considerations

Key your transmitter before engaging in speech. The complexities in communications system design often introduce delay in the time it takes to turn on the various components comprising the system. Transmitters take time to come up to full power output, tone squelch decoding equipment requires time to open receivers and receiver voting systems take time to select the best receiver. While these events generally are accomplished in less than one second’s time, there are many voice transmissions that could be missed in their entirety if the operator did not delay slightly before beginning his/her voice message. Pausing one second after depressing the push-to-talk button on the microphone or handset is sufficient in most cases to prevent missed words or responses.

Transmissions should generally be kept to less than 20 seconds, or within the time specifically allocated by the system. Most radio systems limit transmissions to less than 30 seconds to prevent malfunctioning transmitters or accidentally keyed microphones from dominating a system, and will automatically stop transmitting at the expiration of the allowed time cutting off additional audio.

Keep loudspeaker clear of clutter. Papers or other materials covering or obstructing loudspeakers can diminish receiver audio and alter intelligibility.

Avoid turning receiver volume too low. A low setting may fail to attract the operator’s attention to an incoming call.

# RADIO THEORY

### 1.   Land Mobile Radio Frequency Bands

In the spectrum between 25 MHz and 1,000 MHz are various bands allocated by the FCC for two-way mobile radio communications known as land mobile radio bands. They have the following common designations:

| 25 – 50 MHz | VHF Low Band |
| --- | --- |
| 150 – 174 MHz | VHF High Band |
| 450 – 470 MHz | UHF Band |
| 470 – 512 MHz | UHF TV Sharing (specific areas only) or “T” Band |
| 806 – 824/851 – 869 MHz | 800 MHz Band |

Each of these frequency sub-bands are widely used for two-way land mobile radio communications in the Public Safety Radio Services. The choice as to which one is best for a particular operation depends on the frequency availability, the particular type of communications system required, the radio coverage area required, and many other engineering factors. Because of the consistently high demand for radio frequencies within the past few years, it usually becomes a matter of frequency availability rather than preference. However, when it is possible to choose the operating frequency of a radio system, the characteristics for each band should be carefully considered. Each frequency band has its unique properties which must be factored into the overall engineering of the system design for each user.

### 2.   VHF Low Band

VHF Low Band has, as its advantage, the farthest coverage distance (other factors being equal) of any of the land mobile frequency bands. Given the same operating conditions (transmitter power and antenna height) low band will generally “talk” farther base-to-mobile and mobile-to-mobile. It is also better suited for traversing hilly terrain and penetrating heavily wooded areas than higher frequencies.

Unfortunately, VHF Low Band has several disadvantages not shared by higher frequencies. It is commonly affected by skip interference (which occurs when radio signals are reflected from the upper atmosphere at great distances from the location of origin). It is not uncommon to receive stations over 2,000 miles away, and such occurrences tend to disrupt local communications. VHF Low Band is also affected to more of an extent by man-made noise sources than higher frequencies. Automobile ignition systems, motors, commercial power lines and electric fences in the vicinity of radio receivers may create so much electrical noise that the desired radio signals may be masked at times to the point that they become unusable.

Additionally, and for some of the above reasons, VHF Low Band does not generally fare well in urban environments. In addition to the above shortcomings, antennas for VHF Low Band communications must be relatively large compared to higher frequency antennas; attempts to shorten these antennas for convenience or practicality results in inefficiency and reduced coverage area.

### 3.   VHF High Band

Within the 150 MHz range of VHF High Band, skip interference is considerably reduced. Manmade noise sources also are not of as much concern, and better penetration into metropolitan area environments is realized. Due to the shorter wavelength of VHF High Band, it becomes practical to use shorter antennas that exhibit greater gain than with similar lengths at VHF Low Band.

VHF High Band has typically been, for the above reasons, the band of choice for many applications. In many parts of the United States, however, VHF High Band has become so congested, particularly in metropolitan areas, that interference of several kinds from neighboring systems is often received. Point-to-point co-channel interference is particularly severe in view of the simplex-type allocation of these frequencies by the FCC. VHF High Band is also characterized by a somewhat shorter communications range than VHF Low Band, especially on a mobile-to-mobile basis.

### 4.   UHF BAND

UHF Band communications are virtually free from skip interference and electrical noise when compared to lower bands. At 450 MHz, the radio waves are physically shorter than VHF Low Band or High Band such that they have an ability to easily reflect off of common hard surfaces. Thus, the UHF Band is often an excellent choice for penetrating into, and around, heavy building structures in urban areas.

As frequency is increased however, losses due to hills and foliage also increase. The UHF Band has more difficulty transmitting signals over hilly or irregular terrain than with lower bands. Hills tend to block the signal more severely and can significantly reduce range. Also, absorption of the signal by trees and other foliage is more prevalent at UHF and must be factored into any UHF system design. Since mobile-to-mobile range is significantly less than that accommodated by the lower frequency bands, repeater stations are commonly used to relay transmissions between mobile units.

Most EMS systems utilize the Emergency Medical Service UHF MED channels within this band.

### 5.	 700 MHz Band

Until recently, the FCC has licensed most of the 700 MHz spectrum to television broadcasters for analog television. This spectrum was deemed desirable for both broadband communications in general and public-safety uses due to the unique propagation characteristics of this band and the fact that many urban areas currently use the 800MHz band.  This spectrum is divided into two bands -- the lower and upper 700 MHz. The lower band is 48 MHz wide, and the upper band is 60 MHz wide. Of the upper 60 MHz, 24 MHz is reserved for public safety use since this portion of the spectrum is contiguous with the existing 800 MHz band already in use by public safety.  The FCC auctioned large portions of the lower 700 MHz band to commercial carriers who will use the spectrum for broadband applications, while the upper 700 MHz band is divided in to several sub-bands. Public Safety will use the upper-most band of the 700 MHz while the adjacent “D block” band will be auctioned by the FCC in an effort to create a Public / Private partnership which will operate a nationwide broadband network, with priority access granted to public safety.

The lower a radio signal's frequency, the farther it can propagate provided that no objects obstruct its paths. Conversely, the higher a frequency, the more easily it can penetrate dense obstacles like walls and buildings. Higher frequencies also tend to be used to support trunked radio systems and high speed data networks which are more efficiently utilize the spectrum, enabling radios to transmit more data for each hertz of frequency band. As a result, the 700-MHz band should provide better coverage in urban areas for public safety when used to support a properly designed and implemented system than current cellular bands do.

### 6.   800 MHz Band

The characteristics of the 800 MHz Band are very similar to the UHF Band except that the negative aspects are somewhat accentuated. With the proper engineering and design however, the 800 MHz Band can be a viable alternative to the lower frequencies. Beyond any question it is currently the one band for which the latest communications technology is offered. It is also the only land mobile frequency band that (at least today) is generally less congested than lower bands. In many areas of the United States, including areas of California, the 800 MHz Band is the only band in which new channel assignments are currently available. EMS units utilizing 800 MHz systems are typically affiliated with a local agency hosting such systems. These systems are usually based on a complex trunked radio network. The trunked system administrator must grant access to and normally provides and/or maintains equipment of the local EMS providers to access these systems.

## RADIO FREQUENCY INTERFERENCE

The ability to communicate by radio may be significantly affected by other communications systems operating on the same or different frequencies. Most interference that occurs is unintentional and can be difficult to identify if it can be detected at all.

### 1.   Co-Channel Interference

This type of interference is most readily identified and occurs from different radio systems sharing the same frequency. Ideally, systems are authorized with sufficient geographic distance between them such that one system does not hear the other system and vice-versa. On occasion, however, atmospheric conditions will support better than normal communications range and audible signals of the distant system are received. Depending on the strength of these co-channel signals, normal communications may be disrupted or precluded. Co-channel interference will result on shared radio channels, such as the UHF MED channels, unless careful coordination of frequency assignment and usage is ensured.

### 2.   Receiver Desensitization

When using a radio receiver in the physical vicinity of a transmitter operating on a frequency close to that which the receiver is tuned (but not directly on it), the receiver’s ability to hear weak on-channel signals is impaired. The effect may be to lose a desired transmission completely or it may appear to be partially cut off.

### 3.   Transmitter Noise

Transmitters are not perfect devices and will radiate some amount of noise in addition to the primary signal. This noise appears on either side of the transmitted signal and can interfere with nearby receivers tuned to other frequencies. The end result is similar to what is experienced with receiver desensitization, but the mechanism of interference is masking of desired signals by the noisy transmitter.

### 4.   Intermodulation Interference

Inter-modulation interference, or “inter-mod”, is caused when two or more radio signals of different frequencies combine to create yet other frequencies (a process known as mixing). If one of the new frequencies produced happens to occur on a desired receiver frequency, interference may result to desired signals. Such frequency mixing often occurs either in a transmitter or a receiver.

Transmitter-produced inter-mod occurs when strong radio signals are combined in the power amplifier of a transmitter, and the mix frequencies are re-radiated along with the intended signal. If one of the mix frequencies is heard in the affected receiver, it may be possible to detect the audio of the interfering signal as comprised of multiple voices in accordance with the number of transmitters participating in the mix.

Receiver-produced intermod manifests itself when two or more strong off-frequency signals combine in the receiver electronic circuitry to create still other frequencies through mixing. Like the transmitter-produced case, if one of the resultant frequencies is nearly the same as the frequency to which the receiver is tuned, the inter-mod signal will compete with the desired received signal.

Inter-modulation interference can generally be identified by listening to the interfering signal, because it will usually be comprised of two or more voices and is likely to suddenly cease when one of the transmitters contributing to the mixing process is turned off. However, the process of identifying the participants so as to remedy the interference problem may not be so easy since they may be located at other radio sites and operate in different radio services. Additionally, inter-mod is produced in sites other than transmitters and receivers. These sites of production may include antennas, metallic flashing on rooftops, rusted or corroded mechanical joints of antenna towers, and on occasion, rusted automobile bodies or similar materials.

### 5.   Equipment and Interference Rejection

While the occurrence of interference in the radio environment cannot be totally eliminated, it can often be controlled to the point where its harmful effects minimize the disruption of communications. For the public safety services, the purchase of communications equipment exhibiting quality in the design of interference rejection circuitry will do much for dealing with the problems of receiver desensitization, transmitter noise and inter-modulation interference. Additionally, proper system engineering is required to provide for ancillary protective devices (such as radio frequency filters and isolators) where needed.

## CONCEPTS OF EMS COMMUNICATIONS

### 1.   General

An EMS communications system must provide the means by which emergency medical resources can be accessed, mobilized, managed, and coordinated in both normal and adverse situations. An EMS communications system must therefore, employ sufficient communications paths and operational capabilities among all participants to facilitate the functional EMS communications concepts described in the remainder of this section.

### 2.   Citizen Access

The EMS communications system must have the ability to receive and process any incoming requests that report emergencies and require emergency medical assistance. All individuals shall be able to summon help rapidly in an emergency situation whether for medical, police, fire, rescue, or other emergency need. Local, statewide, and national uniformity is required to fully enable this concept.

The State of California 9-1-1 Plan provides for a cohesive statewide emergency telephone number system to provide citizens with this rapid direct access to public safety agencies.

### 3.   Vehicle Dispatch and Response (VDR)

On notification of need for emergency medical assistance, the communications system must enable prompt dispatch of EMS vehicles (including notification of rotor-wing aircraft) to the location of the emergency. The communications system must further enable dispatchers to communicate with responding vehicles while in route to the scene, while at the scene, while in route to hospital emergency department facilities, and during their return to availability for further assignment.

### 4.   Automatic Vehicle Location

Use of automatic vehicle location (AVL) systems provide real-time geographic location of vehicles to ensure the nearest available vehicle is dispatched to the scene of an incident. Additionally, an AVL system displays vehicle positions to dispatchers on either tabular and/or graphic displays as well as providing the information necessary to a computer-aided dispatch (CAD) program when utilized in a system status management structure.

### 5.   Crew Alert Paging

As a sub concept to vehicle dispatch and response some EMS communications systems, as determined by local procedure, may require the direct alerting of EMS personnel either individually or in groups, through the use of either monitor or paging receivers, station public address system, or by means of two-way handheld portable radios with a selective call capability. Crew alert paging may also include call-specific information via digital pager or paper printout.

### 6.	Local Medical Coordination (LMC)

The EMS communications system must provide EMS field personnel with a channel of communications that permits the exchange of vital information between both EMS field personnel and emergency department personnel while the patient is at the scene of the medical emergency and while being transported to an emergency department facility. Typical LMC communications involve patient status and destination, as well as information permitting or requesting medical control decisions regarding patient care.

### 7.	Statewide Medical Coordination (SMC)

In addition to LMC capability, the EMS communications system must provide a communications channel to enable medical coordination between EMS field personnel and emergency department personnel during situations in which a vehicle is out of its prime area and unable to access an emergency department using their assigned LMC channels, or in isolated critical situations during which prolonged use of the LMC channel would not be feasible due to other LMC communications traffic. Such uses of the SMC channel would typically occur for temporary durations.

### 8.	On-Scene Coordination (OSC)

The EMS communications system must have the capability for mobile and portable radios to communicate directly (unit-to-unit) while on the scene of an emergency requiring multiple vehicle and multi-agency responses. Typically this coordination takes place either on VHF high band interoperability channels, or on channels maintained by the local rescue agencies involved.

### 9.	Medical Resource Coordination (MRC)

The EMS communications system must allow for point-to-point coordination of EMS resources between hospitals, providers, and communications control centers for response to a disaster or mass casualty incident. Telephone lines between communications control centers are typically used for resource coordination during normal operations, and networked software specifically for this use is becoming more prevalent. However, radio communications are needed during situations following hurricanes, tornadoes, floods, fires, etc., when telephone lines are inoperative, or when telephone central office switching facilities are jammed or disabled. Most EMS agencies and hospitals maintain some functionality of the HEAR network VHF high band frequencies for this purpose.

# CALIFORNIA EMS ALLOCATIONS

## GENERAL

The following tables of radio channels and allocations and organizational data for EMS communications within California was a major undertaking by the State of California. The effort began in 1997 with a survey of all counties, EMS providers, and hospitals in the State. That survey was followed by numerous site visits, mail surveys and telephone inquiries continuing through the fall of 1998. In October 2008, revision efforts began by requesting that each local agency  representative review data relating to its respective area(s) and submit any corrections or changes to the previously submitted information. Every effort has been made to ensure the data collected is as accurate, complete, and up-to-date as possible. If errors are identified, please advise the EMS Authority.

## INTRODUCTION TO TABLES

Note: In the following tables the symbol N/A = Not Available and N/R = No Response

The following tables are organized alphabetically by the local EMS agency. Within each local EMS agency is a list of radio channel information, followed by information on emergency department facilities, and EMS providers.

### 1.  Radio Channel Information

Radio channel information is shown by channel use description, by continuous tone controlled squelch (CTCSS) frequency (in Hertz), by primary or alternate status, and by base-transmit and base-receive frequency in (MHz or MED channel number).

- MED Channel Frequencies

MED Channel numbers 1 through 103 are prescribed by FCC Rules, Part 90.27(c)(13)(i) and 90.27(b) as corresponding to the following radio transmit frequencies in MHz:

MED Channel			Frequency (Base/Mobile)				Frequency (Mobile Only)

1	463.000	468.000

2	463.025	468.025

3	463.050	468.050

4	463.075	468.075

5	463.100	468.100

6	463.125	468.125

7	463.150	468.150

8	463.175	468.175

9	462.950	467.950

10	462.975	467.975

B.	CTCSS Frequencies

Continuous Tone-Controlled Squelch (CTCSS) systems provide a reduction of nuisance interference in FM radio systems by incorporating a sub-audible tone onto the radio carrier information such that only a similarly equipped radio receiver will open its squelch circuit to receive the transmission. Systems equipped with CTCSS will eliminate much interference from distant sources, although CTCSS by itself cannot prevent undesired “FM capture” from occurring due to nearby simultaneous co-channel transmissions.

CTCSS frequencies are designated by the Electronic/Telecommunications Industries Association (EIA/TIA) in EIA/TIA Standard 603. The following table is a portion of those CTCSS frequencies above 90 Hz and below 211 Hz which are approved for EMS radio communications in California. Since there is an abbreviated code scheme for these frequencies common to systems supplied by Motorola Communications & Electronics Inc., the Motorola (MOT.) code designations of these CTCSS frequencies are also shown. Similarly, the Wolfsberg (WOLF.) codes are also shown. To the extent possible, CTCSS tones within a local geographic area should be exclusively from either Group A or Group B to avoid false sensing due to adjacent tone frequencies.

Group A

CTCSS		MOT.	WOLF

Freq.(Hz)	      Code	Code

100.0	1Z		14

107.2	1B		16

114.8	2A		18

123.0	3Z		22

131.8	3B		24

141.3	4A	 26

151.4	5Z		28

162.2	5B		32

173.8	6A		34

186.2	7Z		36

203.5	M1		38

Group B

CTCSS		MOT.	WOLF

Freq.(Hz)  	Code		Code

94.8	ZA		12

103.5	1A		15

110.9	2Z		17

127.3	3A		23

136.5	4Z		25

146.2	4B		27

156.7	5A		31

167.9	6Z		33

192.8	7A		37

210.7	M2		-

210.7	M2

Excluded from the above list are:

CTCSS frequencies below 90 Hz which may cause unacceptably long receiver response times in some systems; frequencies above 211 Hz which may require special engineering considerations in production; frequencies which would receive interference from common 60 Hz AC power systems; and non-EIA frequencies offered by some manufacturers which would limit intersystem and mutual-aid operations.

C.		Primary/Alternate Allocations

The primary and alternate designations on some MED Channels shown on the following tables derive originally from FCC rules requiring not less than four channels (three, if bio-medical telemetry is not employed) be provided from EMS base station operations for medical coordination between ambulances and hospital emergency departments. The primary/alternate scheme of allocation is necessary to insure that a channel is available when needed considering simultaneous MED Channel use in adjacent areas.

### 2.	 Emergency Department Information

For each local EMS agency, emergency department facilities are listed with their address followed by the 24-hour telephone number of either the switchboard (Main), emergency department (ED) or both.

### 3.   EMS Provider

Within each local EMS agency, EMS providers are listed alphabetically showing the type of transportation (ground [G], air [A], water [W]) quantity of ambulances, whether or not the vehicles transport to a hospital and the highest level of Advanced Life Support (ALS) or Basic Life Support (BLS) certification at the location. The telephone number of each provider is also shown.

#### Alameda County EMS Agency

Agency Contact

Michael King, EMS Director
1000 San Leandro Blvd., Ste. 200
San Leandro, CA 94577
(510) 667-7739

FAX: (510) 618-2099
E-MAIL: Michael.King@acgov.org

Channel Use	TX-Freq	RX-Freq	CTCSS		Prim/Alt

| Local Medical Coordination (real time) Trunked system | 800 MHz | N/A | N/A | N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination Fire White CALCORD | N/A N/A | N/A N/A | N/A N/A | N/A N/A |
| Calling Channel | 800 MHz | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Trunked system | 800 MHz | N/A | N/A | N/A |
| Direct to hospitals Trunked system, telephone | 800 MHz | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) For disasters Fire White CALCORD | 800 MHz 155.400 N/A | N/A N/A N/A | N/A N/A N/A | N/A N/A N/A |

Helipad

Emergency Department Facilities	Telephone	Latitude/Longitude

Alameda Hospital	(510) 522-3700

2070 Clinton Avenue

Alameda, California 94501

Valley Care Medical Center	(925) 847-3000	37-41-39.000N

5575 W. Los Positas Blvd.		121-52-46.000W

Pleasanton, California 94588		TLOF – 64’ X 64’

St. Rose Hospital	(510) 264-4000

27200 Calagora Avenue

Hayward, California 94545

Eden Hospital	(510) 889-5048	37-41-54.000N

20103 Lake Chabot Road		122-05-22.000W

Castro Valley, California 94546		TLOF - 55' Diameter.

Children’s Hospital	(510) 428-3273	37-50-12.000N

747 52nd Street		122-15-59.000W

Oakland, California 94609		TLOF - 67' x 67'

Highland General Hospital	(510) 437-4800

1411 E – 31st Street

Oakland, California 94602

Alta Bates Medical Center	(510) 204-4444

2450 Ashby Avenue

Berkeley, California 94705

San Leandro Hospital	(510) 357-6500

13855 East 14th Street

San Leandro, California 94578

Washington Hospital	(510) 797-1111	37-33-23.000N

2000 Mowry Avenue 		121-58-38.000W

Fremont, California 94538 		TLOF - 70' x 70'

Kaiser Hospital, Oakland	(510) 596-7667

280 West Mac Arthur Blvd.

Oakland, California 94611

Kaiser Hospital, Hayward	(510) 784-4000

27400 Hesparian Blvd.

Hayward, California 94545

Summit Medical Center	 (510) 655-4000

350 Hawthorne Street

Oakland, California 94609

San Ramon Regional Medical Center	(925) 275-9200

6001 Norris Canyon Road

San Ramon, California 94623

Helispot Location	Latitude/Longitude	Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response West | (510) 895-7600 | G | 40 | yes | ALS |
| Alameda County Fire Department | (510) 618-3485 | G | 0 | no | ALS |
| Alameda Fire Department | (510) 522-4100 | G | 3 | yes | BLS |
| Albany Fire Department | (510) 528-5771 | G | 1 | yes | ALS |
| Berkeley Fire Department | (510) 644-6665 | G | 3 | yes | ALS |
| CALSTAR | (800) 252-5050 | GA | 2 | yes | ALS |
| California Department of Forestry and Fire | (925) 862-2197 | G | 0 | no | BLS |
| CHP | (707) 253-4906 | A | 1 | yes | ALS |
| East Bay Regional Parks District | (510) 881-1833 | GAW | 0 | yes | BLS |
| Emeryville Fire Department | (510) 596-3750 | G | 0 | no | ALS |
| Fremont Fire Department | (510) 494-4290 | G | 0 | no | ALS |
| Hayward Fire Department | (510) 293-8690 | G | 0 | no | BLS |
| Lawrence Berkeley Lab Fire Dept | (510) 486-636 0 | G | 0 | no | BLS |
| Lawrence Livermore National Laboratory | (925) 422-3980 | G | 1 | no | BLS |
| Livermore Fire Department | (925) 737-5463 | G | 0 | no | ALS |
| Naval Supply Center Fire Dept | (510) 263-3276 | G | 0 | no | BLS |
| Newark Fire Department | (510) 793-1400 | G | 0 | no | ALS |
| Oakland Fire Department | (510) 238-6725 | G | 0 | no | BLS |
| Piedmont Fire Department | (510) 420-3030 | G | 1 | yes | BLS |
| Pleasanton Fire Department | (925) 484-8114 | G | 0 | no | ALS |
| Reach Helicopter | (707) 575-6886 | GA | 2 | yes | ALS |

#### Contra Costa County EMS Agency

Agency Contact

Art Lathrop, EMS Administrator

1340 Arnold Drive, #126

Martinez, California 94553

(925) 646-4690

FAX: (925) 646-4379
E-MAIL: alathrop@hsd.cccounty.us

Channel Use	TX-Freq	RX-Freq	CTCSS		Prim/Alt

| Local Medical Coordination Contra Costa FPD Moraga-Orinda FPD San Ramon Valley FPD Richmond Fire Department Pinole/Rodeo Fire Departments East Diablo/Bethel Isl. FPD’s | 46.32 46.38 45.88 46.42 46.48 46.18 | 46.32 46.38 46.44 46.06 46.48 46.18 | 162.2 162.2 162.2 162.2 162.2 162.2 | N/A N/A N/A N/A N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination Fire Medical Mutual Aid | N/A | N/A | N/A | 155.400 |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Contra Costa FPD Moraga-Orinda FPD San Ramon Valley FPD Richmond Fire Department Pinole/Rodeo Fire Departments East Diablo/Bethel Island FPDs | 46.32 46.38 45.88 46.42 46.48 46.18 | 46.32 46.38 46.44 46.06 46.48 46.18 | 162.2 162.2 162.2 162.2 162.2 162.2 | N/A N/A N/A N/A N/A N/A |
| Direct to hospitals MEDARS 12 (T-band) MEDARS 13 (T-band) MEDARS 14 (T-band) | 491.9125 491.6125 491.6625 | 488.9125 488.6125 488.6625 | N/A N/A N/A | N/A N/A N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities	Telephone	Latitude/Longitude

Doctor’s Hospital, San Pablo Campus 	(510) 970-5000	37-57-15.000N

2000 Vale Road		122-20-10.000W

San Pablo, California 94806 		TLOF - 41' x 41'

Sutter Delta Hospital	(925) 779-7200

3901 Lone Tree Way

Antioch, California 94509

Kaiser Antioch Medical Center 	(925) 813-6500

5601 Deer Valley Road 
Antioch, California 94531

John Muir Medical Center 	(925) 939-3000	37-54-46.000N

1601 Ygnacio Valley Road 		122-02-18.000W

Walnut Creek, California 94598 		TLOF - 65' Diameter.

Kaiser Medical Center-Walnut Creek 	(925) 295-4000

1425 South Main Street

Walnut Creek, California 94596

Kaiser Richmond	(510)307-1500

901 Nevin Ave

Richmond , California 94801

Contra Costa Regional Medical Center	(925) 370-5000

2500 Alhambra Avenue

Martinez, California 94553

Mt. Diablo Medical Center	(925) 682-8200	37-55-28.000N/

PO Box 4110 		121-43-57.000W

2540 East Street 		TLOF - 42' X 42'

Concord, California 94524

San Ramon Regional Medical Center	(925) 275-9200

6001 Norris Canyon Road

San Ramon, California 94583

Helispot Location	Latitude/Longitude	Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response West | (925) 602-1300 | G | 47 | yes | ALS |
| Bethel Island Fire Protection Dist | (925) 634-3400 | G | 0 | no | ALS |
| Contra Costa County Fire Protection District | (925) 941-3640 | G | 0 | no | ALS |
| Crockett-Carquinez Fire Protection District | (510) 787-2717 | G | 0 | no | BLS |
| East Diablo Fire Protection District | (925) 634-3400 | G | 0 | no | BLS |
| El Cerrito Fire Department | (510) 215-4450 | G | 0 | no | ALS |
| Moraga/Orinda Fire Protection Dist | (925) 258-4599 | G | 2 | yes | ALS |
| Pinole Fire Department | (510) 724-8970 | G | 0 | no | ALS |
| Richmond Fire Department | (510) 307-8031 | G | 0 | no | BLS |
| Rodeo-Hercules Fire Protection District | (510) 799-4561 | G | 0 | no | ALS |
| San Ramon Valley Fire Protection District | (925) 838-6691 | G | 7 | yes | ALS |

#### El Dorado County EMS Agency

Agency Contact 
Richard W. Todd, Acting EMS Administrator
415 Placerville Dr Ste J
Placerville, CA 95667
(530) 621-6505

FAX: (530) 621-2758
E-MAIL: rtodd@co.el-dorado.ca.us

Channel Use	TX-Freq	RX-Freq	CTCSS	Prim/Alt

| Local Medical Coordination East Slope-Police West Slope | 154.445 159.225 | 156.03 151.19 | N/A Multiple | N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | Microwave | Microwave | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) East Slope-City Fire East Slope-Lake Valley West Slope | 154.445 N/A 159.225 | N/A 154.34 151.19 | N/A N/A Multiple | N/A N/A N/A |
| Direct to hospitals East Slope West Slope | Mednets Mednets | Mednets Mednets | Multiple Multiple | Cellphone Cellphone |
| Other (e.g. tactical, etc.) East Slope-S&R Sierra Channel East Slope-White Fire West Slop[e Command Channel | 160.875 154.280 159.270 | 160.875 154.280 154.430 | N/A N/A Multiple | N/A N/A N/A |

Helipad

Emergency Department Facilities	Telephone	Latitude/Longitude

Marshall Hospital 	(530) 622-1441	38-43-22.7N/

1040 Marshall Way 		120-14-28.8W

Placerville, California 95667

Barton Memorial Hospital 	(530) 541-3420	38-54-40.700N/

PO Box 9578 		119-59-48.600W

South Lake Tahoe, California 96158 		TLOF - 42'

Helispot Location	Latitude/Longitude	Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| California Department of Forestry | (530) 644-2345 | GA | 0 | no | BLS |
| Cameron Park CSD/CDF | (530) 677-6190 | G | 1 | yes | ALS |
| Diamond Springs/El Dorado Fire Protection District | (530) 626-3190 | G | 1 | yes | ALS |
| El Dorado County Fire Protection District | (530) 644-9630 | G | 5 | yes | ALS |
| El Dorado Hills Fire Department | (916) 933-6623 | G | 1 | yes | ALS |
| Fallen Leaf Lake Fire Protection District | (530) 542-1343 | G | 0 | no | BLS |
| Garden Valley Fire Protection Dist | (530) 333-1240 | G | 0 | no | ALS |
| Georgetown Fire Protection District | (530) 333-4111 | G | 1 | yes | ALS |
| Lake Valley Fire Protection District | (530) 577-3737 | G | 1 | yes | ALS |
| Latrobe Fire Protection District | (530) 677-6366 | G | 0 | no | ALS |
| Meeks Bay Fire Protection District | (530) 525-7548 | G | 0 | no | BLS |
| Mosquito Fire Protection District | (530) 626-9017 | G | 0 | no | BLS |
| Pioneer Fire Protection District | (530) 620-4444 | G | 0 | no | ALS |
| Rescue Fire Protection District | (530) 677-1868 | G | 0 | no | ALS |
| South Lake Tahoe Fire Department | (530) 542-6152 | G | 3 | yes | ALS |
| Tahoe Douglas Fire Protection Dist | (775) 588-3591 | G | 0 | no | ALS |
| North Tahoe Fire Protection Dist | (530) 583-6913 | G | 0 | no | ALS |

#### Central California EMS Agency

Agency Contact

(Fresno, Kings, Madera, Tulare)
Dan Lynch, EMS Administrator
PO Box 11867
Fresno, CA 93775
(559) 445-3387

FAX: (559) 445-3205
E-MAIL: DLynch@co.fresno.ca.us

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordinator(real time) Med 1 Med 2 Med 3 Med 4 Med 5 Med 6 Med 7 Med 8 Med 9 Med 10 Med 11 Med 12 Med 13 Med 14 Med 15 Med 16 | 468.00 468.025 468.050 468.075 468.100 468.125 468.150 468.175 467.950 467.975 458.300 458.325 458.1875 456.425 466.575 468.625 | 463.00 463.025 463.050 463.075 463.100 463.125 463.150 463.175 462.950 462.975 453.300 453.325 458.1875 451.425 461.575 463.625 | 114.8 114.8 114.8 179.9 179.9 179.9 179.9 114.8 141.3 114.8 156.7 156.7 156.7 114.8 114.8 156.7 | N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Hanford City Fire Kings County Fire Fresno City Fire Clovis City Fire Fresno County Fire NCFPD Fire White Net 1 HEAR Madera County Fire Tulare City Fire Visalia City Fire Portville City Fire Tulare County Fire Dinuba City Fire | 465.575 465.625 155.055 155.055 155.085 155.895 156.075 | 460.575 460.600 153.845 154.235 153.890 154.190 154.280 155.340 151.460 154.335 154.325 156.000 154.010 154.085 | 146.2 146.2 173.8 103.5 None 100.0 None None None 162.2 131.8 123.0 131.8 146.2 | N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A |
| Direct to hospitals | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) Calcord | 156.075 | 156.075 | 156.7 | N/A |

Helipad

Emergency Department Facilities	Telephone	Latitude/Longitude

Pad A

Community Regional Medical Center			(559) 442-6000 - Main			36-44-39.000N/

2823 Fresno Street	(559) 442-2432 - ED	119-47-07.000W

Fresno, California 93715 							TLOF - 52.5 x 54

Pad B

36-44-37.000NN/

119-47-07.800W

TLOF - 52.5' x 54'

Pad C

36-44-35.000N/

119-47-06.000W

TLOF - 44' x 45'

Saint Agnes Medical Center 	(559) 449-3000 - Main	36-44-14.0/

1201 E. Herndon, #105	(559) 449-3534 - ED 	119-45-58.000W

Fresno, California 93720 		TLOF - 50' x 50'

Community Medical Center Clovis 	(559) 324-4000 - Main 	36-50-19.000N/

2755 E. Herndon Avenue 	(559) 324-4040 - ED	119-39-29.000W

Clovis, California 93611 		TLOF - 75' x 75'

Sierra Kings Hospital 	(559) 638-8155

372 W. Cypress

Reedley, California 93654

Kaiser Permanente 	(559) 448-3138

7300 N. Fresno Street

Fresno, California 93720

Selma Community Hospital	(559) 891-1000

1141 Rose Avenue

Selma, California 93662

Coalinga Regional Medical Center	(559) 935-6400

1191 Phelps Avenue

Coalinga, California 93210-9609

Veteran’s Administration Hospital 	(559) 225-6100

2615 E. Clinton Ave

Fresno, California 93703

Hanford Community Medical Center	(559) 582-9000 - Main 	36-19-48.000N/

450 Greenfield Avenue	(559) 585-5251 - ED 	119-39-31.000W

Hanford, California 93230 		TLOF - 55' Diameter.

Central Valley General Hospital 	(559) 583-2100 - Main

1025 N. Douty	(559) 583-2250 - ED

Hanford, California 93230

Corcoran District Hospital 	(559) 992-5051

1310 Hanna Avenue

Corcoran, California 93212

Children’s Hospital of Central California	(559)353-3000 	Pad 2

9300 Valley Children’s Place		36-52-57.300N/

Madera, California 93637		119-47-59.800E

TLOF - 48' x 48'

Pad 3

36-52-53.000N/

119-48-04.000W

TLOF – 20’ x 20’

Madera Community Hospital 	(559) 675-5500 - Main

1250 E. Almond 	(559) 675-5520 - ED

Madera, California 93637

Community Medical Center Oakhurst	(559)683-2992

48677 Victoria Lane

Oakhurst, California 93644

Kaweah Delta District Hospital	(559)625-2211- Main

400 W. Mineral King	(559)625-7215 - ED

Visalia, California 93277

Tulare District Hospital	(559)688-0821 - Main

869 Cherry St	(559)685-3450 - ED

Tulare, California 93274

Sierra View District Hospital	(559)784-1110 - Main

465 W Putnam	(559)784-8885 - ED

Portville, California 93257

Helispot Location						Latitude/Longitude					Description of Location

Batterson – Madera	37-22-79 / 119-37-75	Helipad at Fire Station, Mtns

Buckeye – Fresno	37-03-00 / 119-23-8	Forest Service Helipad, 4000’

Dunlap – Fresno	36-45-43 / 119-09-90	Ranger Station or Library PL

Hwy 41 & Rd 200 - Madera	37-37-0 / 119-44-5	Park N Ride Area

Millerton Lake – Fresno	36-59-20 / 119-40-96	Boat Ramp or Fire Station

North Fork – Madera	37-14-40 / 119-30-74	Forest Service Pad

Kettleman City – Kings	36-03-02 / 119-56-38	Trucking Co. or Fire Station

Huntington Helipad – Fresno	37-14-06 / 119-10-1	Hunting Lake Fire Station Pad

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Ambulance | (559)445-5900 | G | 68 | yes | ALS |
| American Ambulance of Visalia | (559)730-3015 | G | 8 | yes | ALS |
| Avenal District Ambulance | (559) 386-4021 | G | 2 | yes | ALS |
| CHP | (559) 488-4121 | A | 1 | yes | ALS |
| California Hot Springs Ambulance | (559)548-6548 | G | 1 | yes | LALS |
| Camp Nelson Vol. Ambulance | (559)542-2140 | G | 2 | yes | LALS |
| Clovis City Fire Department | (559) 297-2460 | G | 0 | no | BLS |
| Coalinga City Fire Department | (559) 935-1652 | G | 3 | yes | ALS |
| Dinuba City Fire Department | (559) 591- 5931 | G | 4 | yes | ALS |
| Exeter District Ambulance | (559) 594-5250 | G | 4 | yes | ALS |
| Fresno City Fire Department | (559) 498-1542 | G | 0 | no | BLS |
| Fresno County Fire Department | (559) 485-7500 | G | 0 | no | BLS |
| Hanford City Fire Department | (559) 585-2545 | G | 0 | no | BLS |
| Imperial Ambulance | (559) 784-8500 | G | 6 | yes | ALS |
| Kings County Fire Department | (559) 582-3211 | G | 0 | no | BLS |
| Kingsburg City Fire Department | (559) 897-5457 | G | 3 | yes | ALS |
| Lemoore City Fire Department | (559) 924-6797 | G | 0 | no | BLS |
| LifeStar Ambulance | (559) 688-2550 | G | 6 | yes | ALS |
| Madera County Fire/CDF | (559) 661-5497 | G | 0 | no | BLS |
| Mobile Life Support (AMR) | (559) 730-3022 | G | 8 | yes | ALS |
| North Central Fire Protection Dist | (559) 846-5353 | G | 3 | yes | ALS |
| Pistoresi Ambulance | (559) 673-8004 | G | 8 | yes | ALS |
| Portville City Fire Department | (559) 782-7536 | G | 0 | no | BLS |
| Sanger City Fire Department | (559) 875-6568 | G | 5 | yes | ALS |
| Selma City Fire Department | (559) 896-2525 | G | 3 | yes | ALS |
| Sequoia Safety Council | (559) 638-9995 | G | 5 | yes | ALS |
| Sierra Ambulance | (559) 642-0650 | G | 6 | yes | ALS |
| Skylife of Central California | (559) 456-7878 | A | 1 | yes | ALS |
| Tulare City Fire Department | (559) 684-4300 | G | 0 | no | ALS |
| Tulare County Fire Department | (559) 732-5954 | G | 0 | no | BLS |
| Visalia City Fire Department | (559) 731-4266 | G | 0 | no | ALS |

#### Coastal Valleys EMS Agency

Agency Contact

(Sonoma/Mendocino/Napa)
Bryan Cleaver, Regional Administrator
475 Aviation Blvd., Suite 200
Santa Rosa, CA 95403
(707) 565-6501

FAX: (707) 565-6510

E-MAIL: bcleaver@sonoma-county.org

Channel Use												TX-Freq	RX-Freq	 	CTCSS		Prim/Alt

| Local Medical Coordination (real time) MedNet (Napa) Med 1 Med 2 Med 3 Med 4 Med 5 Med 6 Med 7 Med 8 | 155.835 155.100 155.265 468.000 468.025 468.050 468.075 468.100 468.125 468.150 468.175 | 155.100 155.100 155.265 463.000 463.025 463.050 463.075 463.100 463.125 463.150 463.175 | 131.8* N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A | 155.100 N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination Napa | N/A N/A | N/A N/A | N/A 127.3** | N/A N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Napa 4 | 155.835 155.265 N/A | 155.100 155.265 N/A | N/A N/A N/A | N/A N/A 155.805/City Fire Dept.131.8 |
| Direct to hospitals Napa (Cellular) | 155.355 155.355 | 155.355 155.355 | N/A 131.8 | N/A N/A |
| Other (e.g. tactical, etc.) Napa | 155.340 N/A | 155.340 N/A | N/A N/A | N/A N/A |

*131.8 T&R Atlas Pic

** 127.3 T and 131.8 R – MT ST Helena

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Healdsburg General Hospital 						(707) 431-6500

1375 University Avenue

Healdsburg, California 95448

Howard Memorial Hospital						(707) 459-6801

1 Madron Street

PO Box 1430

Willits, California 95490

Kaiser-Santa Rosa 									(707) 571-4000 - Main

401 Bicentennial Way 								(707) 571-4510 - ED

Santa Rosa, California 95403

Mendocino Coast District Hospital 				(707) 961-1234					39-25-55.000N/

700 River Drive 																				123-47-55.000W

Ft. Bragg, California 95437 																TLOF - 40' x 40'

Palm Drive Hospital 								(707) 823-8511					38-23-48.000N/

501 Petaluma Avenue 																		122-49-05.000W

Sebastopol, California 95472 																TLOF - 65' x 65'

Petaluma Valley Hospital 							(707) 778-2634 – Main			38-15-19.000N/

400 North McDowell Blvd. 						(707) 864-1250 – ED			122-37-46.000W

Petaluma, California 94952 																TLOF - 65' Diameter

Queen of the Valley Hospital 						(707) 252-4411					38-19-45.000N/

1000 Trancas Street 																			122-17-35.000W

Napa, California 94558 																	TLOF - 40' Diameter

Redwood Coast Medical Services 				(707) 884-4005

46900 Ocean Drive

Gualala, California 95455

Saint Helena Hospital								(707) 963-3611 					38-32-34.000N/

650 Sanitarium Road 																		122-28-38.000W

Deer Park, California 94576 																TLOF - 55' x 55'

Santa Rosa Memorial Hospital 					 (707) 546-3210 – Main		38-26-38.000N/

1165 Montgomery Drive 							 (707) 525-5207 – ED			122-42-01.000W

Santa Rosa, California 95405 															TLOF - 53' x 68'

Sonoma Valley Hospital 							 (707) 935-5000

347 Andrieux Street

Sonoma, California 95476

Sutter Medical Center 								(707) 576-4000 – Main			38-28-15.000N/

3325 Chanate Road 									(707) 576-4040 – ED			122-42-21.000W

Santa Rosa, California 95404 															TLOF - 42' x 42'

Ukiah Valley Medical Center 					(707) 462-3111					39-09-34.000N/

275 Hospital Drive 																			123-16-42.000W

Ukiah, California 95482 																	TLOF - 40' x 40'

Warrack Hospital 									(707) 542-9030

2449 Summerfield Road

Santa Rosa, California 95405

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (707) 579-9421 | G | 10 | yes | ALS |
| Anderson Valley Ambulance | (707) 895-3123 | G | 1 | yes | ALS |
| Angwin Volunteer Ambulance | (707) 965-2468 | G | 2 | yes | BLS |
| Bell's Ambulance Service | (707) 433-1408 | G | 3 | yes | ALS |
| Bodega Bay Fire Dept. | (707) 875-3700 | G | 1 | yes | ALS |
| Brooktrails Fire Dept/Ambulance | (707) 459-4441 | G | 1 | yes | BLS |
| CALSTAR | (707) 462-5972 | N/R | N/R | N/R | ALS |
| CDF-Helo 101 | (707) 459-7408 | A | 1 | no | BLS |
| CHP Helicopter | (707) 224-3123 | G | 8 | yes | ALS |
| Cloverdale Ambulance Service | (707) 894-5862 | G | 1 | yes | ALS |
| Coast Life Support | (707) 884-1216 | G | 2 | yes | ALS |
| Covelo Fire Department Ambulance | (707) 983-6719 | G | 2 | yes | BLS |
| Elk Fire Department | (707) 877-3350 | G | 2 | yes | BLS |
| Laytonville Fire Department | (707) 984-6055 | G | 2 | yes | ALS |
| Mendocino Coast Hospital/Amb. | (707) 961-1234 | G | 2 | yes | ALS |
| Mercy St. Helena Ambulance | (707) 257-0103 | A | 1 | yes | ALS |
| Napa City Fire Department | (707) 963-1510 | G | 4 | yes | ALS |
| Petaluma Fire | (707) 778-4390 | G | 2 | yes | ALS |
| Piner's Ambulance | (707) 257-9593 | G | 0 | no | ALS |
| REACH Helicopter | (707) 575-6886 | A | 2 | yes | ALS |
| Redwood Empire Life Support | (707) 542-6771 | G | 20 | yes | ALS |
| Russian River FPD | (707) 869-9089 | G | 3 | yes | ALS |
| Sonoma Co. Sheriff Department | (707) 527-9595 | A | 1 | yes | ALS |
| Sonoma Fire - Medical | (707) 996-2102 | G | 2 | yes | ALS |
| Ukiah Ambulance | (707) 462-3001 | G | 4 | yes | ALS |
| Ukiah Fire Department | (707) 463-6274 | G | 3 | yes | ALS |
| Ukiah Flightcare | (707) 462-1414 | A | 1 | yes | ALS |
| Willits Ambulance | (707) 459-7088 | G |  | yes | ALS |

#### Imperial County EMS Agency

Agency Contact

Ryan E. Kelley, EMS Administrator
Imperial County Public Health Department
797 Main St. Suite A
El Centro, CA 92243
(760) 482-2974

FAX: (760) 336-3903
E-MAIL: ryankelley@imperialcounty.net

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) Med 2 |  |  | N/A | Prim |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel |  |  | N/A | Prim |
| Dispatch (for each EMS Agency) | N/A | N/A | N/A | N/A |
| Direct to hospitals |  |  | N/A | N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Pioneers Memorial Hospital 						(760) 344-2120					32-57-30.000N/

207 W. Legion Road 																		115-33-15.000W

Brawley, California 92227 																TLOF - 50' Diameter

El Centro Regional Medical Center 			(760) 339-7100 					32-36-51.000N/

1415 Ross Avenue 																			115-34-47.000W

El Centro, California 92243 																TLOF - 40' Diameter

US Public Health Service Fort					(760) 572-0217

Yuma Indian Hospital

Winterhaven, California

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| Blythe Ambulance Services | (760) 922-8460 | G | 4 | yes | ALS |
| Calexico Fire Department | (760) 768-2150 | G | 2 | yes | ALS |
| Gold Cross Ambulance Service | (760) 353-3380 | GA | 9 | yes | ALS |
| Rural/Metro Corporation | (520) 782-4757 | G | 10 | yes | ALS |
| West Shore Ambulance Service | (760) 395-6800 | G | 4 | yes | ALS |

#### Inland County EMS Agency

Agency Contact

(San Bernardino, Inyo, Mono) 
Virginia Hastings, Executive Director
515 N. Arrowhead
San Bernardino, CA 92415-0060
(909) 388-5823

FAX: (909) 388-5825
E-Mail: vhastings@cao.sbcounty.gov

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) San Bernardino Inyo Mono | 800 MHz (6ALS1) 155.865 154.025 | 800 MHz (6ALS1) 155.895 154.025 | N/A 131.8 131.8 | N/A Primary Primary |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | 800 MHz (6ALS1) | 800MHz (6ALS1) | N/A | N/A |
| Dispatch (for each EMS Agency) Mono | 155.760 | 153.860 | 136.5 | N/A |
| Direct to Hospitals Mono | 155.895 | 154.025 | 136.5 | N/A |
| Other (e.g. tactical, etc.) HEAR NGT | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Helipad #1

Arrowhead Regional Medical Center 			(909) 580-1357					34-04-31.000N/

400 N. Pepper Ave. Emergency Dept. 													117-20-57.000W

Colton, California 92324 																	TLOF - 70' x 70'

Helipad #2

34-04-31.000N/

117-20-57.000W

TLOF - 104' x 104'

Barstow Community Hospital  					 (760) 256-1761 ext3030		34-53-37.000N/

555 S. Seventh Street																		117-01-03.000W

Barstow, California 92311																	TLOF - 40' x 40'

Bear Valley Community Hospital 				(909) 866-6501 ext8201

41870 Garstin Drive

P.O. Box 1649

Big Bear Lake, California 92315

Chino Valley Medical Center   					(909) 464-8604 ext8967

5451 Walnut Avenue

Chino, California 91710

Colorado River Med. Ctr.   						(760) 326-4531 ext198

1401 Bailey Avenue

Needles, California 92363

Community Hospital of San Bernardino   		(909) 887-6333 ext3550

1805 Medical Center Drive

San Bernardino, California 92411

Desert Valley Hospital  							(760) 381-8041

16850 Bear Valley Road									ext8587 or 8580

Victorville, California 92395

Doctors Hospital-Montclair   						(909)625-8307

5000 San Bernardino

Montclair, California 91763

Hi Desert Medical Center   						(760) 366-6126					34-07-54.000N/

6601 White Feather Road																	116-16-32.000W

Joshua Tree, California 92252															TLOF - 40' x 40'

JJP VA MED CTR AMB Care/11C  			(909) 825-7084 ext6102

11201 Benton St.

Loma Linda, California 92357

Kaiser Permanente Hospital  						(909) 427-5521					34-04-22.000N/

9961 Sierra Avenue																			117-25-53.000W

Fontana, California 92335																	TLOF - 65' x 65'

North

Loma Linda University Medical Center   		(909) 558-4444					34-03-00.000N/

11234 Anderson Street, Room A108													117-15-49.000W

Loma Linda, California 92354															TLOF -  54' x 54'

South

34-02-56.000N/

117-15-50.000W

TLOF -  51' x 51'

Mammoth Hospital   								(760) 934-3311 ext. 2234

85 Sierra Park Road

P.O. Box 660

Mammoth Lakes, California 93546

Mountains Community Hospital   				(909) 336-3651 ext3080		34-15-55.000N/

P.O. Box 70																					117-10-02.000W

Lake Arrowhead, California 92352														TLOF - 50' Diameter

Northern Inyo Hospital   							(760) 873-5811 ext2264

150 Pioneer Lane

Bishop, California 93514

Redlands Community Hospital   					(909) 335-5600

350 Terracina Blvd

Redlands, California 92373

San Antonio Community Hospital 				(909) 920-4747 					34-06-09.000N/

999 San Bernardino Road 																	117-38-11.000W

Upland, California 91786 																	TLOF - 50' Diameter

St. Bernardine Medical Center 					(909) 883-8711 x3364

2101 N. Waterman Avenue P.O Box 2338

San Bernardino, California 92406

St. Mary Regional Medical Center				(760) 242-2311 ext6500

18300 Hwy 18 P.O. Box 7025

Apple Valley, California 92307

Southern Inyo Hospital 								(760) 876-5501 ext2220

501 E. Locust Street

P.O. Box 1009

Lone Pine, California 93545

Victor Valley Community Hospital 				(760) 843-6099 					34-31-40.000N/

15248 Eleventh Street 																		117-17-34.000W

Victorville, California 92395 																TLOF - 60' x 60'

Helispot Location						Latitude/Longitude						Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| AMR - Redlands | (909) 793-7676 | G | 38/7 | yes | ALS/BLS |
| AMR - Rancho Cucamonga | (909) 477-5000 | G | 38/9 | yes | ALS/BLS |
| AMR – Victorville | (760) 925-7400 | G | 19/3 | yes | ALS/BLS |
| Adelanto (City) Fire Department | (760) 246-3344 | G | 0 | no | BLS |
| Antelope Valley Fire Department | (530) 495-2900 | G | 0 | no | BLS |
| Apple Valley (City) Fire Dept | (760) 247-7618 | G | 0 | no | BLS |
| Arrowbear Lake CWO | (909) 867-3479 | G | 0 | no | BLS |
| Barstow (City) Fire Department | (760) 256-2254 | G | 0 | no | ALS |
| Bear Valley Paramedic | (909) 866-7478 | G | 8 | yes | ALS |
| Big Bear City Fire Department | (909) 585-2565 | G | 0 | no | BLS |
| Big Bear Lake Fire Department | (909) 866-7566 | G | 0 | no | BLS |
| Big Pine Fire Department | (760) 938-2146 | N/R | N/R | N/R | BLS |
| Bridgeport Fire Department | (760) 932-7101 | G | 0 | no | BLS |
| Bureau of Land Management | (760) 872-4881 | G | 0 | no | BLS |
| CDF-#13 Yucaipa | (909) 797-1000 | G | 0 | no | ALS |
| CDF-#6 Highland | (909) 862-3031 | G | 0 | no | ALS |
| CHP-Air | (760) 254-2956 | A | 2 | yes | ALS |
| Chalfant Valley Fire Department | (760) 873-3990 | G | 0 | no | BLS |
| China Lake Naval Weapons Ctr | (760) 939-2146 | G | 3 | yes | ALS |
| Chino Valley (City) Fire Dept | (909) 902-5260 | G | 0 | no | BLS |
| Cole-Schaefer Ambulance Svs | (909) 622-1273 | G | 7 | yes | BLS |
| Colton (City) Fire Department | (909) 370-5100 | G | 0 | no | BLS |
| Crest Forest Fire District | (909) 338-3311 | G | 3 | yes | ALS |
| Daggett Community Service Dist. | (760) 254-2415 | G | 0 | no | BLS |
| Death Valley National Monument | (760) 786-2342 | G | 3 | yes | ALS |
| Delano Ambulance Service | (661) 725-3374 | G | 4 | yes | ALS |
| Desert Ambulance Service | (760) 256-6854 | G | 6 | yes | ALS |
| Green Valley Lake Fire Dept | (909) 337-8586 | G | 0 | no | BLS |
| Hesperia (City) Fire Department | (760) 947-8023 | G | 5 | yes | ALS |
| Independence Fire Department | (760) 878-2113 | G | 0 | no | BLS |
| Lee Vining Fire Department | (760) 647-6358 | G | 0 | no | BLS |
| Liberty Ambulance | (760) 375-6565 | G | 3 | yes | ALS |
| Loma Linda (City) Fire Dept | (909) 799-2850 | G | 0 | no | BLS |
| Long Valley Fire Department | (760) 935-4545 | G | 0 | no | BLS |
| Lucerne Valley Fire Department | (760) 248-7322 | G | 1 | yes | BLS |
| Mammoth Hospital | (760) 934-8631 | G | 1 | yes | BLS |
| Mammoth Lakes Fire Department | (760) 934-2300 | G | 0 | no | ALS |
| Mercy Air Service | (909) 829-7030 | A | 8 | yes | ALS |
| Montclair (City) Fire Department | (909) 626-1217 | G | 0 | no | BLS |
| Mountain Warfare Training Ctr. | (760) 932-7761 | G | 3 | yes | BLS |
| Searles Valley Minerals | (760) 372-2341 | G | 1 | yes | BLS |
| Olancha/Cartago Fire Department | (760) 764-0029 | N/R | N/R | N/R | BLS |
| Ontario (City) Fire Department | (909) 935-2002 | G | 0 | no | ALS |
| Ontario Airport Fire Department | (909) 337-2815 | G | 0 | no | BLS |
| Paradise Fire Department | (760) 387-2720 | G | 0 | no | BLS |
| Rancho Cucamonga Fire Dept | (909) 477-2770 | G | 0 | no | ALS |
| Redlands (City) Fire Department | (909) 798-7600 | G | 0 | no | ALS |
| Rialto (City) Fire Department | (909) 820-2501 | G | 3 | yes | ALS |
| Running Springs Water District | (909) 867-2630 | G | 5 | yes | ALS |
| S. Amargosa Valley Emergency Service | (760) 852-4506 | N/R | N/R | N/R | BLS |
| San Bernardino Co. Fire Dept | (909) 387-5974 | G | 0 | no | BLS |
| San Bernardino Co. Fire-Fontana | (909) 829-4441 | G | 0 | no | BLS |
| San Bernardino Co. Fire Agency-Yucca Valley | (760) 365-3335 | G | 3 | yes | ALS |
| San Bernardino Co. Fire Agency-Forest Falls | (909) 794-4413 | G | 1 | yes | BLS |
| San Bernardino Co Fire Agency-Lake Arrowhead | (909) 337-8586 | G | 5 | yes | ALS |
| San Bernardino Co Fire Agency Searles | (760) 372-5988 | G | 2 | yes | BLS |
| San Bernardino Co. FD-Wrightwood | (760) 249-3206 | G | 5 | yes | ALS |
| San Bernardino City Fire Dept | (909) 384-5286 | G | 0 | no | ALS |
| Sheriff's Aviation | (909) 356-3800 | A | 3 | yes | ALS |
| Symons Emergency Services | (760) 873-8904 | G | 4 | yes | ALS |
| Twentynine Palms Fire Dept | (760) 367-7524 | G | 0 | no | BLS |
| Upland (City) Fire Department | (909) 931-4180 | G | 0 | no | ALS |
| Victorville (City) Fire Dept | (760) 955-5277 | G | 0 | no | BLS |
| White Mountain Fire Department | (760) 933-2617 | G | N/R | N/R | BLS |

#### Kern County EMS Agency

Agency Contact

Ross Elliott, Director
1800 Mount Vernon Avenue, 2nd Floor

Bakersfield, California 93306
(661) 868-5200

FAX: (661) 322-8453
E-MAIL: relliott@co.kern.ca.us

Channel Use											TX-Freq		RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) |
| --- |
| MUTUAL AID R | County Mutual Aid | 453.2250 | 458.2250 | 131.8 | 131.8 |
| Med 1R | Soledad | 463.0000 | 468.0000 | 186.2 | 186.2 |
| Med 2D | Direct | 463.0250 | 463.0250 |  | 186.2 |
| Med 3R | Fm Hill | 463.0500 | 468.0500 | 186.2 | 186.2 |
| Med 4D | Direct | 463.0750 | 463.0750 |  | 186.2 |
| Med 5R | Grapevine | 463.1000 | 468.1000 | 186.2 | 186.2 |
| Med 6D | Direct | 463.1250 | 463.1250 |  | 186.2 |
| Med 7R | Mebane | 463.1500 | 468.1500 | 186.2 | 186.2 |
| Med 8D | Direct | 463.1750 | 463.1750 |  | 186.2 |
| Med 9R | County-wide | 462.9500 | 467.950 | 186.2 | 186.2 |
| Med 10D | Direct | 462.9750 | 462.9750 |  | 186.2 |
| Statewide Medical Coordination | 0 | 0 | 0 | N/A |
| Calling Channel Med 7 Med 9 | 463.1500 462.9500 | 468.1500 467.9500 | 186.2 186.2 | 186.2 186.2 |
| Dispatch (for each EMS Agency) Several, Not centralized |  |  |  |  |
| Direct to hospitals Med 9 | 462.9500 | 467.9500 | 186.2 | 186.2 |
| Assigned COR Radio Frequencies (Non-Repeater, line-of-sight only) |
| Med-1 | San Joaquin Hospital | 463.000 | 468.000 | PL 173.8 |
| Med-2 | Mercy Main | 463.025 | 468.025 | PL 173.8 |
| Med-3 | Bakersfield Memorial Hospital | 463.050 | 468.050 | PL 173.8 |
| Med-4 | Delano Regional Medical Center | 463.075 | 468.075 | PL 173.8 |
| Med-5 | Kern Medical Center | 463.100 | 468.100 | PL 173.8 |
| Med-10 | Bakersfield Heart Hospital | 462.975 | 467.975 | PL 173.8 |
| Greater Bakersfield & Delano (Kern Medical Center, Mercy Hospital, San Joaquin Hospital, Bakersfield Memorial Hospital, Heart Hospital, Mercy Southwest Hospital, Delano Regional Medical Center) |
| MED9R | County-wide | 462.9500 | 467.9500 | 186.2 | 186.2 |
| MED5R | Grapevine | 463.1000 | 468.1000 | 186.2 | 186.2 |
| Kern Valley Hospital |
| MED9R | County-wide | 462.9500 | 467.9500 | 186.2 | 186.2 |

| Tehachapi Hospital |
| --- |
| MED9R | County-wide | 462.9500 | 467.9500 | 186.2 | 186.2 |
| MED1R | Soledad | 463.0000 | 468.0000 | 186.2 | 186.2 |
| Ridgecrest Regional Hospital |
| MED9R | County-wide | 462.9500 | 467.9500 | 186.2 | 186.2 |
| MED3R | FM Hill (Lone Butte) | 463.0500 | 468.0500 | 186.2 | 186.2 |
| Other (e.g. tactical, etc.) Med 7 | 463.1500 | 468.1500 | 186.2 | Med-Alert Comm |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Bakersfield Memorial Hospital 					(661) 327-1792					35-23-28.000N/

420 34th Street																					119-00-19.000W

Bakersfield, California 93301 															TLOF 40' x 40'

Bakersfield Heart Hospital 						(661) 316-6000

3001 Sillect Ave

Bakersfield, California 93308

Delano Regional Medical Center					(661) 725-4800

1401 Garces Hwy

Delano, California 93215

Kern Medical Center								(661) 326-2000					35-23-03.000N/

1830 Flower Street 																			118-58-05.000W

Bakersfield, California 93305 															TLOF - 70' Diameter

Mercy Hospital										(661) 632-5000

2215 Truxtun Ave

Bakersfield, California 93301

Mercy Southwest										(661) 663-6000

400 Old River Rd

Bakersfield, California 93311

San Joaquin Community Hospital				(661) 395-3000 					35-23-01.000N/

2615 Eye Street 																				119-01-08.000W

Bakersfield, California 93301 															TLOF - 40'X40'

Kern Valley Hospital								(760) 379-2681 					35-43-41.825N/

6412 Laurel Ave																				118-25-11.305W

Lake Isabella, California 93240 															TLOF - 66' x 66'

Ridgecrest Community Hospital 					(760) 446-3551					35-38-25.000N/

1081 North China Lake Blvd. 															117-40-16.000W

Ridgecrest, California 93555 																TLOF - 77' Diameter.

Tehachapi Hospital 									(661) 822-3241

115 West “E” Street

Tehachapi, California 93561

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| Bakersfield Fire Department | (661) 326-3941 | G | 0 | no | BLS |
| CARE Ambulance | (760) 376-2271 | G | 7 | yes | ALS |
| California City Fire Department | (760) 373-4841 | G | 0 | no | ALS |
| Delano Ambulance | (661) 725-3374 | G | 6 | yes | ALS |
| Hall Ambulance Service, Inc. | (661) 322-8741 | GA | 63 | yes | ALS |
| Kern Ambulance | (661) 758-3200 | G | 7 | yes | ALS |
| Kern County Fire Department | (661) 391-7000 | G | 0 | no | BLS |
| Kern County Fire Department | (661) 391-7000 | A | 1 | yes | BLS |
| Mercy Air Service Inc. | (909) 357-9006 | A | 1 | yes | ALS |
| Liberty Ambulance | (760) 375-6565 | G | 9 | yes | ALS |
| Taft Fire Department | (661) 765-4136 | G | 0 | no | BLS |
| U.S. Borax Ambulance Service | (760) 762-7610 | G | 1 | yes | ALS |

BLS Rescue Aircraft – limited use for transport

#### Los Angeles County EMS Agency

Agency Contact

Cathy Chidester BSN, MSN, Director
10100 Pioneer Blvd., Suite 200
Santa Fe Springs, California 90670
(562) 347-1500

FAX: (562) 941-5835
E-MAIL: cchidester@dhs.lacounty.gov

Channel Use											TX-Freq			RX-Freq		CTCSS	Prim/Alt

| Local Medical Coordination (real time) Shared w/other counties HEAR – intra-county | 155.340 155.280 | N/A N/A | N/A N/A | N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) | N/A | N/A | N/A | N/A |
| Direct to hospital | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) RediNet – For disasters | 968.000 | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Alhambra Hospital 	(626) 570-1606

100 S. Raymond Avenue

Alhambra, California 91801

Antelope Valley Hospital Medical Ctr 			(661) 949-5000					34-41-17.000N/

1600 West Avenue J 																		118-09-31.000W

Lancaster, California 93534 																TLOF - 60' Diameter

Bellflower Medical Center 	(562) 925-8355

9542 E. Artesia Blvd.

Bellflower, California 90706

Beverly Hospital 	(323) 726-1222

309 West Beverly Blvd.

Montebello, California 90640

Brotman Medical Center	(310) 836-7000

3828 Delmar Terrace

Culver City, California 90231

California Hospital Medical Center  	(213) 748-2411 Main

1401 S. Grand Avenue 	(213) 742-5446 ED

Los Angeles, California 90015

Cedars Sinai Medical Center -					(310) 855-5000- Main			34-04-38.000N/

Saperstein Critical Care Tower					(310) 967-8781 – ED			118-22-44.000W

8700 Beverly Blvd. 				89’ Diameter

Los Angeles, California 90048

Centinela Freeman Regional Medical 	(310) 673-4660 - Main

Center, Centinela Campus	(310) 419-8636 - ED

555 East Hardy Street

Inglewood, California 90301

Children’s Hospital of Los Angeles 	(323) 660-2450 - Main	34-05-50.000N/

4650 Sunset Blvd. 	(323) 660-2450 x4455 -	118-17-2.000W

Los Angeles, California 90027 	          ED Manager	TLOF – 50’ Diameter

Citrus Valley Medical Center 	(626) 331-7331- ED

Inter-Community Campus

210 W. Bernardino Road

Covina, California 91723

Citrus Valley Medical Center						(626) 962-4011 - ED

Queen of the Valley Campus

1115 S. Sunset Avenue

West Covina, California 91790

City of Angels Medical Center	(213) 989-6100

Downtown Campus

1711 West Temple Street

Los Angeles, California  90026

Coast Plaza Doctors Hospital 	(562) 868-3751 - Main

13100 Studebaker Road 	(562) 868-3751 x2158 -

Norwalk, California 90650 	           ED Manager

Community Hospital of Huntington Park	(323) 583-1931

2623 E. Slauson Avenue

Huntington Park, California 90255

Community Hospital of Gardena	(310) 516-7931

1246 West 155th Street

Gardena, California  90247

Community Hospital Of Long Beach	(562) 498-1000

1720 Termino Avenue

Long Beach, California  90804

Daniel Freeman Memorial Hospital	(310) 330-8400	33-58-10.000N/

333 N Prairie Ave		118-20-40.000W
Inglewood, California 90301-4514		TLOF – 65’ x 65’

Doctors Hospital of West Covina	(626) 338-0502

725 S. Orange Avenue

West Covina, California 91790

Downey Regional Medical Center	(562) 904-5000 - Main

11500 Brookshire Avenue	(562) 904-5119 -

Downey, California 90241 		ED Manager

East Los Angeles Doctors Hospital	(323) 268-5514 - Main

4060 E. Whittier Blvd. 	(323) 268-5514 x200 -

Los Angeles, California 90023 		ED Manager

East Valley Hospital Medical Center	(626) 335-0231

150 West Route 66

Glendora, California 91740

Encino Hospital Medical Center 	(818) 995-5000 - Main

16237 Ventura Blvd. 	(818) 995-5350 -

Encino, California 91436 		ED Manager

Foothill Presbyterian Hospital,					(626) 963-8411					34-08-00.000N/

Johnston Memorial	117-52-06.000W

250 S. Grand Avenue 																		TLOF - 40' x 40'

Glendora, California 91740

Garfield Medical Center							(818) 573-2222

525 N. Garfield

Monterey Park, California 91754

Glendale Adventist Medical Center	(626) 409-8202 	34-09-06.000N/

1509 Wilson Terrace 				118-13-45.000W

Glendale, California 91206 				TLOF - 42' x 42'

Glendale Memorial Hospital & Health Ctr	(626) 502-1900

1420 South Central Ave.

Glendale, California 91204

Good Samaritan Hospital – Los Angeles	(213) 977-2121	34-03-16.000N/

616 Witmer Street		118-15-51.000W

Los Angeles, California 90017		TLOF - 55' x 55'

Greater El Monte Community Hospital	(626) 579-7777

1701 N. Santa Anita

El Monte, California 91733

Henry Mayo Newhall Memorial Hospital 	(661) 253-8000

23845 McBean Parkway

Valencia, California 91355

Hollywood Presbyterian Medical Ctr	(323) 413-3000	34-05-47.000N/

1300 N. Vermont Avenue		118-17-22.000W

Los Angeles, California 90027 	TLOF - 40' x 40'

Huntington Memorial Hospital					(626) 397-5000 					34-08-02.000N/

100 W. California Blvd. 																	118-09-10.000W

Pasadena, California 91105 				TLOF – 40’ Diameter

Kaiser Foundation Hospital –	(626) 851-1011

Baldwin Park

1011 Baldwin Park Blvd.

Baldwin Park, California 91706

Kaiser Foundation Hospital – Bellflower 	(562) 461-3000 - ED

9400 E. Rosecrans Avenue

Bellflower, California 90706

Kaiser Foundation Hospital – South Bay	(310) 325-5111

25825 S. Vermont Avenue

Harbor City, California 90710

Kaiser Foundation Hospital -	(213) 580-7200
   Mental Health Center

765 College Street

Los Angeles, California  90012

Kaiser Foundation Hospital -	(818) 375-2000

Panorama City

13652 Cantara Street

Panorama City, California 91402

Kaiser Foundation Hospital – Sunset 	(323) 667-4011

4867 Sunset Blvd.

Los Angeles, California 90027

Kaiser Foundation Hospital –	(323) 857-2000

West Los Angeles

6041 Cadillac Avenue

Los Angeles, California 90034

Kaiser West Los Angeles Hospital –	(818) 719-2000

Woodland Hills

5601 De Soto Avenue

Woodland Hills, California 91367

Lakewood Regional Medical Center	(562) 531-2550

3700 E. South Street

Lakewood, California 90712

Lancaster Community Hospital 	(661) 948-4781

43830 N. 10th Street West

Lancaster, California 93534

Lincoln Hospital Medical Center	(323) 261-1181

443 S. Soto Street

Los Angeles, California 90033

Little Company of Mary Hospital	(310) 540-7676

4101 Torrance Boulevard

Torrance, California 90503

Little Company of Mary, San Pedro Hosp.	(310) 832-3311

1300 W. 7th Street

San Pedro, California 90732

Long Beach Memorial Medical Center			(562) 933-2000					33-48-30.000N/

2801 Atlantic Avenue 																		118-11-11.000W

Long Beach, California 90806 															TLOF - 40' x 40'

Los Angeles County – Harbor-UCLA			(310) 222-2345  					33-49-44.000N/

Medical Center																			118-17-33.000W

1000 W. Carson Street 																		TLOF - 40' x 40'

Torrance, California 90509

Los Angeles County – Olive View  UCLA	(818) 364-1555

Medical Center

14445 Olive View Drive

Sylmar, California 91342

Los Angeles County + USC Medical Center 	(323) 226-2622					34-09-30.000N/

1200 N. State Street 																			118-12-30.000W

Los Angeles, California 90033 															TLOF - 40' x 40'

Los Angeles Community Hospital 	(323) 267-0477

4081 E. Olympic Blvd.

Los Angeles, California 90023

Los Angeles Metropolitan Medical Ctr	(323) 730-7300

2231 South Western Avenue

Los Angeles, CA  90018

Memorial Hospital of Gardena	(310) 532-4200

1145 W. Redondo Beach Blvd.

Gardena, California 90247

Methodist Hospital of Southern California	(818) 445-4441

300 W. Huntington Drive

Arcadia, California 91007

Mission Community Hospital	(818) 787-2222

- Panorama City

14850 Roscoe Blvd.

Panorama City, California 91402

Monterey Park Hospital 	(626) 570-9000

900 S. Atlantic Blvd.

Monterey Park, California 91754

Northridge Hospital Medical Center -			(818) 885-8500					34-13-12.000N/

Roscoe Campus																			118-31-56.000W

18300 Roscoe Blvd. 				TLOF – 60’ Diameter

Northridge, California 91328

Norwalk Community Hospital	(562) 863-4763

13222 Bloomfield Avenue

Norwalk, California

Olive View Medical Center						(818) 364-1555					34-19-36.000N

14445 Olive View Drive																	118-26-39.000W

Sylmar, California  91342																	TLOF – 56’ X 56’

Olympia Medical Center	(310) 657-5900

5925 San Vicente Boulevard

Los Angeles, CA  90019

Pacific Hospital of Long Beach 	(562) 595-1911

2776 Pacific Avenue

Long Beach, California 90806

Pacifica of the Valley Hospital 	(818) 767-3310

9449 San Fernando Road

Sun Valley, California 91352

Pomona Valley Medical Center	(909) 623-8715

1798 N. Garey Avenue

Pomona, California 91767

Presbyterian Intercommunity Hospital			(562) 698-0811  					33-58-16.000N/

12401 E. Washington Boulevard															118-02-57.000W

Whittier, California 90602 																TLOF - 60' x 60'

Providence Holy Cross Hospital	(818) 365-8051 	34-16-47.00N/

Medical Center				118-27-38.00W

15031 Rinaldi 				TLOF – 65’ X 65’

Mission Hills, California 91345

Providence St. Joseph Medical Center			(818) 843-5111 					34-09-20.000N

501 S. Buena Vista Street 																	118-19-41.000W

Burbank, California 91505																	TLOF - 50' x 50'

Providence Tarzana Medical Center			(818) 881-0800

Tarzana Campus

18321 Clark Street

Tarzana, California 91356

San Dimas Community Hospital	(909) 599-6811

1350 W. Covina Blvd.

San Dimas, California 91773

San Gabriel Valley Medical Center	(626) 289-5454

218 S. Santa Anita Street

San Gabriel, California 91776

Santa Monica-UCLA Medical Center 	(310) 319-4000

1250 16th Street

Santa Monica, California 90404

Sherman Oaks Community Hospital	 		(818) 981-7111    				34-09-36.000N

4929 Van Nuys Blvd.   																		118-26-55.000W

Sherman Oaks, California 91403 														TLOF - 48' x 52'

Shriner Hospital for Children-Los Angeles	(213) 388-3151

3160 Geneva Street

Los Angeles, California 90020

St. Francis Medical Center 						(310) 900-7301 					33-48-31.200N

3630 E. Imperial Highway 																118-11-11.800W

Lynwood, California 90262 																TLOF - 94' x 64'

St. John’s Hospital and Health Center	(310) 829-5511

1328 22nd Street

Santa Monica, California 90404

St. Mary Medical Center							(562) 491-9000 					33-46-50.000N

1050 Linden Avenue 																		118-11-09.800W

Long Beach, California 90813 															TLOF - 40' x 40'

St. Vincent Medical Center						(213) 484-5525 					34-03-48.000N

2131 W. 3rd Street 																			118-16-08.000W

Los Angeles, California 90057 															TLOF - 50' x 50'

Torrance Memorial Medical Center	(310) 325-9110

3330 Lomita Blvd.

Torrance, California 90505

Tri-City Regional Medical Center	(562) 860-0401

21530 South Pioneer Boulevard

Hawaiian Gardens, California 90716

USC – University Hospital 						(323) 342-8500					34-03-14.000N/

1500 San Pablo Street 																		118-12-03.000W

Los Angeles, California 90033 															TLOF - 55' x 55'

Valley Presbyterian Hospital	(818) 782-6600

15107 Van Owen Street

Van Nuys, California 91405

Verdugo Hills Hospital								(626) 790-7100 					34-12-15.000N/

1812 Verdugo Blvd. 																		118-13-00.000W

Glendale, California 91208 																TLOF - 62' x 62'

West Hills Regional Medical Center	(818) 676-4000

7300 Medical Center Drive

West Hills, California 91307

White Memorial Medical Center	(323) 268-5000

1720 Cesar Chavez Avenue

Los Angeles, California 90033

Whittier Hospital Medical Center	(562) 945-3561

15151 Janine Drive

Whittier, California 90606

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| APT Ambulance Company | (310) 846-4000 | G | 29 | yes | ALS |
| Alhambra Fire Department | (626) 570-5190 | G | 2/5 | yes | ALS |
| Allen Ambulance Service | (323) 732-9156 | G | 1 | yes | BLS |
| AmbuServe, Inc. | (310) 644-0500 | G | 28 | yes | ALS |
| AmeriCare Ambulance | (310) 835-9390 | G | 6 | yes | ALS |
| AMR-Antelope Valley Division | (800) 433-7522 | G | 20 | yes | ALS |
| AMR-Glendale/San Fernando Div. | (310) 851-7710 | G | 40 | yes | ALS |
| AMR-Los Angeles Division | (310) 851-7710 | G | 89 | yes | ALS |
| AMR-San Gabriel Valley Division | (310) 851-7710 | G | 63 | yes | ALS |
| AMR-Metro/South Division | (310) 851-7710 | G | 69 | yes | ALS |
| Antelope Ambulance Service | (661) 95*-1998 | G | 11 | yes | ALS |
| Arcadia Fire Department | (626) 574-5112 | G | 2/1 | yes | ALS |
| Avalon Fire Department | (310) 510-0203 | G | 1 | yes | BLS |
| Beverly Hills Fire Department | (310) 281-2700 | G | 2/4 | yes | ALS |
| Bowers Ambulance Service | (562) 988-6400 | G | 18 | yes | ALS |
| Burbank Fire Department | (818) 238-3411 | G | 3/8 | yes | ALS |
| Care Ambulance | (714) 828-7937 | G | 94 | yes | BLS |
| Compton Fire Department | (310) 605-5670 | G | 2 | yes | ALS |
| Culver City Fire Department | (310) 253-5900 | G | 2/4 | yes | ALS |
| Downey Fire Department | (562) 904-7301 | G | 2 | yes | ALS |
| El Segundo Fire Department | (310) 524-2395 | G | 2 | yes | ALS |
| Emergency Ambulance Service | (714) 990-1742 | G | 7 | yes | ALS |
| Gerber Ambulance Service | (310) 524-6464 | G | 8 | yes | ALS |
| Glendale Fire Department | (818) 548-4814 | G | 5/12 | yes | ALS |
| Guardian Ambulance Corporation | (626) 792-3688 | G | 8 | yes | ALS |
| Hall Ambulance Service, Inc. | (661) 322-8791 | G | 7 | yes | ALS |
| Hermosa Beach Fire Department | (310) 376-2479 | G | ½ | yes | ALS |
| Huntington Ambulance Service | (310) 904-1550 | G | 3 | yes | ALS |
| Impulse Ambulance, Inc. | (818) 982-3500 | G | 4 | yes | BLS |
| LaHabra Heights Fire Department | (562) 694-8283 | G | 1 | yes | ALS |
| Los Angeles City Fire Department | (213) 485-7153 | GWA | 95/46 | yes | ALS |
| Los Angeles Co. Fire Department | (323) 881-2485 | GWA | 75/21 | no | ALS |
| Los Angeles County Sheriff Dept | (323) 881-7800 | A | 3 | yes | ALS |
| Los Angeles County Lifeguard | (310) 989-7203 | GW | 2 | yes | ALS |
| La Verne Fire Department | (909) 596-5991 | G | 2/2 | yes | ALS |
| Long Beach Fire Department | (562) 570-2500 | G | 9/11 | yes | ALS |
| Manhattan Beach Fire Department | (310) 802-5203 | G | 2 | yes | ALS |
| Mauran Ambulance Service | (818) 365-3182 | G | 9 | yes | BLS |
| Medcoast Med Service, Inc. | (866) 926-9990 | F | 3 | yes | BLS |
| Mercy Ambulance Service | (877) 486-3729 | G | 3 | yes | BLS |
| Westmed/McCormick Ambulance Service | (310) 219-1779 | G | 60 | yes | ALS |
| Med-Event Medical | (909) 880-2979 | G | 12 | yes | BLS |
| MedReach Ambulance | (310) 781-9395 | G | 10 | yes | BLS |
| Monrovia Fire Department | (626) 256-8100 | G | 1/1 | no | ALS |
| Montebello Fire Department | (323) 887-4510 | G | 3/2 | no | ALS |
| Monterey Park Fire Department | (626) 307-1270 | G | 3/2 | yes | ALS |
| Pasadena Fire Department | (626) 744-4655 | G | 9/9 | yes | ALS |
| Priority One Medical Transport | (800) 600-3370 | G | 30 | yes | ALS |
| PRN Ambulance, Inc. | (323) 888-7750 | G | 26 | yes | ALS |
| Redondo Beach Fire Department | (310) 318-0663 | G | 3/3 | no | ALS |
| Rescue Services International | (800) 989-5027 | G | 6 | yes | BLS |
| San Gabriel Fire Department | (626) 308-2880 | G | 1/3 | yes | ALS |
| San Marino Fire Department | (626) 300-0735 | G | 2/1 | yes | ALS |
| Santa Fe Springs Fire Department | (562) 944-9713 | G | 4 | no | ALS |
| Santa Monica Fire Department | (310) 458-8651 | G | ¾ | no | ALS |
| Schaefer Ambulance. Service, Inc | (323) 469-1473 | G | 52 | yes | ALS |
| Sierra Madre Fire Department | (626) 355-1401 | G | 1 | yes | BLS |
| South Pasadena Fire Department | (626) 403-7300 | G | 2/1 | yes | ALS |
| Torrance Fire Department | (310) 781-7000 | G | 7/6 | no | ALS |
| West Coast Ambulance | (800) 880-0556 | G | 14 | yes | ALS |
| West Covina Fire Department | (626) 338-8800 | G | 4/6 | no | ALS |

#### Marin County EMS Agency

Agency Contact

Miles Julihn, EMS Administrator
899 Northgate Dr., Suite 104
San Rafael, CA 94903
(415) 499-6871

FAX: (415) 499-3747
E-MAIL: mjulihn@co.marin.ca.us

Channel Use											TX-Freq			RX-Freq		CTCSS	Prim/Alt

| Local Medical Coordination (real time) | N/A | N/A | N/A | N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | 154.280 | N/A | N/A | N/A |
| Calling Channel – Aircraft to Fire | 156.075 | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) | N/A | N/A | N/A | N/A |
| Direct to hospitals | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

(All MERA Motorola Type II Smart Zone – 480 Trunked System)

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Novato Community Hospital 						(415) 209-1300

180 Rowland Way

Novato, California 94947

Kaiser Hospital, San Rafael						(415) 444-2400

99 Monticello Road

San Rafael, California 94903

Marin General Hospital 							(415) 925-7000

PO Box 8010

San Rafael, California 94912-8010

Helispot Location							Latitude/Longitude						Description of Location

Field												38-06-00.49/								Adjacent to hospital

122-33-38.07

School											38-00-13-50N/								Flat grassy field

122-33-14.69W

Park												37-56-53-66N/

122-32-10.61W

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (415) 499-9191 | G | 10 | yes | ALS |
| Corte Madera Fire Department | (415) 925-5077 | G | 1 | yes | ALS |
| Marin County Fire Department. | (415) 499-3742 | G | 4 | yes | ALS |
| Novato Fire Protection District | (415) 898-9719 | G | 3 | yes | ALS |
| Ross Valley Paramedic Authority | (415) 258-4686 | G | 1 | yes | ALS |
| S. Marin Emergency Med Paramedic System | (415) 389-4144 | G | 4 | yes | ALS |
| San Rafael Fire Department | (415) 485-3307 | G | 3 | yes | ALS |
| St. Joseph's Ambulance Service | (415) 460-6020 | G | 9 | yes | BLS/ALS |
| Stinson Beach Ambulance | (415) 868-0622 | G | 1 | yes | ALS |

#### Merced County EMS Agency

Agency Contact

Chuck Baucom, EMS Administrator
260 East 15th Street
Merced, CA 95340
(209) 381-1255

FAX: (209) 381-1259
E-MAIL: cbaucom@co.merced.ca.us

Channel Use											TX-Freq			RX-Freq		CTCSS	Prim/Alt

| Local Medical Coordination (Med 8) | 468.175 | 463.175 | N/A | N/A |
| --- | --- | --- | --- | --- |
| Local Dispatch Coordination (Med 9) | 467.950 | 462.950 | N/A | N/A |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Ambulance Dispatch | 467.950 | 462.950 | N/A | N/A |
| Direct to hospitals | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) Fire White for disasters CALCORD | 155.400 156.075 | N/A 156.075 | N/A 156.7 | N/A N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Mercy Medical Center-Merced 					(209) 385-7201-ED

301 E. 13th Street

Merced, California 95340

Mercy Hospital 										(209) 384-6444

2740 M Street

Merced, California 95346

Dos Palos Memorial Hospital						(209) 392-6121

2118 Marguerite St.

Dos Palos, California 93620

Memorial Hospital of Los Banos					(209) 826-0591-Main 			37-03-45.8N/

520 West I 																						120-51-43.7W

Los Banos, California 93635 																TLOF - 40' x 40'

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (209) 576-1984 | G | 3 | yes | ALS |
| Air Medical Team | (209) 576-3939 | A | 1 | yes | ALS |
| Atwater Fire Department | (209) 357-6353 | G | 0 | no | BLS |
| CALSTAR | (800) 252-5050 | A | 4 | yes | ALS |
| Los Banos Fire Department | (209) 827-7025 | G | 0 | no | BLS |
| Mediflight of Northern California | (209) 572-7050 | A | 3 | yes | ALS |
| Merced City Fire Department | (209) 385-6897 | G | 0 | no | BLS |
| Merced Co. Fire/CDF | (209) 385-7345 | G | 0 | no | BLS |
| Riggs Ambulance | (209) 725-7011 | G | 14 | yes | ALS |
| Skylife of Central California | (209) 292-5248 | A | 2 | yes | ALS |
| Westside Ambulance | (209) 520-1790 | G | 3 | yes | ALS |

#### Monterey County EMS Agency

Agency Contact

Tom Lynch, EMS Director
19065 Portola Dr Ste I
Salinas, CA 93908
(831) 755-5013

FAX: (831) 455-0680
E-MAIL: lynchtg@co.monterey.ca.us

Channel Use											TX-Freq			RX-Freq		CTCSS	Prim/Alt

| Local Medical Coordination (real time) Med 2 Med 5 Med 6 Med 7 | 468.025 468.100 468.125 468.150 | 463.025 463.100 463.125 463.150 | 173.8 173.8 173.8 173.8 | N/A N/A N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | 0 | 0 | 0 | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) AMR – Med 9 AMR – Med 10 CRFA | 467.950 467.975 156.240 | 462.950 462.975 154.995 | N/A N/A N/A | N/A N/A N/A |
| Direct to hospitals Disaster only | 800 MHz | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Community Hospital of Monterey 				(831) 624-5311

Peninsula

23625 Holman Highway

Monterey, California 93942

Salinas Valley Memorial 							 (831) 757-4333

450 East Romie Lane

Salinas, California 93901

Natividad Medical Center 							(831) 755-4111					36-41-52.000N/

1441 Constitution Blvd.																	121-38-58.000W

Salinas, California 93906																	TLOF - 74' Diameter

George Mee Memorial Hospital 					(831) 385-6000					36-12-30.000N/

300 Canal Street																				121-07-50.000W

King City, California 93930																TLOF - 50' x 50'

Watsonville Community Hospital				(831) 724-4741

75 Nielsen Street

Watsonville, CA 95076

Helispot Location						Latitude/Longitude					Description of Location

Salinas Airport	36-66463664/-121-6119361	Salinas Airport

Marina Airport	36-67384889/-121-76229	Marina Airport

Monterey Airport	36-58665627/-121-8472087	Monterey Airport

Soledad Prison Fire Department	36-46645551/-121-3847101	Soledad Prison Helipad

Greenfield: El Camino Real/	36-32965603/-121.2518764	Greenfield Hall

Cherry Street

835 Forest Avenue	36-61370626/-121.9185501	Pacific Grove Middle School

Pacific Grove		Football Field

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| AMR | (831) 883-3280 | G | 20 | yes | ALS |
| AMR-Santa Cruz | (831) 423-7030 | G | 1 | yes | ALS |
| Big Sur Volunteer Fire Brigade | (831) 667-2113 | G | 0 | no | BLS |
| Cachagua Fire Protection District | (831) 659-7700 | G | 0 | no | BLS |
| Cambria Community Healthcare District | (831) 927-8304 | G | 1 | yes | ALS |
| Carmel Regional Fire Ambulance | (831) 624-7881 | G | 3 | yes | ALS |
| Carmel Valley Fire Protection Dist | (831) 659-2021 | G | 3 | yes | ALS |
| Carmel-by-the-Sea Fire Dept | (831) 624-1718 | G | 0 | no | BLS |
| Carmel-by-the-Sea Police Dept | (831) 624-6304 | G | 0 | no | BLS |
| CDF-Aromas Tri-County Fire Protection District | (831) 333-2600 | G | 0 | no | BLS |
| CDF-Carmel Highlands Fire Protection District | (831) 333-2600 | G | 0 | no | BLS |
| CDF-Consolidated State Resources | (831) 333-2600 | G | 0 | no | BLS |
| CDF-Cypress Fire Protection Dist | (831) 647-6208 | G | 0 | no | ALS |
| CDF-Pebble Beach | (831) 333-2600 | G | 0 | no | ALS |
| CDF- South Monterey County | (831)678-0690 | G | 0 | no | BLS |
| Central Coast Ambulance Services | (831) 899-3100 | G | 11 | wc | BLS |
| CHP-Monterey HQ | (831) 796-2100 | G | 0 | no | BLS |
| CSUMB Police Department | (831) 582-3360 | G | 0 | no | BLS |
| Del Ray Oaks Police Department | (831) 349-9333 | G | 0 | no | BLS |
| Department of Fish and Game | (831) 649-2870 | G | 0 | no | BLS |
| Gonzales Police Department | (831) 675-4235 | G | 0 | no | BLS |
| Gonzales Volunteer Fire Dept. | (831) 675-4223 | G | 0 | no | BLS |
| Greenfield Police Department | (831) 674-5111 | G | 0 | no | BLS |
| Greenfield Volunteer Fire Dept | (831) 674-5484 | G | 0 | no | BLS |
| King City Police Department | (831) 385-4848 | G | 0 | no | BLS |
| King City Volunteer Fire Dept | (831) 385-3343 | G | 0 | no | BLS |
| Marina Dept of Public Safety | (831) 384-5225 | G | 0 | no | BLS |
| Mid Coast Fire Brigade | (831) 624-3473 | G | 0 | no | BLS |
| Monterey Fire Department | (831) 646-3900 | G | 0 | no | BLS |
| Monterey Peninsula Airport Fire Department | (831) 648-7008 | G | 0 | no | BLS |
| Monterey Police Department | (831) 646-3805 | G | 0 | no | BLS |
| Naval Postgraduate School Police | (831) 656-2556 | G | 0 | no | BLS |
| North County Fire Protection Dist | (831) 633-2578 | G | 0 | no | BLS |
| Pacific Grove Fire Department | (831) 648-3110 | G | 0 | no | BLS |
| Pacific Grove Police Department | (831) 648-3147 | G | 0 | no | BLS |
| Parks Department – South County | (831) 427-2311 | G | 0 | no | BLS |
| POM-DLI/Fort Ord Police Dept | (831) 242-7738 | G | 0 | no | BLS |
| POM-Fort Hunter-Liggett | (831)386-2517 | G | 3 |  | BLS |
| POM-Fort Ord Fire Department | (831) 242-7545 | G | 0 | no | BLS |
| Salinas Fire Department | (831) 758-7261 | G | 0 | no | ALS |
| Salinas Police Department | (831) 758-7236 | G | 0 | no | BLS |
| Salinas Rural Fire District | (831) 455-1828 | G | 0 | no | ALS |
| San Ardo Volunteer Fire Dept | (831) 627-2465 | G | 0 | no | BLS |
| San Luis Ambulance | (831) 543-2626 | G | 17 | yes | ALS |
| Seaside Fire Department | (831) 899-6262 | G | 0 | no | BLS |
| Sheriff-Central Patrol (Salinas) Station | (831) 755-3807 | G | 0 | no | BLS |
| Sheriff-Coastal (Monterey) Station | (831) 647-7675 | G | 0 | no | BLS |
| Sheriff-Custody Operations Bureau | (831)755-3789 | G | 0 | no | BLS |
| Sheriff-Search and Rescue (SAR) Team | (831) 647-7702 | G | 0 | no | BLS |
| Sheriff-South County Station (KC) Station | (831) 385-8366 | G | 0 | no | BLS |
| Sheriff- Special Operations (Salinas) | (831) 755-3775 | G | 0 | no | BLS |
| Sheriff’s Office-HQ | (831)755-3803 | G | 0 | no | BLS |
| Soledad Fire Department | (831) 678-2054 | G | 0 | no | BLS |
| Soledad Police Department | (831) 678-1332 | G | 0 | no | BLS |
| Spreckels Volunteer Fire Company | (831) 455-2211 | G | 0 | no | BLS |
| U.S. Forest Services-Monterey | (831) 385-5434 | G | 0 | no | BLS |

#### Mountain Valley EMS Agency

Agency Contact

(Alpine, Amador, Calaveras, Mariposa, Stanislaus) 
Steve Andriese, EMS Administrator
1101 Standiford Ave #D1
Modesto, CA 95350
(209) 529-5085

FAX: (209) 529-1496
E-MAIL: sandriese@mvemsa.com

Channel Use											TX-Freq			RX-Freq	CTCSS		Prim/Alt

| Local Medical Coordination (real time) Alpine Med 1 Med 2 Amador Med 13 Med 3 Med 8 Med 9 Calaveras Med 3 Med 9 Mariposa Med 8 Med 14 Stanislaus Med 1 Med 5 All Hospitals VHF Med - HEAR | 468.000 468.025 458.425 468.250 468.175 468.950 468.050 467.950 468.175 456.425 468.000 468.100 | 463.000 463.025 453.425 463.050 463.175 463.950 463.050 462.950 463.175 451.425 463.000 463.100 155.385 | 100.0 179.9 100.0 167.9 100.0 100.0 107.2 167.9 123.0 149.9 179.9 179.9 88.5 | Prim Prim Prim Alt Alt Alt Alt Prim Prim Alt |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Alpine Medical Markleeville Bear Valley Alpine Fire Kirkwood-Camino (CDF) Bear Valley-San Andreas Amador Medical VHF Med 10 Amador Fire Camino (CDF) Calaveras Medical Med 9 Calaveras Fire San Andreas (CDF) Mariposa Medical Mariposa CDF Mariposa CDF-Med 14 Stanislaus Medical AMR Stanislaus Fire Modesto City Stanislaus County Fire | 154.100 154.100 159.225 159.450 159.225 467.975 159.225 467.950 159.450 151.460 451.425 151.5725 155.295 154.145 153.770 | 153.800 153.800 151.190 151.175 151.190 462.975 151.190 462.950 151.175 159.390 451.425 160.055 155.295 155.940 153.770 | 107.2 131.8 123.0 156.7 123.0 100.0 123.0 167.9/ 103.5 110.9 146.2 179.9 1110.9 88.5 123.0 123.0 | Prim Prim Prim Prim Alt Prim Prim Prim Prim Prim Alt Prim Alt Duplex |
| Direct to hospitals | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Sutter Amador Hospital 							(209) 223-7500 					38-21-00.000N/

810 Court Street 																				120-45-48.000W

Jackson, California 95642 																	TLOF - 60' Diameter

Mark Twain St. Joseph Hospital 					(209) 754-3521 					38-11-34.000N/

768 Mountain Ranch Road 																120-40-24.000W

San Andreas, California 95249 															TLOF - 70' Diameter

John C. Fremont Hospital							(209) 966-3631 					37-30-10.000N/

5189 Hospital Road 																			119-58-90.000W

Mariposa, California 95338 																TLOF - 65' Diameter

Temp. Ground Base

Emanuel Medical Center 							(209) 667-4200 					37-30-44.000N/

825 Delbon Avenue 																			120-50-18.000W

Turlock, California 95380 																	TLOF – 45' Diameter

Proposed Rooftop

37-30-44.000N/

120-50-18.000W

TLOF - 65' x 65'

Memorial Medical Center 							(209) 526-4500 					37-40-10.000N/

1800 Coffee Road 																			120-58-19.000W

Modesto, California 95355 																TLOF - 30' Diameter

Oak Valley Hospital 								(209) 847-3011 					37-45-30.000N/

350 South Oak 																				120-51-35.000W

Oakdale, California 95361 																TLOF - 50' Diameter

Doctors Medical Center 							(209) 578-1211 					37-39-53.000N/

1441 Florida Avenue 																		120-59-46.000W

Modesto, California 95350 																TLOF - 65' x 65'

Kaiser Permanente Hospital	(209) 557-1000

4601 Dale Road

Modesto, California

Helispot Location						Latitude/Longitude					Description of Location

| Alpine County |
| --- |
| Bear Valley Ski Resort | 38 29.53 120 02.67 | Land in Parking Lot on North end of Building (Elevation 7050’) |
| Bear Valley Resort | 38 27.03 120 02.06 | Right along Hwy 4. Across the street from Air Strip. Caution: Light Poles along road (Elevation 6700’) |
| Kirkwood Meadows | 38 41.58 120 04.29 | (Elevation 7500’) |
| Amador County |
| Bear River (Quarry) | 38 32.28 120 15.56 | On the spillway side of the first dam. (Elevation 5796’) |
| Calvary Chapel [18480 Ridge Road, Pine Grove] | 38 24.85 120 41.14 | S side of Ridge Road between Druid Lane and Toma Lane. (Elevation 2355’) |
| Camino Del Apparacio | 38 29.94 120 39.48 | S side of Fiddletown Road 2 1/2 miles W of the Shake Ridge Road intersection. (Elevation 2797’) |
| Cdf Academy [4501 Highway 104, Ione] | 38 22.03 120 56.55 | E side of Highway 104 between Preston and Mule Creek Prisons. (Elevation 330’) |
| Colburn Field [Plymouth] | 38 28.57 120 51.05 | W of Highway 49 on S end of Amador County Fairgrounds @ ball field. (Elevation 1070’) |
| Comanche Boatramp | 38 14.21 120 56.82 | S of Comanche Parkway @ end of Comanche Parkway @ Park Headquarters office. (Elevation 281’) |

| Darling Ranch [15851 Shake Ridge Rd] | 38 26.62 120 43.95 | N side of Shake Ridge Rd., ¼ mile E of East Quartz Mt. Rd. (Elevation 1897) |
| --- | --- | --- |
| Eagle’s Nest [17220 Lambert Road] | 38 26.45 121 00.69 | 1 ½ mile N of Carbondale Road, W side of Lambert Road, behind white gate. (Elevation 233’) |
| Homestead [Ranch House Estates) | 38 24.50 120 37.25 | N of Highway 88 on W side of Homestead Drive. Across from Ranch House Estates (Elevation 2598’) |
| Howard Park (Ione) | 38 20.56 120 55.89 | Soccer field @ SW corner of the sports complex. (Elevation 296’) |
| Iron Mountain Ski Resort | 38 37.50 120 12.60 | 1/16 mile N of Highway 88 on Mormon Emigrant Trail. 1st road to right. (Elevation 7440’) |
| Jackson Valley Sta. #171 [ 2701 Quiver Drive] | 38 14.98 120 57.24 | Intersection of Comanche and Quiver Roads. (Elevation 300’) |
| Kirkwood Meadows | 38 41.58 120 04.29 | (Elevation 7500’) |
| Latrobe [Amador Christian Center] [16829 Latrobe Road] | 38 27.26 120 54.93 | NE corner of the intersection of Highway 16 and Latrobe Road. (Elevation 685’) |
| Lockwood Station #151 [23141 Shake Ridge Road] | 38 29.24 120 35.73 | N of Shakeridge Road near the market. (Elevation 3199’) |
| Lockwood Station #152 | 38 27.67 120 39.51 | NE corner of intersection of Shake Ridge Road and Hale Road (Elevation 2640’) |
| Lumberyard Ranger Station | 38 32.97 120 18.40 | N of Highway 88 immediately W of USFS Lumberyard Ranger Station. (Elevation 6456’) |
| Mace Meadows [26570 Fairway Drive, Buckhorn] | 38 27.28 120 32.03 | N side of Highway 88 at Meadow Drive (Elevation 3000’) |
| Pardee Marina Parking Lot (Main Gate) | 38 17.18 120 52.16 | W side of the Pardee Lake between store and marina fueling station. Widest part of parking lot. (Elevation 566’) |
| Pardee Vista Point | 38 15.92 120 51.32 | E side of Pardee Road ¼ mile N of Pardee Dam (Elevation 764’) |
| Peddler Hill Maintenance Station | 38 35.02 120 15.26 | N side of Highway 88 at CALTRANS Peddler Hill Maintenance Station. (Elevation 7090’) |
| Peddler Hill Vista Point (Aka Bear River Overlook). | 38 33.97 120 15.73 | S side of Highway 88 at Peddler Hill. (Elevation 6768’) |
| Pine Grove Camp [13630 Aqueduct Road] | 38 24.30 120 38.39 | N of Highway 88 off Aqueduct Road. (Elevation 2411’) |
| Pioneer Lumber Mill [Aka Cal Mills (Pioneer)] | 38 26.08 120 30.53 | S side of Highway 88 @ paved entrance to cedar mill. (Elevation 3036’) |
| Plasses’s Resort | 38 38.48 120 07.53 | S side of Hwy 88 at W end of Silver Lake. Between Chapel and lake’s edge @ windsock. (Elevation 7285’) |
| Plymouth Elementary School [18601 Sherwood Street] | 38 28.80 120 51.28 | S side of Main Street at intersection of Sherwood Street. (Elevation 1038’) |
| Plymouth Fairgrounds | 38 28.41 120 50.47 |  |
| River Pines | 38 32.47 120 45.00 | E side of Highway 16E between South Fork of the Cosumnes River and Meadow Drive. (Elevation1950’) |
| UPPER JACKSON VALLEY (Aka Boring Ranch) | 38 19.45 120 54.37 | 1/8 mile S of Hwy 88 on E side of Upper Jackson Valley Road., first farmhouse w/ PG&E lock. (Elevation 399’) |
| Westover Field (Sutter Hill) | 38 22.75 120 48.02 | E of Highway 49 at the end of Airport Road. Land on Marked Helipad on Ramp (Elevation 1690’) |
| 4000’emergency [28233 Highway 88, Amador Pines] | 38 29.84 120 30.47 | N side of Highway 88 near the 4000’ elevation sign. (Elevation 4000’) |
| Calaveras County |
| Angels Camp Pd (Frogtown) | 38 04.54 120 33.54 |  |
| Appaloosa | 38 02.58 120 33.54 | On Hwy 4, NW side of Bear Mountain. North of New Melones (Elevation 1480’) |
| Copperopolis Fire Dept | 37 58.73 120 38.40 | (Elevation 600’) |
| Crescent Cove | 38 10.90 120 22.60 | North side of Hwy 4, two pads (Elevation 3250’) |
| Jenny Lind | 38 05.56 120 52.14 | (Elevation 300’) |
| Mokolumne Hill | 38 18.10 120 42.25 | Land in Ball Park (Elevation 1500’) |
| Moran & Rainey (Arnold) | 38 15.22 120 19.98 | Ball Park at intersection of Moran and Rainey Streets. SW end of Golf Course. Land in parking lot next to pond. (Elevation 4000’) |
| Mountain Ranch Ball Park | 38 13.72 120 32.40 | (Elevation 2400’) |
| Saddle Creek | 37 55.15 120 38.14 | Golf Course by Copperopolis (Elevation 820’) |
| Sandy Gultch Ballpark | 38 22.50 120 31.58 |  |
| Willseyville (Associated Office) | 38 22.24 120 31.69 | (Elevation 3000’) |
| Mariposa County |
| Awahnee Meadow (Yosemite Clinic) | 44.90 119 34.86 | Call Yosemite Fire 20 minutes out (Elevation 4000’) |
| Badger Pass Ski Resort | 37 39.83 119 39.79 | Upper Parking Lot (Elevation 7265’) |
| Cathy’s Valley | 37 26.18 120 05.10 |  |
| Greeley Hill Market | 37 38.48 120 07.91 | (Elevation 2900’) |
| Horseshoe Bend | 37 41.56 120 10.44 | North tip of Lake McClure, Wires at north |
| Mariposa Airport | 37 30.65 120 02.51 | Mountain Peak on North Side of Airport 4360’ (Elevation 2254’) |
| Ponderosa | 37 44.29 120 10.38 | Concrete Helipad East of Coulterville. Sits on Ridgeline. VASI set at 9 (Elevation 2700’) |
| Usona Helipad | 37 27.75 119 47.14 |  |

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| AMR | (209) 567-4000 | G | 26 | yes | ALS |
| Air Medical Team | (209) 550-0881 | A | 1 | yes | ALS |
| Altaville-Melones Fire Protection District | (209) 736-2331 | G | 0 | no | BLS |
| Amador Fire Protection District | (209) 223-6391 | G | 0 | no | BLS |
| American Legion Ambulance | (209) 223-2963 | G | 6 | yes | ALS |
| Bear Valley Fire Department | (209) 753-2232 | G | 0 | no | BLS |
| Burbank-Paradise Fire Protection District | (209) 523-1129 | G | 0 | no | BLS |
| California Department of Forestry-Sutter | (209) 267-5215 | G | 0 | no | BLS |
| Department of Forestry | (209) 966-3622 | G | 0 | no | BLS |
| Ceres Fire Department | (209) 538-5701 | G | 0 | no | BLS |
| City of Angels | (209) 736-4081 | G | 0 | no | BLS |
| Copperopolis Fire Protection Dist | (209) 785-2329 | G | 0 | no | ALS |
| Denair Fire District | (209) 632-5032 | G | 0 | no | BLS |
| Ebbetts Pass Fire Protection Dist | (209) 795-1646 | G | 0 | no | ALS |
| Glenco Rlrd Flat Fire Protection District | (209) 286-1536 | G | 0 | no | BLS |
| Hughson Fire Protection District | (209) 883-2863 | G | 0 | no | BLS |
| Hughson Paramedic Ambulance | (209) 883-9177 | G | 5 | yes | ALS |
| Ione Volunteer Fire Department | (209) 274-4548 | G | 0 | no | BLS |
| Jackson Fire Department | (209) 223-1646 | G | 0 | no | BLS |
| Jackson Valley Fire Protection District | (209) 763-5848 | G | 0 | no | BLS |
| Jenny Lind Fire Protection District | (209) 786-2227 | G | 0 | no | BLS |
| Keyes Fire Protection District | (209) 634-7690 | G | 0 | no | BLS |
| Kirkwood Fire Protection District | (209) 258-4444 | G | 0 | no | BLS |
| Mariposa County Sheriff's Office | (209) 966-3615 | G | 0 | no | BLS |
| Mariposa County Fire Department | (209) 966-4330 | G | 0 | no | BLS |
| Markleeville Volunteer Fire Dept | (916) 694-2357 | G | 0 | no | BLS |
| Medi-Flight of Northern California | (209) 572-7050 | A | 2 | yes | ALS |
| Mercy Medical Transport | (209) 966-5762 | G | 3 | yes | ALS |
| Modesto City Fire Department | (209) 572-9590 | G | 0 | no | BLS/ALS |
| Mokelumne Hill Fire Protection District | (209) 286-1536 | G | 0 | no | BLS |
| Mountain View Fire Protection District | (209) 634-4766 | G | 0 | no | BLS |
| Mountain Ranch Fire Protection District | (209) 754-4330 | G | 0 | no | BLS |
| Murphys Fire Protection District | (209) 728-3864 | G | 0 | no | BLS |
| Newman Fire Dept. | (209) 862-1716 | G | 0 | no | BLS |
| Oak Valley District Ambulance | (209) 847-3011 | G | 4 | yes | ALS |
| Oakdale City Fire Dept. | (209) 847-5904 | G | 0 | no | BLS |
| Oakdale Rural Fire Protection Dist | (209) 847-6898 | G | 0 | no | BLS |
| Patterson District Ambulance | (209) 892-2618 | G | 3 | yes | ALS |
| Pine Grove Conservation | (209) 296-7591 | G | 0 | no | BLS |
| Plymouth Vol. Fire Department | (209) 245-4833 | G | 0 | no | BLS |
| ProTransport 1 Ambulance | (800) 650-4043 | G | 2 | yes | ALS |
| Salida Fire Protection District | (209) 545-0365 | G | 0 | no | BLS |
| Stanislaus Consolidated Fire Dist | (209) 525-4650 | G | 0 | no | BLS |
| Sutter Creek Fire Protection Dist | (209) 267-0285 | G | 0 | no | BLS |
| Turlock City Fire Department | (209) 668-5800 | G | 0 | no | BLS |
| Turlock Rural Fire Protection Dist | (209) 632-3953 | G | 0 | no | BLS |
| Valley Home Fire Protection Dist | (209) 847-8556 | G | 0 | no | BLS |
| Foothill Fire Company | (209) 786-2697 | G | 0 | no | BLS |
| Westside Ambulance | (209) 862-2951 | G | 2 | yes | ALS |
| West Stanislaus Fire Protection District | (209) 892-5621 | G | 0 | no | BLS |
| Westport Fire Protection District | (209) 537-1391 | G | 0 | no | BLS |
| Woodfords Fire Department | (916) 694-2750 | G | 0 | no | BLS |
| Woodland Avenue Fire Protection District | (209) 524-4239 | G | 0 | no | BLS |

#### North Coast EMS Agency

Agency Contact

(Del Norte, Humboldt, Lake) 
Larry Karsteadt, Executive Director
3340 Glenwood Avenue
Eureka, CA 95501
(707) 445-2081

FAX: (707) 445-0443
E-MAIL: larry@northcoastems.com
Or: execdir@northcoast.com

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) | N/A | N/A | N/A | N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Del Norte Ambulance City Ambulance of Eureka Inc. Crescent Fire Protection District Arcata/Mad River Ambulance Service Arcata Fire Department Eureka Fire Department Fortuna Fire Department Garberville Fire Department Humboldt Fire District #1 Loleta Fire Department Clearlake Oaks Fire Department Kelseyville Fire Protection District Lake County Fire Protection District Nice Volunteer Fire Department Upper Lake Fire Protection District Northshore Fire Protection District Briceland Volunteer Fire Dept. Blue Lake Volunteer Fire Dept. CAL FIRE Carlotta Volunteer Fire Dept. Crescent City Volunteer Fire Dept. Ferndale Fire Department Fieldbrook Volunteer Fire Fort Dick Fire District Fruitland Ridge Volunteer Fire Dept. Gasquet Volunteer Fire Dept. Honeydew Volunteer Fire Dept. Hoopa Volunteer Fire Dept. Klamath Volunteer Fire Dept. Kneeland Fire Protection District Korbel Volunteer Fire Dept. Lakeport Fire Dept. Maple Creek Volunteer Fire Dept. Myers Flat Volunteer Fire Dept. Miranda Fire Dept. Orick Volunteer Fire Dept. Palo Verde Volunteer Fire Dept. Orleans Volunteer Fire Dept. Petrolia Fire Protection District Patricks Point Volunteer Fire Dept. Redcrest Fire Department Phillipsville Fire Department Rio Dell Volunteer Fire Dept. Redway Volunteer Fire Dept. Salyer Volunteer Fire Dept. Salmon Creek Volunteer Fire Dept. Scotia Volunteer Fire Dept. Samoa Peninsula Fire Dept. Smith River Volunteer Fire Dept. Shelter Cover Fire Department Southern Trinity Volunteer Fire Dept. South Lake County Fire Dept. Telegraph Ridge Fire Dept. Sprowel Creek Volunteer Fire Dept. Trinidad Volunteer Fire Dept. Westhaven Fire Department Weott Volunteer Fire Department Willow Creek Volunteer Fire Dept. Whitethorn Fire District Yurok Tribe Volunteer Fire Dept. Lake Pillsbury Fire Department |  | 155.175 154.250 155.175 46.06 154.43 33.70 46.22 154.325 154.010 155.205 155.025 155.205 155.025 155.025 | N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A | N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A |
| Direct to hospitals | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Jerold Phelps Community Hospital				(707) 923-3921

733 Cedar Street

Garberville, California 95542

Mad River Community Hospital 				(707) 826-8264					40-54-00.000N/

PO Box 1115 																					124-05-00.000W

Arcata, California 95518 																	TLOF - 60' x 60'

Adventist Health-Redbud Hospital				(707) 994-6486

PO Box 6720

Clearlake, CA 95422

Redwood Memorial Hospital 						(707) 725-7238

3300 Renner Drive

Fortuna, California 95540

St. Joseph Hospital 									(707) 445-8121					40-47-02.000N/

2700 Dolbeer Street 																			124-08-48.000W

Eureka, California 95501 																	TLOF - 62' x 62'

Sutter Coast Hospital 								(707) 464-8511

PO Box 2009

Crescent City, California 95531

Sutter-Lakeside Hospital 						(707) 263-5651 						39-06-21.300N/

5176 Hill Road 																				122-54-20.400W

Lakeport, California 954530 																TLOF - 40 Diameter

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| Arcata Mad River Ambulance Inc. | (707) 822-3353 | G | 1 | yes | ALS |
| City Ambulance of Eureka Inc. | (707) 445-4907 | G | 5 | yes | ALS |
| Clearlake Oaks Fire Department | (707) 998-3294 | G | 2 | yes | ALS |
| Del Norte Ambulance Inc | (707) 487-1116 | GA | 5 | yes | ALS |
| City of Fortuna Ambulance | (707) 445-4907 | G | 2 | yes | ALS |
| City of Gaberville Ambulance | (707) 445-4907 | G | 1 | yes | ALS |
| K’ima W Ambulance | (530) 625-4261 | G | 3 | yes | ALS |
| Kelseyville Fire Protection District | (707) 279-4268 | G | 2 | yes | ALS |
| Lakeport Fire Department | (707) 263-4396 | G | 3 | yes | ALS |
| Lake County Fire Department | (707) 994-2170 | G | 0 | no | ALS |
| Loleta Fire Department | (707) 733-5407 | G | 0 | no | ALS |
| Northshore Fire Department | (707) 274-3100 | G | 2 | yes | ALS |
| Orleans Fire Department | (530) 627-3493 | G | 0 | no | ALS |
| Shelter Cove Fire Department | (707) 986-7507 | G | 0 | no | ALS |
| Southern Trinity Area Rescue | (707) 574-6616 | G | 2 | yes | ALS |
| Southlake County Fire Protection District | (707) 987-3089 | G | 3 | yes | ALS |
| REACH |  | A | 1 | yes | ALS |

#### Northern California EMS Agency

Agency Contact

(Butte, Colusa, Glenn, Lassen, Modoc,

Plumas, Shasta, Sierra, Siskiyou, Tehama, Trinity) 
Dan Spiess, Chief Executive Officer
43 Hilltop Dr.
Redding, CA 96003-2807
(530) 229-3979

FAX: (530) 229-3984
E-MAIL: dspiess@norcalems.org

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) Antelope Peak Bass Mountain Beckwourth Mountain Widow Mountain Bloomer Mountain Bear Springs Cedarville Dyer Mountain Grey Butte Mountain Hayfork Bally Hough Mountain Likely Mountain Mahogany Peak Oregon Mountain Red Hill South Fork Mountain Shasta Bally Shaffer Mountain Slater Butte Southfork Mountain St. John Mountain Tuscan Butte West Prospect Peak | 468.050 468.075 468.175 468.100 468.175 468.175 468.150 468.150 468.000 468.125 468.125 468.100 468.175 468.175 468.125 467.975 468.050 468.075 468.125 468.025 468.025 468.100 468.000 | 463.050 463.075 463.175 463.100 463.175 463.175 463.150 463.150 463.000 463.125 463.125 463.100 463.175 463.175 463.125 462.975 463.050 463.075 463.125 463.025 463.025 463.100 463.000 | 1,8 5,8 4,8 6,8 3,8 6,8 6,8 4,8 1,8 2,8 4,8 6,8 1,8 5,8 7 5,8 5,8 6,8 1,8 5,8 3,8 8,5 8 | N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | 0 | 0 | 0 | N/A |
| Calling Channel | 0 | 0 | 0 | N/A |
| Dispatch (for each EMS Agency) Trinity Center Fire Department Mt. Shasta Ambulance Downieville Fire Department Lewiston Fire Department Happy Camp Ambulance Service Peninsula Fire District Ambulance Surprise Valley Hospital Ambulance Northern Siskiyou Ambulance Trinity County Life Support Westside Ambulance Modoc Medical Center Butte Valley Ambulance Redding Medical Center American Medical Response | 155.925 155.010 46.200 155.925 468.125 153.770 155.175 158.835 155.925 468.025 154.515 N/A 467.975 468.050 467.975 468.050 | 155.115 155.010 46.200 155.115 463.125 154.190 155.175 158.835 155.115 463.025 154.515 N/A 462.975 463.050 462.975 463.050 | N/A N/A N/A N/A N/A N/A N/A N/A N/A 3 N/A N/A 5 5 5 5 | P P P P N/A N/A P N/A P P P N/A Prim Alt Prim Alt |
| City of Etna Ambulance Enloe Hospital Chico Colusa Glenn Air Burney Fire Department Ambulance Salmon River Vol. Fire Rescue Co. McCloud Fire Dept. Ambulance Hyampom Fire Department Plumas District Hospital Ambulance | N/A 467.950 153.905 468.025 154.430 460.675 156.105 151.325 155.925 468.125 | N/A 462.950 153.905 463.025 154.430 460.675 154.250 151.325 155.115 463.125 | N/A N/A 3 N/A N/A N/A N/A N/A PL1 | N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A |
| Direct to hospitals Oroville Hospital St. Elizabeth Hospital Banner Lassen Medical Center Biggs-Gridley Hospital Colusa Regional Medical Center Eastern Plumas Health Care Enole Medical Center Fairchild Medical Center Feather River Hospital Freemont-Rideout Hospital Glenn Medical Center Indian Valley Hospital Mayers Memorial Hospital Mercy Med Center Mt. Shasta Mercy Med Center Redding Modoc Medical Center Mountain Community Health Services Plumas District Hospital Shasta Regional Medical Center Seneca District Hospital Surprise Valley Hospital | 468.175 468.100 468.075 468.175 468.025 468.175 468.075 468.25 468.050 468.050 468.125 155.220 468.025 468.150 468.125 468.100 468.175 468.150 468.050 468.075 468.050 468.125 468.050 468.125 468.125 468.125 468.125 468.025 468.050 468.150 468.025 468.125 468.100 | 463.175 463.100 463.075 463.175 463.025 463.175 463.075 468.025 463.050 463.050 463.125 463.025 436.150 463.125 463.100 463.175 463.150 463.050 463.000 463.050 463.125 463.050 463.125 463.125 463.125 463.125 463.025 463.050 463.150 463.025 463.125 463.100 | N/A PL5 PL6 PL3 PL3 PL4 PL3 PL3 PL1 PL3 PL210.7 PL127.3 PL3 PL4 PL4 PL6 PL6 PL1 PL1 PL5 PL5 PL6 PL6 PL2 PL7 PL4 PL7 PL5 PL5 PL4 PL6 PL4 PL6 | N/A ED Dispatch Prim Sec Prim Sec Prim Air Contact Ground Contacts Air & Trinity County Prim Sec Hayfork Bally Oregon Mtn Prim Sec Ground Contacts Air Contacts Prim |
| Other (e.g. tactical, etc.) (varied by each local agency) |  |  |  |  |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

| Banner Lassen Medical Center 1800 Spring Ridge Dr Susanville, California 96130 | (530) 252-2000 | 40° 26' 18.1752"N/ -120° 39' 2.3688"W TLOF – 50’ Diameter |
| --- | --- | --- |
| Colusa Community Hospital 199 E. Webster Street Colusa, California 95932 | (530) 458-5821 |  |
| Eastern Plumas Health Care 500 First Avenue Portola, California 96122 | (530) 832-4277 |  |
| Enloe Hospital (Medical Center) 1531 Esplanade Chico, California 95926 | (530) 891-7300 | 39° 44' 31.7688"N/ -121° 50' 59.4996"W TLOF - 75’ X 66’ |
| Fairchild Medical Center 444 Bruce Street Yreka, California 96097 | (530) 842-4121 |  |
| Feather River Hospital 5974 Pentz Road Paradise, California 95969 | (530) 877-9361 |  |
| Glenn Medical Center 1133 W. Sycamore Street Willows, California 95988 | (530) 934-1800 |  |
| Mayers Memorial Hospital 43563 State Highway 299E PO Box 459 Fall River Mills, California 96028 | (530) 336-5511 |  |
| Mercy Medical Center Mt. Shasta 914 Pine PO Box 239 Mt. Shasta, California 96067 | (530) 926-6111 | 41° 19' 8.0616"N/ -122° 19' 23.1456"W TLOF – 36’ Diameter |
| Mercy Medical Center Redding 2175 Rosaline Ave PO Box 496009 Redding, California 96049-6072 | (530) 225-6000 | 40° 34' 20.2548"N/ -122° 23' 50.3016"W TLOF – 87’ Diameter |
| Modoc Medical Center 228 McDowell Street Alturas, California 96101 | (530) 233-5131 |  |
| Oroville Hospital 2767 Olive Highway Oroville, California 95966 | (530) 533-8500 | 39° 30' 25.0668"N/ -121° 32' 28.6656"W TLOF – 48’ X 48’ (round) |
| Plumas District Hospital 1065 Bucks Lake Road Quincy, California 95971 | (530) 283-2121 | 39° 56' 21.4224"N/ -120° 57' 45.2088"W TLOF - 65’ X 70’ |
| St. Elizabeth Hospital 2550 Sister Mary Columba Drive Red Bluff, California 96080 | (530) 529-8000 | 40° 8' 57.246"N/ -122° 13' 16.9392"W |
| Seneca District Hospital 130 Brentwood Dr. PO Box 737 Chester, California 96020 | (530) 258-2151 |  |
| Shasta Regional Medical Center 1100 Butte St. Redding, CA 96001 | (530) 244-5400 | North Pad 40-35-11.000N/ 122-23-02.000W TLOF – 45’ X 45’ South Pad 40-35-11.000N/ 122-23-02.000W 54’ Diameter |
| Surprise Valley Hospital 741 Main St. PO Box 246 Cedarville, California 96104 | (530) 279-6111 |  |
| Trinity Hospital 60 Easter Ave. PO Box 1229 Weaverville, CA 96093 | (530) 623-5541 |  |

.

Helispot Location						Latitude/Longitude					Description of Location

Colusa Community Hospital			39° 12' 26.4996"N/

122° 0' 1.0332"W

Eastern Plumas Health Care			39° 48' 18.7164"N/					Lawn

120° 28' 13.9152"W

TLOF – 50’ X 50’

Fairchild Medical  Center				41° 43' 6.9564"N/					Lawn

122° 38' 46.536"W

Feather River Hospital					39° 45' 25.9956"N/

121° 34' 17.1804"W

Glenn Medical Center					39° 31' 13.6812"N/

122° 12' 28.4652"W

Mayers Memorial Hospital			41° 1' 27.5484"N/

121° 25' 27.7608"W

Modoc Medical Center					41° 28' 47.9964"N/

120° 32' 39.8076"W

Seneca District Hospital				40° 18' 18.4428"N/

121° 14' 3.012"W

Surprise Valley Hospital				41° 31' 55.9668"N/

120° 10' 18.8292"W

Trinity Hospital							40° 44' 24.9504"N/

122° 56' 31.0884"W

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (530) 246-9111 | G | 9 | yes | ALS |
| Anderson Fire Department | (530) 378-6699 | G | 0 | no | BLS |
| Burney Fire District | (530) 335-2212 | G | 2 | yes | ALS |
| Butte Co. Fire Department | (530) 538-7111 | G | 0 | no | BLS |
| Butte Valley Ambulance Service | (530) 397-2105 | G | 2 | yes | BLS |
| Cal Fire / Shasta Co. Fire Department | (530) 225-2418 | G | 0 | no | ALS |
| Chester Fire Department | (530) 258-3456 | G | 2 | yes | ALS |
| Coffee Creek Volunteer Fire Dept | (530) 266-3516 | G | 1 | yes | ALS |
| Cottonwood Fire Protection District | (530) 347-4737 | G | 0 | no | BLS |
| Downieville Fire Protection District | (530) 289-3333 | G | 1 | yes | BLS |
| Dunsmuir Fire Department | 530) 235-2551 | G | 0 | no | ALS |
| Eastern Plumas Health Care | (530) 832-4277 | G | 4 | yes | ALS |
| Enloe Hospital | (530) 891-7418 | G | 7 | yes | ALS |
| Etna Ambulance | (530) 467-5256 | G | 2 | yes | ALS |
| Fall River Mills Fire Department | (530) 336-6117 | G | 0 | no | BLS |
| First Responder | (530) 891-4357 | G | 16 | yes | ALS |
| Fort Jones Fire Department | (530) 468-2178 | G | 0 | no | BLS |
| Graeagle Fire Rescue | (530) 836-1340 | G | 0 | no | ALS |
| Grenada Fire Department | (530) 436-2381 | G | 0 | no | BLS |
| Hamilton Branch Fire Protection District | (530) 596-3458 | G | 0 | no | BLS |
| Happy Camp Ambulance | (530) 493-2322 | G | 2 | yes | ALS |
| Happy Valley Fire Department | (530) 357-2345 | G | 0 | no | BLS |
| Hayfork Volunteer Fire Department | (530) 628-5336 | G | 0 | no | BLS |
| Hyampom Fire Department | (530) 628-5701 | G | 1 | yes | BLS |
| Lewiston Volunteer Fire Dept | (530) 778-3965 | G | 1 | yes | BLS |
| Mayers Memorial Hospital | (530) 336-5511 | G | 2 | yes | ALS |
| McArthur Fire Protection District | (530) 336-5026 | G | 0 | no | BLS |
| McCloud Community Service Dist | (530) 964-2422 | G | 1 | yes | BLS |
| Mercy Medical Center | (530) 225-6290 | G | 8 | yes | ALS |
| Modoc Medical Center | (530) 233-5131 | G | 4 | yes | ALS |
| Montague Fire District | (530) 459-5343 | G | 0 | no | BLS |
| Mount Shasta Ambulance | (530) 926-2665 | G | 8 | yes | ALS |
| Mountain Gate Fire Department | (530) 275-3003 | G | 0 | no | ALS |
| Northern Siskiyou Ambulance | (530) 842-3583 | G | 3 | yes | ALS |
| Oak Run Volunteer Fire Company | (530) 547-4324 | G | 0 | no | BLS |
| Old Station Volunteer Fire Dept | (530) 335-7111 | G | 0 | no | ALS |
| Peninsula Fire District | (530) 259-2306 | G | 1 | yes | ALS |
| Plumas District Hospital | (530) 283-1322 | G | 3 | yes | ALS |
| Red Bluff Fire Department | (530) 527-1126 | G | 0 | no | BLS |
| Redding Fire Department | (530) 225-4141 | G | 0 | no | BLS |
| Salmon River Volunteer Fire Rescue Co. | N/A | G | 1 | yes | BLS |
| Shasta Fire Department | (530) 241-4615 | G | 0 | no | ALS |
| Shasta Lake City Fire Protection District | (530) 275-7474 | G | 0 | no | ALS |
| Shasta Lake Volunteer Fire Dept | (530) 238-2129 | G | 0 | no | ALS |
| Shasta Regional Medical Center | (530) 244-5192 | G | 2 | yes | ALS |
| Shingletown Volunteer Fire Dept | (530) 474-3914 | G | 1 | yes | ALS |
| Sierra Emergency Medical Services Alliance (SEMSA) | (530) 257-1803 | G | 4 | yes | ALS |
| South Lassen EMS | (530) 257-0249 | G | 3 | yes | ALS |
| St. Elizabeth Hospital | (530) 529-8000 | G | 5 | yes | ALS |
| Surprise Valley Hospital Amb. | (530) 279-6111 | G | 1 | yes | BLS |
| Tehama County Fire Department | (530) 529-8548 | G | 0 | no | BLS |
| Trinity Center Volunteer Fire Dist | (530) 266-3378 | G | 0 | yes | ALS |
| Trinity County Life Support | (530) 623-2500 | G | 4 | yes | ALS |
| W. Almanor Fire Department | (530) 259-5112 | G | 0 | no | BLS |
| Weed Fire Department | (530) 938-5030 | G | 0 | no | BLS |
| Westside Ambulance Association | (530) 865-3998 | G | 2 | yes | ALS |
| Westwood Fire Department | (530) 256-3589 | G | 1 | no | BLS |
| American Medical Response | (530) 246-9111 | G | 9 | yes | ALS |

#### Orange County EMS Agency

Agency Contact

Greg Boswell, RN, EMS Administrator
405 West Fifth Street, Suite 301A
Santa Ana, CA 92701
(714) 834-3500

FAX: (714) 834-3125
E-MAIL: gboswell@ochca.com

Channel Use	TX-Freq	RX-Freq	CTCSS      Prim/Alt

| Local Medical Coordination (real time) 800 MHz, 6B through 6K | Trunked | Trunked | N/A | Prim |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel - 800 MHz, 6A | Trunked | Trunked | N/A | Prim |
| Calling Channel-UHF –Med10 | 467.950 | 462.950 | 103.5 | Alt |
| For Outside agency interoperability 800 MHz – ICALL UHF – OC Access VHF – OC access Landline- OC Control ONE 714-628-7008 | 866.0125 465.525 159.000 | 821.0125 460.525 151.085 | 156.7 103.5 136.5 | Alt Alt Alt |
| Dispatch (for each EMS Agency) 800 MHz Radio System | Trunked | Trunked | N/A | Prim |
| Direct to hospitals 800 MHz, 4G and 5K | Trunked | Trunked | N/A | Prim |
| Other (e.g. tactical, etc.) 800 MHz Radio System | Trunked | Trunked | N/A | Prim |

Helipad

Emergency Department Facilities	Telephone	Latitude/Longitude

Anaheim General Hospital 	(714) 827-6700

3350 W. Ball road

Anaheim, California 92804

Anaheim Regional Medical Center 	(714) 774-1450

1111 West La Palma Ave.

Anaheim, California 92801

Chapman Medical Center 	(714) 633-0011

2601 E. Chapman Avenue

Orange, California 92869

Childrens Hospital of Orange County	(714) 997-3000	33-46-54.000N/

455 S. Main Street		117-51-51.000W

Orange, California		TLOF 50’ x 50’

Coastal Communities Hospital 	(714) 754-5454

2701 S. Bristol

Santa Ana, California 92704

Huntington Beach Medical Center 	(714) 842-1473

17772 Beach Blvd.

Huntington Beach, California 92647

Saddleback Memorial/San Clemente	(949) 496-1122

654 Camino De Los Mares

San Clemente, California 92672

West Anaheim Medical Center 	(714) 827-3000

3033 West Orange

Anaheim, California 92804

Fountain Valley Regional Hospital 	(714) 966-7200

17100 Euclid Street

Fountain Valley, California 92708

Garden Grove Hospital and Medical Ctr	(714) 537-5160

12601 Garden Grove Blvd.

Garden Grove, California 92843

Hoag Memorial Hospital Presbyterian	(949) 645-8600 		33-37-27.000N/

1 Hoag Drive 			117-55-43.000W

Newport Beach, California 92658 			TLOF - 40' x 40'

Kaiser Permanente Medical Center 	(714) 978-4000

441 Lakeview

Anaheim, California 92807

Kaiser Permanente Medical Center/Irvine	(949) 932-5000

6640 Alton Parkway

Irvine, California 92618

La Palma Intercommunity Hospital 	 (714) 670-7400

7901 Walker Street

La Palma, California 90623

Los Alamitos Medical Center	 (714) 826-6400

3751 Katella Avenue

Los Alamitos, California 90720

Mission Hospital Regional Medical Center 	(949) 364-1400	33-33-38.000N/

27700 Medical Center Road 		117-39-55.000W

Mission Viejo, California 92691 		TLOF - 52' x 96'

Orange Coast Memorial Medical Center	(714) 378-7500

8820 Talbert Avenue

Fountain Valley, California 92708

Placentia Linda Hospital 	(714) 993-2000

1301 North Rose Drive

Placentia, California 92870

Saddleback Memorial Medical Center	(949) 837-4500	33-36-30.000N/

24451 Health Center Road 		117-42-32.000W

Laguna Hills, California 92653 		TLOF - 40' x 40'

St. Joseph Hospital	(714) 633-9111

1100 W. Stewart Drive

Orange, California 92686

St. Jude Medical Center	(714) 871-3280

101 East Valencia Mesa Drive

Fullerton, California 92835

Mission Hospital Medical Center/ Laguna	(949) 499-1311

31872 Coast Highway

South Laguna, California 92677

UC Irvine Medical Center	(714) 456-6011 		33-47-20.000N/

101 The City Drive South 			117-53-23.000W

Orange, California 92868 			TLOF - 40' Diameter

Western Medical Center-Anaheim	(714) 533-6220

1025 S. Anaheim Blvd.

Anaheim, California 92805

Western Medical Center-Santa Ana	(714) 835-3555 		33-45-06.000N/

1001 North Tustin Avenue 			117-49-55.000W

Santa Ana, California 92705 			TLOF - 50' x 50'

Helispot Location	Latitude/Longitude	Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| Ambuserve Ambulance | 310-644-0500 | G | 2 | yes | BLS |
| AmeriCare Ambulance Service | (714) 633-4135 | G | 15 | yes | BLS |
| Anaheim Fire Department | (714) 254-4000 | G | 0 | no | ALS |
| Bowers Ambulance Service | (562) 591-3371 | G | 1 | yes | BLS |
| Brea Fire Department | (714) 990-7644 | G | 0 | no | ALS |
| Care Ambulance Service | (714) 828-7750 | G | 136 | yes | BLS |
| Costa Mesa Fire Department | (714) 754-5106 | G | 0 | no | ALS |
| County Rescue Ambulance | (714) 682-2524 | G | 11 | Yes | BLS |
| Doctor’s Ambulance Service | (949) 951-8535 | G | 27 | yes | BLS |
| Emergency Ambulance Service | (714) 990-1331 | G | 11 | yes | BLS |
| Fountain Valley Fire Department | (714) 593-4436 | G | 0 | no | ALS |
| Fullerton Fire Department | (714) 738-6502 | G | 0 | no | ALS |
| Garden Grove Fire Department | (714) 741-5600 | G | 0 | no | ALS |
| Huntington Ambulance Service | (310) 592-1627 | G | 2 | yes | BLS |
| Huntington Beach Fire Department | (714) 536-5411 | G | 7 | yes | ALS |
| La Habra Police Department | (562) 694-8977 | G | 2 | yes | ALS |
| Laguna Beach Fire Department | (949) 497-0700 | G | 0 | no | ALS |
| Lifeline Ambulance | (800) 700-9344 | G | 10 | Yes | BLS |
| Lynch Ambulance Service | (714) 670-8307 | G | 41 | yes | BLS |
| MedCoast Ambulance | (562) 926 -9920 | G | 25 | Yes | BLS |
| Medix Ambulance Service, Inc. | (949) 470-8921 | G | 29 | yes | BLS |
| Mercy Air Service Inc. | (909) 357-9006 | A | 3 | yes | ALS |
| Newport Beach Fire Department | (949) 644-3101 | G | 5 | yes | ALS |
| Orange City Fire Department | (714) 288-2500 | G | 6 | yes | ALS |
| Orange County Fire Authority | (714) 289-7410 | A | 0 | yes | ALS |
| Pacific Ambulance | (949) 470-2355 | G | 34 | Yes | BLS |
| Premier Medical Transport | (714)353-9556 | G | 7 | Yes | BLS |
| Priority One Medical Transport | (800) 660-3370 | G | 10 | yes | BLS |
| PRN Ambulance | (866) 776- 2274 | G | 5 | Yes | BLS |
| Santa Ana Fire Department | (949) 647-5700 | G | 10 | yes | ALS |
| Schaefer Ambulance Service, Inc | (800) 582-2558 | G | 6 | yes | BLS |
| Shoreline Ambulance | (714 )847-9107 | G | 9 | Yes | BLS |

#### Riverside County EMS Agency

Agency Contact

Bruce Barton, EMS Administrator
PO Box 7600
Riverside, CA 92513-7600
(951) 358-5029

FAX: (951)358-5160
E-MAIL: bbarton@co.riverside.ca.us

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (Real time) MEDNET 1 (Hospital Net) MEDNET 2 (Northwest/ Central Zones) MEDNET 3 (Southwest/Hemet Zones) MEDNET 4 (Desert Zones) | 155.265 155.295 151.355 155.205 | 155.265 155.295 151.355 155.205 | 110.9 110.9 110.9 110.9 | Prim Prim Prim Prim |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) |  |  |  |  |
| Direct to hospitals – (Basic) MEDNET 1 | 155.265 | 155.265 | 110.9 | Prim |
| Corona Regional Medical Center Kaiser - Riverside Parkview Community Hospital Riverside Community Hospital Riverside County Regional Moreno Valley Community Hospital Inland Valley Medical Center Rancho Springs Medical Center Menifee Valley Medical Center Hemet Valley Medical Center San Gorgonio Memorial Hospital Desert Regional Medical Center Eisenhower Medical Center John F. Kennedy Medical Center Palo Verde Community Hospital | DTMF | Prim Prim Prim Prim Prim Prim Prim Prim Prim Prim Prim Prim Prim Prim Prim |  |  |
| Medical Direction - (Paramedic) Med 1 – (Desert Reg, Inland Valley) Med 2 – (RCRMC) Med 3 – (Eisenhower) Med 4 – (JFK, Hemet) Med 5 Med 6 – (Riverside Com. Hosp Med 7 Med 8 – (All Base Hospitals) | 468.000 468.025 468.050 468.075 468.100 468.125 468.150 468.175 | 463.000 463.025 463.050 463.075 463.100 463.125 463.150 463.175 | 167.9 167.9 167.9 167.9 167.9 167.9 167.9 167.9 | Prim Prim Prim Prim Prim Prim Prim Prim |
| Other (e.g. tactical, etc.) CALCORD HEAR (Local) HEAR (Regional) Fire White 1 Fire White 2 Fire White 3 CDF Net 1 CDF Net 2 Western & Eastern Co. Sheriff’s Interface Coachella Valley Co. Sheriff’s Interface Eastern Co. Sheriff’s Interface | 156.075 155.340 155.280 154.280 154.265 151.295 151.385 151.175 159.450 158.760 154.890 | 156.075 155.340 155.280 154.280 154.265 151.295 NA NA 158.850 159.090 158.850 | N/A N/A N/A N/A N/A N/A N/A N/A 110.9 110.9 192.8 | N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Corona Regional Medical Center 				(909) 737-4343 - Main

800 S. Main Street 									(909) 733-6242 - ED

Corona, California 91720

Desert Regional Medical Center 					(760) 323-6511 - Main 			33-50-20.000N/

1150 N. Indian Canyon Drive 					(760) 323-6251 - ED 			116-32-30.000W

Palm Springs, California 92262 															TLOF - 50' x 50'

Eisenhower Medical Center 						(760) 773-1440 – Main			33-45-57.000N/

3900 Bob Hope Drive 								(760) 773-1221 – ED			116-24-20.000W

Rancho Mirage, California 92270 														TLOF - 40' Diameter

Hemet Valley Hospital 								(909) 652-2811 - Main

1116 E. Latham 										(909) 766-6450 - ED

Hemet, California 92543

Inland Valley Regional Medical Center 		(909) 677-8671 – Main			33-35-33.000N/

36485 Inland Valley Drive							(909) 677-9778 – ED			117-14-11.000W

Wildomar, California 92595 																TLOF - 50' x 50'

Riverside Community Hospital 					(909) 788-3300 - Main

4445 Magnolia Ave. 								(909) 788-3200 - ED

Riverside, California 92501

JFK Memorial Hospital 							(760) 347-6191 – Main			33-42-25.000N/

47-111 Monroe Street 								(760) 775-8111 – ED			116-14-02.000W

Indio, California 92201 																	TLOF - 40' x 40'

Menifee Valley Medical Center 					(909) 679-8888 - Main

28400 McCall Blvd. 								(909) 672-7018 - ED

Sun City, California 92586

Riverside County Regional Medical Ctr 		(909) 486-4000 – Main			33-54-46.000N/

26520 Cactus Avenue 								(909) 486-5650 – ED			117-11-00.000W

Moreno Valley, California 912555 														TLOF - 47' Diameter

Moreno Valley Medical Center 					(909) 243-0811 - Main

27300 Iris Avenue 									(909) 243-2018 - ED

Moreno Valley, California 92360

Palo Verde Hospital 									(760) 922-4115 - Main

250 North 1st Street 									(760) 922-4115 x5235- ED

Blythe, California 92225

Kaiser Hospital Riverside 							(909) 353-2000 - Main

10800 Magnolia Ave. 								(909) 353-3661 - ED

Riverside, California 92505

Parkview Community Hospital 					(909) 688-2211 - Main

3805 Jackson Street 									(909) 688-8312- ED

Riverside, California 92503

Rancho Springs Medical Center 					(909) 696-6000 - Main

25500 Medical Center Dr. 							(909) 696-6061 - ED

Murrieta, CA 92562

San Gorgonio Memorial Hospital 				(909) 845-1121 – Main			33-55-51.000N/

600 N. Highland Springs Ave. 					(909) 845-4410- ED				116-56-34.000W

Banning, California 92220 																TLOF – 48’ Diameter

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| AmbuServe Ambulance | (310) 644-0500 | G | 5 | yes | BLS |
| American Medical Response - Riverside | (951) 782-5234 | G | 87 | yes | ALS |
| American Medical Response - Desert | (951) 782-5234 | G | 21 | yes | ALS |
| American Medical Response - Hemet | (951) 782-5234 | G | 22 | yes | ALS |
| Blythe Ambulance Service | (760) 922-6111 | G | 7 | yes | ALS |
| Blythe Fire Department | (760) 922-6111 | G | 0 | no | BLS |
| Cathedral City Fire Department | (760) 770-8200 | G | 4 | yes | ALS |
| Cavalry Ambulance | (888) 774-9900 | G | 6 | yes | BLS |
| CHP Air Operations | (760) 399-0085 | Air | 1 | yes | ALS |
| Corona Fire Department | (951) 736-2220 | G | 0 | no | ALS |
| CRA Ambulance | (951) 943-3654 | G | 9 | yes | BLS |
| Hemet Fire Department | (951) 765-2450 | G | 0 | no | BLS |
| Idyllwild Fire Protection District | (951) 659-2153 | G | 3 | yes | ALS |
| Inland Medical Response Amb. | (951) 686-0053 | G | 2 | yes | BLS |
| Lynch Ambulance | (714) 632-0225 | G | 10 | yes | BLS |
| Mercy Air Transport | (800) 222-3456 | Air | 6 | yes | ALS |
| Mission Ambulance | (800) 899-9100 | G | 17 | yes | BLS |
| Morongo Fire Department | (951) 949-7193 | G | 0 | no | BLS |
| Murrieta Fire Department | (951) 461-6162 | G | 0 | no | ALS |
| Norco Fire Department | (951) 737-8097 | G | 0 | no | ALS |
| Palm Springs Fire Department | (760) 323-8181 | G | 0 | no | ALS |
| Pechanga Fire Department | (951) 506-5332 | G | 0 | no | BLS |
| Premier Ambulance | (909) 433-3939 | G | 2 | yes | BLS |
| Priority One Medical | (800) 600-3370 | G | 3 | yes | BLS |
| Reach | (760) 355-2269 | Air | 1 | yes | ALS |
| Riverside City Fire Department | (951) 782-5321 | G | 0 | no | ALS |
| Riverside Co. Fire Dept - Coves | (951) 955-4700 | G | 8 | yes | ALS |
| Riverside Co. Fire Dept - Indio | (951) 955-4700 | G | 6 | yes | ALS |
| Schaefer Ambulance | (800) 966-4727 | G | 3 | yes | BLS |

#### Sacramento County EMS Agency

Agency Contact

Bruce Wagner, Chief of EMS
9616 Micron Ave, Ste 635
Sacramento, CA 95827
(916)875-9753

FAX: (916) 875-9711
E-MAIL: wagnerems@msn.com

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) | 800 MHz | Analog Trunked radio System |
| --- | --- | --- |
| Statewide Medical Coordination | 868.9875 | 823.9875 | 156.7 | P |
| Calling Channel | 866.0125 | 821.0125 | 156.7 | P |
| Dispatch (for each EMS Agency) | 800 MHz | Analog Trunked Radio System |
| Direct to hospitals | 800 MHz | Analog Trunked Radio System |
| Other (e.g. tactical, etc.) | 868.9875 | 823.9875 | 156.7 | P |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Mercy San Juan Hospital 	(916) 537-5000	38-40-09.000N/

6501 Coyle Avenue 		121-18-53.000W

Carmichael, California 95608 		TLOF - 40' x 40'

Mercy General Hospital 	(916) 453-4545

4001 J. Street

Sacramento, California 95819

Mercy Folsom Hospital 	(916) 983-7400

1650 Creekside Drive

Folsom, California 95630

Tower II

UC Davis Medical Center 	(916) 734-2011 	38-03-17.000N/

2315 Stockton Blvd. 		121-27-21.000W

Sacramento, California 95817 		TLOF - 40' x 40'

Heliport #							38-33-04.000N/					121-27-03.000W					TLOF - 40' x 40'

Methodist Hospital 	(916) 423-3000

7500 Timberlake Way

Sacramento, California 95823

Kaiser South Sacramento 	(916) 688-2000

6600 Bruceville Road

Sacramento, California 95823

Kaiser Hospital Sacramento	(916) 973-5000

2025 Morse Avenue

Sacramento, California 95825

Sutter General Hospital 	(916) 454-2222

2801 L Street

Sacramento, California 95816

Sutter Memorial Hospital 	(916) 454-3333

52nd and F Street

Sacramento, California 95819

Helispot Location						Latitude/Longitude					Description of Location

Mercy General Hospital	38-32.9N/

121-22.3W

Mercy Folsom Hospital	38-40.0N/

121-08.9W

Methodist Hospital	38-27.7N/

121-25.1W

Kaiser South Sacramento	38-28.3N/

121-25.5W

Rideout Memorial Hospital	39-08.4N/

121-35.6W

Sutter Davis Hospital	38-33.4N/

121-46.1

Sutter General Hospital	38-32.9N/

121-22.3W

Sutter Memorial Hospital	38-32.9N/

121-22.3W

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (916) 374-8431 | G | 11 | yes | ALS |
| Auburn Fire Department | (530) 823-4211 | G | 0 | no | BLS |
| Beale AFB Fire Department | (530) 634-8672 | G |  | yes | ALS |
| Bi-County Ambulance Service | (530) 674-2780 | G | 15 | yes | ALS |
| California Highway Patrol | (916) 322-3337 | G | 0 | yes | ALS |
| CDF - Loma Rica/Browns Valley | (530) 749-2316 | G | 0 | no | BLS |
| CDF – Nevada/Yuba/Placer | (530) 823-4904 | G | 0 | no | ALS |
| CALSTAR | (530) 887-8259 | A | 0 | yes | BLS/ALS |
| Capay Valley Fire | (530) 796-3300 | G | 0 | no | BLS |
| Colfax Fire Department | (530) 346-2323 | G | 0 | no | BLS |
| Courtland Fire Protection District | (916) 775-1210 | G | 0 | no | BLS |
| Cosumnes Community Service District | (916) 405-7100 | G | 6 | yes | ALS |
| Davis Fire Department | (530) 757-5684 | G | 0 | no | BLS |
| Delta Fire Protection District | (707) 374-2233 | G | 0 | no | BLS |
| Dobbins Oregon Fire Protection District | (530) 692-1175 | G | 0 | no | BLS |
| Dunnigan Fire Protection District | (530) 724-3315 | G | 0 | no | BLS |
| Dutch Flat Fire Department | (530) 389-2287 | G | 0 | no | BLS |
| Elkhorn Volunteer Fire Dept | (530) 371-4541 | G | 0 | no | BLS |
| Esparto Fire Protection District | (530) 787-330 | G | 0 | no | BLS |
| First Responder EMS Inc. | (916) 381-3780 | G | 18 | yes | ALS |
| Folsom Fire Department | (916) 984-2284 | G | 4 | yes | ALS |
| Foothill Volunteer Fire Depart | (530) 675-2383 | G | 0 | no | BLS |
| Foresthill Safety Club | (530) 367-2509 | G | 2 | yes | BLS/ALS |
| Forty-Niner Fire Protection Dist | (530) 265-4431 | G | 0 | yes | BLS |
| Galt Fire Protection District | (209) 745-1001 | G | 4 | yes | ALS |
| Grass Valley Fire Department | (530) 274-4370 | G | 0 | yes | BLS |
| Herald Fire Protection District | (209) 748-2322 | G | 0 | no | BLS |
| Higgins Fire Protection District | (530) 269-2488 | G | 0 | no | BLS |
| Isleton Fire Protection District | (916) 777-7776 | G | 0 | no | BLS |
| Knights Landing Fire Protection District | (530) 735-6590 | G | 0 | no | BLS |
| Lincoln Fire Department | (530) 645-4040 | G | 0 | no | BLS |
| Linda Fire Department | (530) 743-1553 | G | 0 | no | BLS |
| Madison Fire Protection District | (530) 662-5745 | G | 0 | no | BLS |
| Marysville Fire Department | (530) 741-6622 | G | 0 | no | BLS |
| Medic Ambulance Service | (916) 564-9040 | G | 4 | yes | ALS |
| Nevada City Fire Department | (530) 265-2351 | G | 0 | no | BLS |
| North Star Fire Department | (530) 562-1212 | G | 0 | no | BLS |
| North Tahoe Fire Protection Dist | (530) 583-6913 | G | 0 | no | BLS |
| Penryn Fire Protection District | (916) 663-3389 | G | 0 | no | BLS |
| Placer Consolidated Fire Protection District | (530) 889-7991 | G | 0 | no | BLS |
| Placer County Fire Department | (530) 823-4909 | G | 0 | no | BLS |
| Placer Hills Fire Department | (530) 878-0405 | G | 0 | no | BLS/ALS |
| Pleasant Grove Fire Department | (916) 655-3937 | G | 0 | no | BLS |
| REACH | (707) 447-6886 | A | 1 | yes | ALS |
| Rocklin Fire Department | (916) 632-4150 | G | 0 | no | BLS |
| Sacramento Int. Airport Fire Dept | (916) 874-0648 | G | 0 | no | BLS |
| Sacramento Fire Department | (916) 264-5352 | G | 16 | yes | ALS |
| Sacramento Metropolitan Fire District | (916) 566-4000 | G | 13 | yes | ALS |
| Sierra Nevada Memorial Hospital Ambulance | (530) 274-6233 | G |  | yes | ALS |
| South Placer Fire Department | (916) 791-7059 | G | 3 | yes | ALS |
| Squaw Valley Fire Department | (530) 583-6111 | G | 0 | no | BLS |
| Sutter County Fire | (530) 822-7400 | G | 0 | no | BLS |
| US Forest Service | (530) 367-2224 | G | 0 | no | BLS |
| Walnut Grove Fire Protection District | (916) 417-4070 | G | 0 | no | ALS |
| Wheatland Fire Department | (530) 633-2930 | G | 0 | no | BLS |
| Wilton Fire District | (916) 687-6920 | G | 0 | no | ALS |
| Winters Fire Department | (530) 795-4131 | G | 0 | no | BLS |
| Yuba City Fire Department | (530) 741-4691 | G | 0 | no | BLS |
| TLC Transportation Inc. | (916) 368-5202 | G | 4 | yes | ALS |

#### San Benito County EMS Agency

Agency Contact

Marcie Morrow, EMS Coordinator
1111 San Felipe Rd., Ste. 102
Hollister, CA 95023
(831) 636-4066

FAX: (831) 636-4037
E-MAIL: mmorrow@sanbenitoco.org

Channel Use	TX-Freq	RX-Freq	CTCSS       Prim/Alt

| Local Medical Coordination (real time) | 155.280 | 155.280 | 2000 | Prim |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | 463.000 | 463.00 | 2000 | Prim |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) | N/A | N/A | N/A | N/A |
| Direct to Hospitals (Mednet 1) | 468.000 | 463.000 | 2000 | Prim |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities	Telephone	Latitude/Longitude

Hazel Hawkins Hospital 	(831) 637-5711 – Main	36-49-57.000N/

911 Sunset Drive 	(831) 636-2640 – ED	121-22-57.000W

Hollister, California 95023 		TLOF - 30' x 30'

Helispot Location	Latitude/Longitude	Description of Location

Hollister Airport	36-53-16.3N/121-24-42.31W		Airport

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| AMR | 831-636-9391 | G | 2 | yes | ALS |

#### San Diego County EMS Agency

Agency Contact

Marcy Metz, Acting EMS Director
6255 Mission Gorge Rd.
San Diego, CA 92120
(619) 285-6429 ext. 6546

Fax: (619) 515-6527
E-MAIL: Marcy.Metz@sdcounty.ca.gov

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) Trunked System | 800 MHz | N/A | N/A | N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) | N/A | N/A | N/A | N/A |
| Direct to hospitals Trunked System | 800 MHz | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) Trunked System | 800 MHz | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Alvarado Community Hospital					(619) 287-3270

6655 Alvarado Road

San Diego, California 92120

Rady Children’s Hospital San Diego			(858) 966-8800					32-47-57.000N/

3020 Children’s Way																		117-09-06.000W

San Diego, California 92123 	TLOF – 80’ Diameter

Sharp Coronado Hospital							(619) 435-6251

250 Prospect Place

Coronado, California 92118

Fallbrook Hospital 									(760) 728-1191

624 East Elder Street

Fallbrook, California 92028

Sharp Grossmont Hospital 						(619) 465-0711 – ED				32-46-46.000N/

5555 Grossmont Center Drive 					(619) 644-4066 – Main				117-00-22.000W

La Mesa, California 91941 																	TLOF - 40' x 40'

Kaiser Foundation Hospital 						(619) 528-5000 - Main

4647 Zion Avenue									(619) 528-5700 - ED

San Diego, California 92120

Scripps Mercy Hospital and Medical Ctr 		(619) 294-8111 – Main			32-45-05.000N/

4077 Fifth Avenue 									(619) 686-3800 – ED			117-09-34.000W

San Diego, California 92103 																TLOF - 39' x 39'

US Naval Hospital-San Diego 					(619) 532-6400 - Main

34800 Bob Wilson Drive							(619) 532-82745 – ED

San Diego, California 92134

US Naval Hospital-Camp Pendleton 			(949) 725-1288

US Marine Corps.

Camp Pendleton, California 92055

Palomar Medical Center 							(760) 739-3000					33-07-28.000N/

555 East Valley Parkway 																	117-04-28.000W

Escondido, California 92025 																TLOF - 65' Diameter

Paradise Valley Hospital 							(619) 470-4321

2400 East Fourth Street

National City, California 91950

Pomerado Hospital 									(858) 485-6511					32-59-54.000N/

15615 Pomerado Road 																		117-03-21.000W

Poway, California 92064 																	TLOF - 45' Diameter

Scripps Mercy Hospital-Chula Vista			(619) 691-7000

435 H Street

Chula Vista, California 91910

Scripps Memorial Hospital-Encinitas 			(760) 753-6501 - Main

354 Santa Fe Drive 									(760) 633-7685 - ED

Encinitas, California 92024

Scripps Memorial Hospital-La Jolla 			(858) 457-4123 – Main			32-53-53.000N/

9888 Genesee Drive 								(858) 626-6150 - ED 			117-14-19.000W

La Jolla, California 92038 																	TLOF - 60' Diameter

Sharp Chula Vista Hospital 						(619) 482-3400 - Main 			32-37-11.000N/

751 Medical Center Court 							(619) 482-5825 – ED			117-01-19.000W

Chula Vista, California 91910-6699 													TLOF - 40' Diameter

Sharp Memorial Hospital							(858) 939-3411– ED				32-47-57.000N/

7901 Frost Street										(858) 939-3400 - Main			117-09-115.000W

San Diego, California 92123																TLOF - 40' Diameter

Tri-City Medical Center 							(760) 724-8411- Main 			33-11-07.000N/

4002 Vista Way 										(760) 940-3518 – ED			117-17-25.000W

Oceanside, California 92054 																TLOF - 58' x 68'

UCSD Medical Center 								(619) 543-6222 – Main			32-45-16.000N/

200 West Arbor Drive 								(619) 543-6400 – ED			117-09-53.000W

San Diego, California 92103 																TLOF - 45' x 50'

UCSD Thornton Hospital 							(619) 657-7000 - Main

9300 Campus Point Drive 							(619) 657-7600 - ED

La Jolla, California 92037

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (619) 492-8100 | G | 86 | yes | ALS |
| Alert Ambulance | (619) 298-7203 | G | 6 | yes | BLS |
| Alpine Fire Department | (619) 445-2635 | G | 0 | no | ALS |
| Ambumed Ambulance | (619) 644-5321 | G | 6 | yes | BLS |
| Americare Ambulance | (760) 781-3895 | G | 12 | yes | BLS |
| Balboa Ambulance | (619) 295-1941 | G | 13 | yes | BLS |
| Barona Fire Department | (619) 390-2794 | G | 2 | yes | ALS |
| Bonita-Sunnyside Fire Dept | (619) 479-2346 | G | 0 | no | ALS |
| Borrego Springs Fire Department | (619) 767-5436 | G | 3 | yes | ALS |
| Boulevard CSA | (619) 766-4633 | G | 0 | no | BLS |
| Cal Fire | (619) 588-0364 | G | 0 | no | BLS |
| Camp Pendleton Fire Department | (760) 763-2702 | G | 4 | yes | ALS |
| Campo Reservation Fire | (619) 478-5310 | G | 0 | no | BLS |
| Care Medical Transport | (619) 514-4111 | G | 26 | yes | BLS |
| Carlsbad Fire Department | (619) 931-2141 | G | 3 | yes | ALS |
| Chula Vista Fire Department | (619) 691-5055 | G | 0 | no | BLS |
| Coronado Fire Department | (619) 522-7374 | G | 2 | yes | ALS |
| Deer Springs Fire Department | (619) 749-8001 | G | 0 | no | ALS |
| Del Mar Fire Department | (619) 755-1522 | G | 1 | yes | ALS |
| El Cajon Fire Department | (619) 441-1600 | G | 3 | yes | ALS |
| Elfin Forest Fire Department | (760) 744-2186 | G | 1 | yes | BLS |
| Encinitas Fire Department | (619) 633-2800 | G | 0 | no | ALS |
| ER Ambulance | (619) 401-9900 | G | 2 | yes | BLS |
| Escondido Fire Department | (619) 738-5400 | G | 4 | yes | ALS |
| Federal Fire Department | (619) 556-7001 | G | 6 | yes | ALS |
| Imperial Beach Fire Department | (619) 423-8223 | G | 0 | no | ALS |
| Intermountain Valley Fire Dept | (760) 789-3710 | G | 0 | no | BLS |
| Julian-Cuyamaca Fire Dept | (619) 765-1510 | G | 2 | no | ALS |
| La Mesa Fire Department | (619) 667-1355 | G | 0 | no | ALS |
| Lakeside Fire Department | (619) 390-2350 | G | 2 | yes | ALS |
| Lemon Grove Fire Department | (619) 469-4115 | G | 0 | no | ALS |
| Medfleet Ambulance | (619) 222-2244 | G | 3 | yes | BLS |
| Mercy Air Ambulance | (909) 347-9006 | A | 6 | yes | ALS |
| Mercy Medical Transport | (760) 739-8026 | G | 6 | yes | ALS |
| Miramar Fire Department | (858) 577-6136 | G | 2 | yes | ALS |
| Mt. Laguna Volunteer Fire Dept | (619) 473-8143 | G | 0 | no | BLS |
| NASSCO | (619) 544-8889 | G | 0 | no | BLS |
| National City Fire Department | (619) 336-4271 | G | 0 | no | ALS |
| North County Fire Department | (619) 723-2005 | G | 4 | yes | ALS |
| Oceanside Fire Department | (619) 966-4883 | G | 4 | yes | ALS |
| Ocotillo Wells Fire Department | (619) 358-7735 | G | 1 | yes | BLS |
| Pala Fire Battalion | (619) 742-1632 | G | 0 | no | ALS |
| Palomar Mountain CSA 100 | (619) 742-1693 | G | 0 | no | BLS |
| Pacific Ambulance | (619) 544-8889 | G | 21 | yes | BLS |
| Pine Valley Fire Department | (619) 696-2612 | G | 0 | no | BLS |
| Poway Fire Department | (619) 679-4340 | G | 3 | yes | ALS |
| Priority One Transport | (800) 600-3370 | G | 10 | yes | BLS |
| Ranchita Fire Battalion | (619) 565-5257 | G | 0 | no | BLS |
| Rancho Santa Fe Fire Department | (619) 756-5971 | G | 0 | no | ALS |
| Ramona Municipal Water District | (619) 789-1330 | G | 2 | yes | ALS |
| SDMSE | (619) 280-6060 | G | 85 | yes | ALS |
| San Diego City Fire Department | (619) 533-4300 | G | 0 | no | ALS |
| San Marcos Fire Department | (619) 744-1050 | G | 4 | no | ALS |
| San Miguel Cons. Fire Dept | (619) 670-0500 | G | 0 | no | ALS |
| San Onofre Fire Department | (949) 368-6655 | G | 1 | yes | BLS |
| San Pasqual Fire Department | (619) 745-9565 | G | 0 | no | BLS |
| Santee Fire Department | (619) 258-4100 | G | 2 | yes | ALS |
| Schaefer Ambulance Service, Inc | (619) 583-0454 | G | 4 | yes | BLS |
| Solana Beach Fire Department | (619) 755-1179 | G | 0 | no | ALS |
| Sycuan Fire Department | (619) 445-2614 | G | 2 | yes | ALS |
| Valley Center Fire Department | (619) 751-7600 | G | 0 | no | BLS |
| Viejas Reservation Fire Dept | (760) 751-7600 | G | 1 | yes | ALS |
| Vista Fire Department | (619) 726-2144 | G | 3 | yes | ALS |
| Warner Springs Ranch Fire Dept | (619) 782-3555 | G | 0 | no | BLS |
| West Shore Ambulance Company | (760) 395-6800 | G | 3 | yes | ALS |

#### San Francisco City and County EMS Agency

Agency Contact

John F. Brown, MD, Medical Director

68-12th Street, #220

San Francisco, CA 94103-1242

(415) 355-2607; fax: (415) 552-0194

e-mail: john.brown@sfdph.org

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) San Francisco has a trunked 800 MHz system with 23 frequencies called Citywide Emergency Radio System (CERS) using Motorola equipment. It services police-fire-EMS-sheriff. This works with eight repeaters. Local medical coordination is assigned four talk groups: EMS1, EMS2, EMS3, EMS4. The first two are encrypted for field providers to notify hospitals; the second two are used by Dispatch and the private companies, as well as non-emergency communications with SFFD. EMERGENCY BACK-UP SYSTEM Med 9 Med 10 | 462.95 462.98 | 467.95 467.98 | 167.9 167.9 | Alt-1 Alt-2 |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination HEAR Network | 155.34 | 155.34 | CSQ/ DTMF | Prim |
| Calling Channel | n/a | n/a | n/a | n/a |
| Dispatch (for each EMS Agency) See comments above. The Dispatch talk groups are: FD-A1 FD-A2 FD-A3 | 462.95 462.98 488.36 488.56 488.76 489.11 489.16 489.19 | 467.95 467.98 491.36 491.56 491.76 492.11 492.16 492.19 | 167.9 167.9 506 506 506 506 506 506 | Alt Prim Prim Prim Prim Prim Prim Prim |
| Direct to Hospitals (talk groups): EMSA1-community hospitals EMSA2-SF General, and Base Hospital physician consults |  |  |  |  |
| Other: OES State Fire Net Fire White CALCORD N.Cal. Mutual Aid-9 (Firemars-low) | 159.195 154.280 156.075 821.9125 | 154.160 154.280 156.075 866.9125 | 103.5 CSQ CSQ 156.7 | Alt Alt Alt Alt |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Chinese Hospital										(415) 677-2300

845 Jackson Street

San Francisco, California 94133

Kaiser Permanente Medical Center 				(415) 833-3300

2425 Geary Blvd.

San Francisco, California 94115

California Pacific Medical Center				(415) 641-6625

-St. Lukes Campus

3555 Cesar Chavez

San Francisco, California 94115

California Pacific Medical Center				(415) 600-3333

-Pacific Campus

2333 Buchanan

San Francisco, California 94115

California Pacific Medical Center				(415) 600-6060

- Davies Medical Center

Castro & Duboce Streets

San Francisco, California 94114

St. Francis Memorial Hospital 					(415) 353-6300

900 Hyde Street

San Francisco, California 94121

St. Mary’s Hospital & Medical Center 			(415) 750-5700

450 Stanyan Street

San Francisco, California 94117

San Francisco General Hospital 					(415) 206-8111

1001 Potrero Avenue

San Francisco, California 94110

UCSF/Stanford Medical Center					(415) 502-8841

505 Parnassus Street, L-138

San Francisco, California 94143

VA Medical Center									(415) 221-4810

4150 Clement Street

San Francisco, California 94121

Seton Medical Center								(650) 991-6892

1900 Sullivan Avenue

Daly City, California 94015

Kaiser South City										(650) 742-2513

1200 El Camino Real

So. San Francisco, California 94080

Helispot Location						Latitude/Longitude					Description of Location

Galileo High School	36-48/122-25	Football Field

Nob Hill	37-47/122-25	Stop traffic on Calif. Street

Ferry Park	37-47/122-23

Washington Square	37-48/122-24

James Lang Playground	37-46.897/122.25.527

Jackson Playground	37-45.903/122.23.926

Treasure Island	37-49.411/122.22.410	Soccer Field/asphalt parking lot

Yerba Buena Gardens	37-47/122.24

Kimball Playground	37-46.995/122.25.527

Lafayette Park	37.47/122.25	Grass clearing at the Southeast

Corner of Washington &

Laguna

Moscone Playground	37-48.079/122.25.995

Golden Gate Park	37-46.002/122.27.760	Big Rec

Golden Gate Park	37-46.042/122.27.296	Kezar Stadium

Golden Gate Park	37-45.932/122-29.652	Polo Field

Rossi Playground	37-46.702/122-27.499

South Sunset	37-44.184/122-29.840

West Sunset	37-44.967/122-29.981	No. 3 Playground

West Sunset	37-45.069/122-29.867	No. 2 Playground

Balboa Playground	37-43.355/122-26.725

Crocker Amazon Field	37-42.777/122-26.004

Candlestick Park	37-42.83/122-23.12	Parking Lot – K railed area

between	between gates E & F

Across from RV Park

Rolph Playground	37-44.979/122-24.362

Crissy Field (NPS* LZ# 63)	37-48.15/122-28.01	Access through Marina Gate

Presidio Main Parade Grounds	37-48.02/122-27.29

Fort Scott Parade Grounds	37-48.04/122-28.28

Baker Beach	37-47.34/122-28.60	Parking Lot

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| AMR- S. F. Ambulance Service | (800) 931-9197 | G | 19 | yes | ALS |
| Bayshore | (650) 525-9700 | G |  | yes | ALS |
| Cal Star | (800) 252-5050 | A |  | yes | ALS |
| King American Ambulance Co. | (415) 931-1400 | G | 13 | yes | ALS |
| Life Flight | (800) 321-7828 | A |  | yes | ALS |
| National Park Service | (415) 561-5184 | G | 1 | no | ALS |
| Presidio Fire Department | (415) 561-5656 | G |  | yes | ALS |
| Pro-Transport-1 | (707) 586-4041 | G |  | yes | ALS |
| REACH | (800) 338-4045 | A |  | yes | ALS |
| San Francisco Fire Department | (415) 558-3291 | G | 20 | yes | ALS |
| St. Joseph's Ambulance Service | (415) 921-0707 | G | 2 | yes | BLS |

#### San Joaquin County EMS Agency

Agency Contact

Dan Burch, EMS Administrator

PO Box 1020

Stockton, California 95201

(209) 468-6818

FAX: (209) 468-6725
E-MAIL: dburch@sjgov.org

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) San Joaquin General Hospital – North Co. San Joaquin General Hospital – South Co. Kaiser Hospital Manteca Sutter Tracy Community Hospital Doctors Hospital of Manteca Lodi Memorial Hospital Dameron Hospital St. Joseph’s Medical Center Med 1 Med 2 Med 3 Med 4 Med 5 Med 6 Med 7 Med 8 Med 9 Med 10 | 468.000 468.025 468.050 468.075 468.100 468.125 468.150 468.175 468.000 468.025 468.050 468.075 468.100 468.125 468.150 468.175 467.950 467.975 | 463.000 463.025 463.050 463.075 463.100 463.125 463.150 463.175 463.000 463.025 463.050 463.075 463.100 463.125 463.150 463.175 462.950 462.975 | DPL 132 5B DPL 331 5B DPL 532 5B DPL 732 5B DPL 132 5B DPL 331 5B DPL 532 5B DPL 732 5B N/A N/A | P P P P P P P P P P P P P P P P N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) | N/A | N/A | N/A | N/A |
| Direct to hospitals | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) CALCORD | 156.075 | 156.075 | N/A | N/A |

Dispatch and tactical frequencies for transport and non-transport providers.

| Channel | Function | Rpt/ Smplx | Current | Rx Freq | PL/DPL | Tx Freq | PL/DPL |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Control 1 | North Dispatch | R | Orange | 154.1300 | 110.9 | 156.1200 | 156.7 |
| Control 2 | Countywide Repeated Frequency (NB) | R | Command 1 | 152.3525 | 100.0 | 157.5825 | DPL143 |
| Control 3 | Countywide Repeated Frequency (NB) | R | Command 2 | 152.4125 | 100.0 | 157.6125 | DPL365 |
| Control 4 | South Dispatch | R | Gold | 155.8950 | 82.5 | 154.3100 | 82.5 |
| Control 5 | South Rept Tactical (NB) | R | Ripon COM | 159.1125 | DPL565 | 154.6575 | DPL565 |
| Control 6 | South Rept Tactical | R | Tracy Tac 2 | 154.7250 | 82.5 | 158.8950 | 82.5 |
| Interop | SFD Interoperability | R | STO Pub |  |  |  |  |
| TAC 1 | Fireground Tactical | S | Blue | 154.0700 | 110.9 | 154.0700 | 110.9 |
| TAC 2 | Fireground Tactical | S | Brown | 154.2350 | 156.7 | 154.2350 | 156.7 |
| TAC 3 | Fireground Tactical | S | Gold | 155.8950 | 82.5 | 155.8950 | 82.5 |
| TAC 4 | Fireground Tactical | S | Purple | 158.9400 | 192.8 | 158.9400 | 192.8 |
| TAC 5 | Fireground Tactical | S | Green | 153.9500 | 82.5 | 153.9500 | 82.5 |
| TAC 6 | Fireground Tactical | S | Grey | 154.7250 | 82.5 | 154.7250 | 82.5 |
| TAC 7 | Fireground Tactical | S | SCD (TRY) | 153.8150 | 82.5 | 153.8150 | 82.5 |
| CalCoord | Air Operations | S | CalCord | 156.0750 | CSQ | 156.0750 | CSQ |
| White 1 | Fireground Tactical | S | White 1 | 154.2800 | CSQ | 154.2800 | CSQ |
| White 2 | Fireground Tactical | S | White 2 | 154.2650 | CSQ | 154.2650 | CSQ |
| White 3 | Fireground Tactical | S | White 3 | 154.2950 | CSQ | 154.2950 | CSQ |
| Metro Airport | Airport Tactical | S | Airport Fire | 155.0250 | 127.3 | 155.0250 | 127.3 |
| Lodi Dispatch | Lodi City | R | Lodi Primary | 154.0100 | 192.8 | 159.0600 | 192.8 |
| Manteca City | Manteca City Fire Dispatch | R | SCD | 155.0550 | 82.5 | 153.8150 | 82.5 |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Dameron Hospital 									(209) 944-5550

525 W. Acacia Street

Stockton, California 95203

Lodi Memorial Hospital 							(209) 334-3411 					38-07-21.000N/

975 S. Fairmont Ave. 																		121-17-09.000W

Lodi, California 95240 																		TLOF - 65' x 65'

St. Joseph’s Medical Center 						(209) 467-6400					37-58-16.000N/

1800 N. California Street 																	121-17-15.000W

Stockton, California 95204 																TLOF - 45' x 45'

San Joaquin General Hospital 					(209) 468-6000					37-53-19.000N/

500 W. Hospital Road 																		121-17-02.000W

French Camp, California 95231 															TLOF - 40' Diameter

Doctor’s Hospital Manteca						(209) 823-3111

1205 E. North Street

Manteca, California 95336

Sutter-Tracy Community Hospital 				(209) 835-1500

1420 Tracy Blvd.

Tracy, California 95376

Kaiser Hospital Manteca							(209) 825-3555					37-47-54.000N/

1777 W. Yosemite Avenue 																121-14-44.000W

Manteca, California 95336 																TLOF - 70' x 70'

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| AMR Inc. | (209) 948-5136 | G | 26 | yes | ALS |
| Air Med Team | (209) 576-3939 | A | 1 | yes | ALS |
| Air Methods | (209) 572-7050 | A | 3 | yes | ALS |
| Escalon Ambulance | (209) 838-1351 | G | 2 | yes | ALS |
| Manteca District Ambulance | (209) 823-1032 | G | 5 | yes | ALS |
| Mediplane Inc. (REACH) | (707) 575-6886 | A | 2 | yes | ALS |
| Ripon Fire Department | (209) 599-4209 | G | 1 | yes | ALS |
| Stockton Fire Department | (209) 937-8801 | G | 0 | no | ALS |
| Priority One Medical Transport | (209) 368-7575 | G | 5 | yes | ALS |
| Protransport-1 | (800) 650-4003 | G | 1 | yes | BLS |
| Numerous non transport providers | N/A | G | 0 | no | BLS |

#### San Luis Obispo County EMS Agency

Agency Contact

Charlotte Alexander, EMS Administrator
712 Fiero Ln., #29
San Luis Obispo, CA 93401
(805) 546-8728

FAX: (805) 546-8736
E-MAIL: calexander@sloemsa.org

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) Med 1 Med 2 Med 3 Med 4 | 468.000 468.025 468.050 468.075 | 463.000 463.025 463.050 463.075 | N/A N/A N/A N/A | N/A N/A N/A N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | 0 | 0 | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Med 1 Med 2 Med 3 Med 4 | 468.000 468.025 468.050 468.075 | 463.000 463.025 463.050 463.075 | N/A N/A N/A N/A | N/A N/A N/A N/A |
| Direct to hospitals Med 2 Med 3 Med 4 | 468.050 468.075 | 463.050 463.075 | N/A N/A | N/A N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities	Telephone						Latitude/Longitude

Twin Cities Community Hospital 				(805) 434-3500 – Main			35-33-30.000N/

110 Las Tablas Road 								(805) 434-4550 – ED			121-17-15.000W

Templeton, California 93465 																TLOF – 45’ x 45’

Sierra Vista Regional Medical Center 			(805) 546-7600 - Main

1010 Murray Street 									(805) 546-7650 - ED

San Luis Obispo, California 93401

Arroyo Grande Community Hospital 			(805) 489-4261 - Main

345 S. Halcyon Road 								(805) 473-7626 - ED

Arroyo Grande, California 93420

French Hospital Medical Center 					(805) 543-5353 - Main

1911 Johnson Avenue 								(805) 542-6377 - ED

San Luis Obispo, California 93401

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| CHP Air Operations | (805) 239-3553 | A | 1 | yes | ALS |
| Cambria Community Healthcare | (805) 927-8304 | G | 3 | yes | ALS |
| San Luis Ambulance Service | (805) 543-2626 | G | 11 | yes | ALS |

#### San Mateo County EMS Agency

Agency Contact

Barbara Pletz, EMS Administrator

225 37th Avenue

San Mateo, California 94403

(650) 573-2564

FAX: (650) 573-2029 
E-MAIL:bpletz@co.sanmateo.ca.us

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) | N/A | N/A | N/A | N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) | N/A | N/A | N/A | N/A |
| Direct to hospitals | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Kaiser Hospital Redwood City 					(650) 299-2201

1150 Veterans Blvd.

Redwood City, California 94063

Kaiser Hospital So. San Francisco 				(650) 742-2513

1200 El Camino Real

So. San Francisco, California 94080

Mills Hospital 										(650) 696-5057

100 South San Mateo Drive

San Mateo, California 94402

Peninsula Hospital 									(650) 696-5500

1501 Trousdale Drive

Burlingame, California 94010

Sequoia Hospital 										(650) 367-5541

170 Alameda de Las Pulgas

Redwood City, California 94063

Seton Coastside 										(650) 563-7107

600 Marine Blvd.

Moss Beach, California 94038

Seton Medical Center 								(650) 991-6892

1900 Sullivan Avenue

Daly City, California 94015

San Mateo Medical Center							(650) 573-2761

222 West 39th Avenue

San Mateo, California 94403

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (650) 235-1333 | G | 35 | Yes | ALS/BLS |
| Bayshore Ambulance | (650) 525-3855 | G | 12 | Yes | BLS |
| Belmont/San Carlos Fire Dept | (650) 802-4255 | G | 0 | No | ALS |
| CALSTAR | (916) 921-4000 | A | 3 | Yes | ALS |
| Central County Fire Authority | (650) 558-7600 | G | 0 | No | ALS |
| CDF | (650)573-3842 | G | 0 | No | ALS |
| Coastside Fire Protection District | (650) 726-5213 | G | 0 | No | ALS |
| Coloma Fire Department | (650) 755-5666 | G | 0 | No | ALS |
| Foster City Fire Department | (650) 286-3350 | G | 0 | No | ALS |
| Life Flight | (650) 723-5578 | A | 1 | Yes | ALS |
| Millbrae Fire Department | (650) 259-2400 | G | 0 | No | ALS |
| North County Fire Authority | (650) 991-8138 | G | 0 | No | ALS |
| Redwood City Fire Department | (650) 780-7400 | G | 0 | No | ALS |
| San Francisco Int’l Airport (City & County of San Francisco) | (650) 821-4650 (650) 821-7405 (650) 821-4610 | G | 0 | No | ALS |
| San Bruno Fire Department | (650) 616-7096 | G | 0 | No | ALS |
| San Mateo Fire Department | (650) 522-7900 | G | 0 | No | ALS |
| South San Francisco Fire Dept | (650) 829-3950 | G | 4 | Y | ALS |
| Woodside Fire Protection District | (650) 851-1594 | G | 0 | No | ALS |

#### Santa Barbara County EMS Agency

Agency Contact

Nancy Lapolla, EMS Administrator

300 North San Antonio Road

Santa Barbara, California 93110

(805) 681-5274

FAX: (805) 681-5142
E-MAIL: nancy.lapolla@sbcphd.org

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) | N/A | N/A | N/A | N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Med 10 | 467.975 | 462.975 | 167.9 | N/A |
| Patch to hospitals Med1 Med 2 Med 3 Med 4 Med 5 (SB Cottage Hospital) Med 6 (Goleta & Santa Ynez Cottage Hospitals) Med 7 (Lompoc Valley Med Ctr) Med 8 (Marian Medical Center) | N/A N/A N/A N/A 468.100 468.125 468.150 468.175 | N/A N/A N/A N/A 463.100 463.125 463.150 463.175 | 173.8 173.8 186.2 146.2 146.2 167.9 N/A N/A | N/A N/A N/A N/A N/A N/A N/A N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |
| Med Net intercom – all hospitals & EMS Agencies are linked on an intercom system (Telco & Microwave networked). Hospitals can selectively call each other or perform a call. |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Santa Barbara Cottage Hospital 			(805) 569-7210

PO Box 689

Santa Barbara, California 93102

Goleta Valley Cottage Hospital 					(805) 967-3411 					34-26-02.000N/

351 South Patterson Avenue 																119-48-31.000W

Santa Barbara, California 93111 															TLOF - 40' Diameter

Lompoc Valley Medical Center					(805) 737-3333

508 East Hickory Avenue

Lompoc, California 93436

Marian Medical Center								(805) 739-3000 					34-57-03.000N/

1400 E. Church Street 																		120-24-42.000W

Santa Maria, California 93454 															TLOF - 56' x 56'

Santa Ynez Valley Cottage Hospital 			(805) 688-6431

700 Alamo Pintado Road

Solvang, California

Helispot Location						Latitude/Longitude					Description of Location

Santa Barbara Cottage Hospital	34 25.881N/	Via KSBA Airport

119 50.084W	Signature Air

Lompoc Valley Medical Ctr	34 39.980N/ 	Via KLPC Airport

120 27.512W

Santa Ynez Valley Cottage Hosp.	34 36.119N/	Dirt area next to hosp

120 7.519W

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (805) 688-5500 | G | 30 | yes | ALS |
| CA Lifeguard/Department Parks-Recreation | (805) 968-3834 | G | 0 | no | BLS |
| Carpinteria Summerland Fire | (805) 684-4591 | G | 0 | no | ALS |
| County of Santa Barbara Parks Department | (805) 568-2461 | G | 0 | no | BLS |
| Guadalupe Fire Department | (805) 343-1444 | G | 0 | no | BLS |
| Guadalupe Police Department | (805) 343-2112 | G | 0 | no | BLS |
| Lompoc City Fire Department | (805) 736-4513 | G | 0 | no | BLS |
| Lompoc Police Department | (805) 736-2341 | G | 0 | no | BLS |
| Montecito FPD | (805) 969-7762 | G | 1 | no | ALS |
| Santa Barbara City Lifeguard | (805) 897-2574 | G | 0 | no | BLS |
| Santa Barbara County Fire Dept | (805) 681-5500 | G | 4 | yes | ALS |
| Santa Barbara City Fire | (805) 965-5254 | G | 0 | no | BLS |
| Santa Barbara Police Department | (805) 897-2300 | G | 0 | no | BLS |
| Santa Barbara Sheriff Department | (805) 681-4100 | G | 0 | no | BLS |
| Santa Maria Fire Department | (805) 925-2631 | G | 0 | no | BLS |
| Santa Maria Police Department | (805) 925-0951 | G | 0 | no | BLS |
| UCSB Police Department | (805) 893-3446 | G | 2 | yes | ALS |

#### Santa Clara County EMS Agency

Agency Contact

Bruce H. Lee, EMS Administrator

645 South Bascom, Room 138

San Jose, California 95128

(408) 885-4250

FAX: (408) 885-3538
E-MAIL: BruceH.Lee@hhs.co.santa-clara.ca.us

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) Cellular | N/A | N/A | N/A | N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) | T-811.4375 | 94.8 | R-856.4375 | (192.5) |
| Direct to hospitals | T-812.4375 | 156.7 | R-857.4375 | (225.7) |
| Other (e.g. tactical, etc.) Radio Paging Signs | 458.100 | 453.100 | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Good Samaritan Hospital 							(408) 559-2217

2425 Samaritan Drive

San Jose, California 95124

Stanford University Hospital 						(650) 723-7337					37-26-08.000N

300 Pasteur Drive, Suite H1249 															122-10-26.000W

Stanford, California 94305 																TLOF - 72' x 72'

Kaiser Medical Center- Santa Clara				(408) 851-5312					37-23-93.000N/

700 Lawrence Expressway 																121-79-99.000W

Santa Clara, California 95051 															TLOF – 50’ x 50’

Palo Alto Veterans Hospital						(650) 493-5000

3801 Miranda Avenue

Palo Alto, California 94304

Community Hospital of Los Gatos 				(408) 866-4040

815 Pollard Road

Los Gatos, California 95030

Santa Clara Valley Medical Center 				(408) 885-6987					37-18-51.000N

751 South Bascom Avenue 																121-56-03.000W

San Jose, California 95128 																TLOF - 65' x 65'

Saint Louise Hospital								(408) 848-8681					37-02-09.000N/

9400 No Name Uno 																			121-34-17.000W

Gilroy, California 94020 																	TLOF - 50' x 50'

Regional Medical Center of San Jose			(408) 259-5000 					37-21-45.000N/

225 N. Jackson Avenue 																	121-50-54.000W

San Jose, California 95116 																TLOF – 54’ x 54’

O’Connor Hospital 									(408) 947-2666

2105 Forest Avenue

San Jose, California 95128

El Camino Hospital 									(650) 940-7055

2500 Grant Road

Mountain View, California 94042

Kaiser San Jose Medical Center					(408) 972-7782

250 Hospital Parkway

San Jose, California 95119

Helispot Location						Latitude/Longitude					Description of Location

Good Samaritan Hospital				37-25-21.000N/

121-94-65.000W

Palo Alto Veterans Hospital			37-39-98.000N/

122-13-62.000

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| (City) Campbell Police Dept | (408) 866-2121 | G | 0 | no | BLS |
| (City) Gilroy Fire Department | (408) 848-0385 | G | 1 | no | ALS/BLS |
| (City) Gilroy Police Dept. | (408) 848-0329 | G | 0 | no | BLS |
| (City) Los Altos Police Dept | (650) 948-8223 | G | 0 | no | BLS |
| (City) Milpitas Fire Department | (408) 942-2394 | G | 0 | no | ALS/BLS |
| (City) Milpitas Police Department | (408) 942-3911 | G | 0 | no | BLS |
| (City) Morgan Hill Police Dept | (408) 776-7304 | G | 0 | no | BLS |
| (City) Mountain View Fire Dept | (650) 903-6803 | G | 0 | no | ALS/BLS |
| (City) Mountain View Police Dept | (650) 903-6354 | G | 0 | no | BLS |
| (City) Palo Alto Fire Department | (650) 329-2220 | G | 3 | yes | ALS/BLS |
| (City) Palo Alto Police Dept | (650) 329-2556 | G | 0 | no | BLS |
| (City) San Jose Fire Department | (408) 277-4084 | G | 0 | no | ALS/BLS |
| (City) San Jose Police Dept | (410) 277-4000 | G | 6 | no | BLS |
| (City) Santa Clara Fire Dept | (408) 984-3054 | G | 0 | no | ALS/BLS |
| (City) Santa Clara Police Dept | (408) 261-5324 | G | 3 | no | BLS |
| (Town) Los Gatos Police Dept | (408) 354-4257 | G | 0 | no | BLS |
| American Medical Response -West | (408) 574-3800 | G | 95 | yes | ALS/BLS |
| AMTRAK Police | (408) 271-3546 | G | 0 | no | BLS |
| Bayshore Ambulance | (650) 525-3855 | G | 7 | yes | BLS |
| California Dept of Forestry | (408) 779-2121 | G | 0 | no | BLS |
| Calif. Highway Patrol – Gilroy | (408) 848-2324 | G | 0 | yes | BLS |
| Calif. Highway Patrol - Redwood City | (650) 369-6261 | G | 0 | no | BLS |
| Calif. Highway Patrol - San Jose | (408) 277-1800 | G | 0 | no | BLS |
| CSU Police Dept | (408) 924-2222 | G | 0 | no | BLS |
| California Community College District Police | (650) 949-7317 | G | 0 | no | BLS |
| California Community College District Police | (408) 864-5555 | G | 0 | no | BLS |
| California Community College District Police | (408) 288-3735 | G | 0 | no | BLS |
| California Shock Trauma Air Rescue | (510) 887-3063 | A | 2 | yes | ALS |
| California Community College District Police | (408) 741-2092 | G | 0 | no | BLS |
| FBI - San Jose | (408) 998-5633 | G | 0 | no | BLS |
| Golden State Medical Services | (408) 879-1400 | G | 4 | yes | BLS |
| Lifeflight | (650) 725-4829 | A | 1 | yes | ALS |
| Mid-Peninsula Regional Open | (650) 691-1200 | G | 0 | no | BLS |
| Nasa Ames Fire Department | (650) 604-5416 | G | 0 | no | BLS |
| South Santa Clara Co. Fire Dist | (408) 779-2121 | G | 0 | no | ALS/BLS |
| Santa Clara Co. Fire Department | (408) 378-4010 | G | 0 | no | ALS/BLS |
| Santa Clara County Parks Dept | (408) 358-3741 | G | 0 | no | BLS |
| Santa Clara Co. Sheriff's Dept | (408) 299-2101 | G | 0 | no | BLS |
| Stanford Dept of Public Safety | (650) 725-2149 | G | 0 | no | BLS |
| Sunnyvale Dept of Public Safety | (408) 730-7162 | G | 0 | no | BLS |
| Westmed Ambulance | (510) 614-1423 | G | 11 | yes | ALS/BLS |
| Reach Air Medical Services | (707) 575-6886 | A | 3 | yes | ALS |
| Silicon Valley Ambulance | (408) 225-2212 | G | 7 | yes | ALS/BLS |

#### Santa Cruz County EMS Agency

Agency Contact

Celia Barry, EMS Administrator
1080 Emeline Ave
Santa Cruz, CA 95060
(831) 454-4120

FAX: (831) 454-4272
E-MAIL: celia.barry@health.co.santa-cruz.ca.us

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) Local Govt HEAR Net | 153.935 155.385 | 155.055 155.385 | 131.8 CSQ | Prim Alt |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel Private | 47.66 | 47.66 | 103.5 | Prim |
| Dispatch (for each EMS Agency) Med 3 | 468.050 | 463.050 | 173.8/ 186.2 | Prim |
| Direct to hospitals | N/A | N/A | N/A | N/A |
| Other (e.g. tactical, etc.) Fire-Red | 153.770 | 154.325 | 162.2 | Prim |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Watsonville Community Hospital 				(831) 724-4741

298 Green Valley Road

Watsonville, California 95076

Dominican Santa Cruz Hospital 					(831) 462-7700 					36-59-27.000N/

1555 Soquel Drive 																			121-58-52.000W

Santa Cruz, California 95065 																TLOF - 80' x 80'

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| AMR | (831) 423-7030 | G | 10 | yes | ALS |
| Aptos/La Selva FPD | (831) 685-6690 | G | 0 | no | ALS |
| Central Fire Protection District | (831) 479-6842 | G | 0 | no | ALS |

* Ambulance communication to hospitals : BLS –MED 8

ALS – MED1and MED 4 – varies by location

#### Sierra-Sacramento Valley EMS Agency

Agency Contact

(Nevada, Placer, Sutter, Yolo, Yuba) 
Victoria A. Pinette, MS , EMS Administrator
5995 Pacific St.
Rocklin, CA 95677
(916) 625-1702

FAX: (916) 625-1730
E-MAIL: vickie@ssvems.com

Channel Use												TX-Freq	RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) | N/R | N/R | N/R | N/R |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/R | N/R | N/R | N/R |
| Calling Channel | N/R | N/R | N/R | N/R |
| Dispatch (for each EMS Agency) | N/R | N/R | N/R | N/R |
| Direct to hospitals | N/R | N/R | N/R | N/R |
| Other (e.g. tactical, etc.) | N/R | N/R | N/R | N/R |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Kaiser Roseville	(916) 973-6600

1600 Eureka Road

Roseville, California

Sierra Nevada Memorial Hospital 	(530) 274-6020 	39-14-32.000N/

155 Glasson Way 		121-02-48.000W

Grass Valley, California 95945 		TLOF - 26' x 44'

Tahoe Forest Hospital 	(530) 587-6011 	39-19-27.000N/

10121 Pine Avenue 		120-11-57.000W

Truckee, California 96161 		TLOF – 40’ Diameter

Sutter Roseville Medical Center 	(916) 781-1200 	38-45-58.000N/

One Medical Plaza 		121-14-52.000W

Roseville, California 95661 		TLOF - 46' Diameter

Sutter Auburn Faith Hospital 	(530) 885-7201

11815 education Street

Auburn, California 95604

Sutter Davis Hospital 	(530) 756-6440

Road 99

Davis, California 95616

Woodland Memorial Hospital 	(530) 662-3691

1325 Cottonwood Street

Woodland, California 95695

Rideout Memorial Hospital 	(530) 742-7381

726 Fourth Street

Marysville, California 95901

Sierra Nevada Memorial Hospital 	(916) 274-6020  		39-14-32.000N/

155 Glasson Way 			121-02-48.000W

Grass Valley, California 95945 			TLOF - 26' x 44'

Tahoe Forest Hospital 	(530) 587-6011		39-19-27.000N/

10121 Pine Ave. 			120-11-57.000W

Truckee, California 96161 			TLOF - 40' Diameter

Sutter Roseville Medical Center	(916) 781-1200

333 Sunrise Ave.

Roseville, California 95661

Sutter Auburn Faith Hospital	(916) 885-7201

11815 Education St.

Auburn, California 95603

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (916) 563-0600 | G | 22 | yes | ALS |
| Alpine Meadows | (530) 583-2342 | G | 0 | no | BLS |
| Alta Volunteer Fire Department | (530) 389-2676 | G | 0 | no | BLS |
| Auburn Fire Department | (530) 823-4265 | G | 0 | no | BLS |
| Beale AFB Fire Department | (530) 634-8672 | G | 0 | no | BLS |
| Bi-County Ambulance | (530) 674-2780 | G | 10 | yes | ALS |
| CALSTAR | (530) 887-8259 | A | 4 | yes | ALS |
| CDF - Nevada/Yuba/Placer | (530) 823-4904 | G | 0 | no | BLS |
| CDF- Lake/Napa/Yolo RU | (707) 963-3601 | G | 0 | no | BLS |
| California Highway Patrol | (530) 823-4055 | A | 1 | yes | ALS |
| Camptonville Volunteer Fire Dept | (530) 288-3425 | G | 0 | no | BLS |
| Capay Valley Fire Department | (530) 796-3300 | G | 0 | no | BLS |
| Clarksburg Fire Protection Dist | (530) 744-1700 | G | 0 | no | BLS |
| Colfax Fire Department | (530) 346-2323 | G | 0 | no | BLS |
| Davis Fire Department | (530) 756-3743 | G | 0 | no | BLS |
| Dobbins Oregon House Fire Protection District | (530) 692-2255 | G | 0 | no | BLS |
| Donner Summit Fire Department | (530) 426-3000 | G | 2 | yes | ALS |
| Dry Creek Fire Department | (530) 771-0107 | G | 0 | no | ALS |
| Dunningan Fire Protection Dist | (530) 724-3314 | G | 0 | no | BLS |
| Dutch Flat Fire Department | (530) 389-2287 | G | 0 | no | BLS |
| East Nicolaus Fire Department | (530) 656-2485 | G | 0 | no | BLS |
| Elkhorn Volunteer Fire Dept | (530) 371-4541 | G | 0 | no | BLS |
| Esparto Fire Protection Dist | (530) 787-3300 | G | 0 | no | BLS |
| Foothill Vol. Fire Department | (530) 675-2383 | G | 0 | no | BLS |
| Foresthill Safety Club | (530) 367-2509 | G | 2 | yes | ALS |
| Forty-Niner Fire Protection Dist | (530) 265-4431 | G | 0 | no | BLS |
| Grass Valley Fire Department | (530) 274-4370 | G | 0 | no | BLS |
| Higgins Fire Protection Dist. | (530) 269-2488 | G | 0 | no | BLS |
| Knights Landing Fire Department | (530) 735-6590 | G | 0 | no | BLS |
| Lincoln Fire Department | (916) 645-4040 | G | 0 | no | BLS |
| Linda Fire Department | (530) 743-1553 | G | 0 | no | BLS |
| Live Oak Fire Department | (530) 695-3522 | G | 0 | no | BLS |
| Loma Rica/ Browns Valley CSD | (530) 692-1616 | G | 0 | no | BLS |
| Loomis Fire Protection District | (916) 652-6858 | G | 0 | no | BLS |
| Madison Fire Protection District | (530) 662-5745 | G | 0 | no | BLS |
| Marysville Fire Department | (530) 741-6622 | G | 0 | no | BLS |
| Meridian Fire Department | (530) 696-2306 | G | 0 | no | BLS |
| Nevada City Fire Department | (530) 265-2351 | G | 0 | no | BLS |
| Nevada Co. Cons. Fire | (530) 273-3158 | G | 0 | no | BLS |
| Newcastle Fire Protection Dist | (530) 663-3323 | G | 0 | no | BLS |
| North San Juan Fire Protection Dist. | (530) 292-9159 | G | 0 | no | BLS |
| North Tahoe Fire Protection Dist | (530) 583-6913 | G | 7 | yes | ALS |
| Northstar Fire Department | (530) 562-1212 | G | 0 | no | BLS |
| Olivehurst PUD | (530) 743-7117 | G | 0 | no | BLS |
| Ophir Hill Fire Protection Dist | (916) 273-8351 | G | 0 | no | BLS |
| Oswald-Tudor | (916) 673-2804 | G | 0 | no | BLS |
| Peardale-Chicago Park Fire Protection District | (530) 273-2503 | G | 0 | no | BLS |
| Penryn Fire Protection District | (530) 663-3389 | G | 0 | no | BLS |
| Placer Co. Fire Department | (530) 823-4904 | G | 0 | no | BLS |
| Placer Foothills Cons. Fire Protection District | (530) 889-7991 | G | 0 | no | BLS |
| Placer Hills Fire Department | (530) 878-0405 | G | 0 | no | ALS |
| Pleasant Grove Fire Department | (530) 655-3937 | G | 0 | no | BLS |
| Plumas-Brophy Fire Protection District | (530) 633-2727 | G | 0 | no | BLS |
| REACH | (707) 447-6886 | A | 2 | yes | ALS |
| Rocklin Fire Department | (916) 632-4150 | G | 0 | no | BLS |
| Rough & Ready Fire Protection District | (530) 432-1140 | G | 0 | no | BLS |
| Sierra NV Memorial Hospital Ambulance | (530) 274-6000 | G | 7 | yes | ALS |
| Smartville Fire Protection Dist | (800) 540-2008 | G | 0 | no | BLS |
| South Placer Fire | (916) 791-7059 | G | 3 | yes | ALS |
| Squaw Valley Fire Department | (530) 583-6111 | G | 0 | no | BLS |
| Sutter Basin Fire Protection Dist | (530) 738-4220 | G | 0 | no | BLS |
| Sutter CDF | (530) 741-7370 | G | 0 | no | BLS |
| Sutter Fire Department | (530) 755-0266 | G | 0 | no | BLS |
| Truckee Fire | (530) 582-7850 | G | 4 | yes | ALS |
| U.S. Forest Service | (530) 288-3231 | G | 0 | no | BLS |
| U.S.Forest Service | (530) 367-2224 | G | 0 | no | BLS |
| U.S.F.S.Tahoe National Forest | (530) 478-6221 | G | 0 | no | BLS |
| U.S.F.S.Truckee Ranger District | (530) 587-3558 | G | 0 | no | BLS |
| UC Davis Fire Department | (530) 752-1236 | G | 0 | no | BLS |
| Walton Fire Department | (530) 673-7833 | G | 0 | no | BLS |
| Watt Park Fire Protection Dist | (530) 273-8088 | G | 0 | no | BLS |
| West Plainfield Fire Protection District | (530) 756-0212 | G | 0 | no | BLS |
| West Sacramento Fire Dept | (530) 373-5840 | G | 0 | no | BLS |
| Wheatland Fire Department | (530) 633-2930 | G | 0 | no | BLS |
| Willow Oak Fire Protection Dist | (530) 662-0781 | G | 0 | no | BLS |
| Winters Fire Department | (530) 795-4131 | G | 1 | yes | BLS |
| Woodland Fire Department | (530) 661-5844 | G | 0 | no | BLS |
| Yolo Fire Protection District | (530) 662-8808 | G | 0 | no | BLS |
| Yuba City Fire Department | (530) 741-4691 | G | 0 | no | BLS |
| Zamora Fire Protection District | (530) 662-6883 | G | 0 | no | BLS |

#### Solano County EMS Agency

Agency Contact

Michael Frenn, EMS Administrator
275 Beck Ave., 2nd Fl., MS5-240
Fairfield, CA 94533
(707) 784-8155
FAX: (707) 421-6682
E-MAIL: mfrenn@solanocounty.com

Channel Use	TX-Freq	RX-Freq	CTCSS		Prim/Alt

| Local Medical Coordination (real time) | N/R | N/R | N/R | N/R |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/R | N/R | N/R | N/R |
| Calling Channel | N/R | N/R | N/R | N/R |
| Dispatch (for each EMS Agency) | N/R | N/R | N/R | N/R |
| Direct to hospitals | N/R | N/R | N/R | N/R |
| Other (e.g. tactical, etc.) | N/R | N/R | N/R | N/R |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Kaiser/Vallejo											(707) 651-4910 (A Side)

975 Sereno Dr.										(707) 651-4920 (B Side)
Vallejo, CA 94589

NorthBay Medical Center							(707) 429-7830					38-15-41.000N/
1200 B. Gale Wilson Blvd.																122-02-50.000W
Fairfield, CA 94533																			TLOF - 40' x 40'

Sutter Solano Medical Center						(707) 554-5210					38-07-55.000N/

300 Hospital Dr.																				122-14-09.000W
Vallejo, CA 94589																			TLOF - 40' x 40'

VacaValley Hospital									(707) 446-5710					38-21-21.000N/

1000 Nut Tree Blvd.																			121-57-91.000W
Vacaville, CA 95688																		TLOF - 40' Diameter

David Grant Medical Center						(707) 423-3825

DGMC/SGHE
101 Bodin Cir
Travis AFB, CA 94535-1800

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| Benicia Fire Department | 707-746-4275 | G | 0 | no | ALS |
| Cordelia Fire Department | 707-864-0468 | G | 0 | no | ALS |
| Dixon Fire Department | 707-678-7060 | G | 0 | no | ALS |
| Fairfield Fire Department | 707-436-7222 | G | 0 | no | ALS |
| Isleton Fire Department | 916-777-7776 | G | 0 | no | BLS |
| Medic Ambulance | 707-644-1761 | G | 15 | yes | ALS |
| Montezuma/Ryer Island Fire Protection District | 707-374-5962 | G | 0 | no | BLS |
| Rio Vista Fire Department | 707-374-2233 | G | 0 | no | ALS |
| River Delta Fire Department | 916-777-8700 | G | 0 | no | BLS |
| Suisun Fire Dept | 707-425-9133 | G | 0 | no | BLS |
| Suisun Fire Protection District | 707-425-3605 | G | 0 | no | BLS |
| Vacaville Fire Department | 707-449-5468 | G | 4 | yes | ALS |
| Vacaville Fire Protection District | 707-447-2252 | G | 0 | no | BLS |
| Vallejo Fire Department | 707-648-4526 | G | 0 | no | ALS |

#### Tuolumne County EMS Agency

Agency Contact

Clarence Teem, EMS Coordinator
20111 Cedar Road North
Sonora, CA 95370
(209) 533-7460

FAX: (209) 533-7406
E-MAIL: cteem@co.tuolumne.ca.us

Channel Use											TX-Freq		RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) | N/A | N/A | N/A | N/A |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | 155.295 | 155.295 | N/A | N/A |
| Calling Channel | 155.295 | 155.295 | 110.9 | N/A |
| Dispatch (for each EMS Agency) | 462.250 | 467.250 | N/A | N/A |
| Direct to hospitals | 462.400 | 462.400 | N/A | N/A |
| Other (e.g. tactical, etc.) | N/A | N/A | N/A | N/A |

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Sonora Regional Medical Center					 (209) 532-5000 					37-58.40/120-22.15

1000 Greenley Road 								 (209) 536-3436

Sonora, California 95370

Helispot Location						Latitude/Longitude				Description of Location

Bald Mountain	38-08.4/120-05.65	CDF Base: 123.025 VHF

Brightman Dump	38-21.37/119-52.26	Normally up canyon winds

Buck Meadows	37-49.06/120-06.00	So. Edge of pad slopes steeply off

Cherry Lake Dam	37-58.00/119-54.50

Chinese Camp Fire	37-52.40/120-26.20

Columbia Airport

Don Pedro Dam	37-41.94/120-25.74

Keystone Bark & Mulch Plant	37-50.30/120-30.60

Moccasin Point	37-48.97/120-18.15	On Lake Don Pedro along

Highway 120, Bottom of Priest Grade - 120, next to power station – Caution:  Many Wires

Outpost	37-59.87/120-16.09	Field NE corner of intersection of

Highway 108 & Soulsby Road

behind mini-mart.

Poker Flat	37-52.54/120-34.56

Sonora Fair Grounds	37-58.00/120-24.00

Tuttletown Boat Ramp	37-58.83/120-30.92

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| Tuolumne Co. Ambulance | (209) 533-5815 (Dispatch) (209) 533-5100 (Admin.) | G | 10 | yes | ALS |

#### Ventura County EMS Agency

Agency Contact

Barry Fisher, EMS Administrator
2220 E. Gonzalez Rd., Ste. 130
Oxnard, CA 93036-0619
(805) 981-5308

FAX: (805) 981-5300
E-MAIL: Barry.Fisher@ventura.org

Channel Use											TX-Freq		RX-Freq		CTCSS		Prim/Alt

| Local Medical Coordination (real time) Cellular Phone | 155.205 N/A | 155.205 N/A | 103.5 N/A | Alternate Primary |
| --- | --- | --- | --- | --- |
| Statewide Medical Coordination | N/A | N/A | N/A | N/A |
| Calling Channel | N/A | N/A | N/A | N/A |
| Dispatch (for each EMS Agency) Ventura County Fire Oxnard Fire Department | 154.010 156.210 | 154.010 154.145 | 100.0 141.3 | Primary Primary |
| Direct to hospitals VCMC, SVH, SJPVH, OVCH LRHMC, SJRMC, SPMH, CMH | 155.355 155.385 | 155.355 155.385 | 103.5 103.5 | Primary Primary |
| Other (e.g. tactical, etc.) 12 Designated SEMS channels for disasters | N/A | N/A | N/A | N/A |

These frequencies are composed of the departmental frequencies of 12 County Departments.

Helipad

Emergency Department Facilities				Telephone							Latitude/Longitude

Community Memorial Hospital 					(805) 652-5011 					34-16-29.000N/

Loma Vista & Brent 																		119-15-25.000W

Ventura, California 93003 																	TLOF - 64' x 66'

Los Robles Hospital and Medical Ctr 			(805) 497-2727					34-12-28.000N/

215 W. Janss Road																			118-52-54.000W

Thousand Oaks, CA 91360																TLOF - 50' x 50'

Ojai Valley Community Hospital 				(805) 646-1401

1306 Maricopa Highway

Ojai, California 93023

Simi Valley Hospital and Health Care Ctr 	(805) 955-6000 					34-17-22.000N/

2975 N. Sycamore Drive 																	118-44-38.000W

Simi Valley, California 93062 															TLOF - 50' Diameter.

St. John’s Pleasant Valley Hospital 				(805) 389-5800

2309 Antonio Avenue

Camarillo, California 93010

St. John’s Regional Medical Center 			(805) 988-2500 					34-13-00.000N/

1600 North Rose Avenue 																	119-09-25.000W

Oxnard, California 93030 																	TLOF - 60' Diameter.

Ventura County Medical Center 					(805) 652-6000 					34-16-40.000N/

3291 Loma Vista Road 																		119-15-05.000W

Ventura, California 93003 																	TLOF - 41' x 41'

VCMC Santa Paula Hospital 						(805) 525-7171

825 North 10th Street

Santa Paula, Ca 93060

Helispot Location						Latitude/Longitude					Description of Location

NONE

VEHICLE CHARACTERISTICS

| Emergency Providers | Telephone | TYPE | AMB’s | TRANS | EMT |
| --- | --- | --- | --- | --- | --- |
| American Medical Response | (805) 517-2000 | G | 28 | yes | ALS |
| Gold Coast Ambulance | (805) 485-3040 | G | 22 | yes | ALS |
| Lifeline Medical Transport | (805) 653-9111 | G | 5 | yes | ALS |
| Ventura County Sheriff Search/Rescue | (805) 388-4212 | A | 3 | yes | ALS |
| Fillmore Fire Department | (805) 524-1500 | G | 0 | no | ALS |
| Oxnard Fire Department | (805) 385-7722 | G | 0 | no | BLS |
| Santa Paula Fire Department | (805) 525-4478 | G | 0 | no | BLS |
| Ventura City Fire Department | (805) 339-4300 | G | 0 | no | ALS |
| Ventura Co. Fire Protection Dist | (805) 389-9710 | G | 0 | no | ALS |
| Ventura Co. Federal Fire Dept. | (805) 989-7034 | G | 0 | no | BLS |

GENERAL ACRONYMS FOR EMS COMMUNICATIONS

A

AA—above average terrain

AC—alternating current

ACD—automatic call distributor

ACLS—advanced cardiac life support

ACSB—amplitude compandored single-sideband

ADP—automatic data processing

AGL—above ground level

ALS—advanced life support

ALERT—automatic law enforcement response team

ALI—automatic location identification

AM—amplitude modulation

AMSL—above mean sea level

ANI—automatic number identification

APB—all points bulletin

APCO—Associated Public-Safety Communications Officers

ASCII—American Standard Code for Information Interchange

ASTM—American Society for Testing and Materials.

ASTRA—Automated Statewide Telecommunications And Records Access

ATLS—Advanced Trauma Life Support

AT&T—American Telephone and Telegraph Company

AVC—automatic volume control

AVI—automatic vehicle identifications

B

balun—balanced-to-unbalanced line transformer

BCD—binary coded decimal

BFO—beat frequency oscillator

BIT—binary digit

BLS—basic life support

BPS—bits per second.

BSC—binary synchronous communications

C

C—Celsius

CAD—computer –aided Dispatch

CB—citizens band

CCH—computerized criminal history

CCITT—International Telegraph And Telephone Consultative Committee

CCSA—common control switching arrangement

CCTV—closed circuit television

CCU—Coronary Care Unit or Critical Care Unit

CDC—Cooperative Dispatch Center

CG—Channel Guard(R) Trademark of General Electric

CMED—Central Medical Emergency Dispatch

CMR—Common Mode Rejection

CMRR—Common Mode Rejection Radio

CNIL—Calling Number Identification and Location

CO—Central Office

COG—Council of Governments

COR—Coronary Observation Radio

CPR—cardiopulmonary resuscitation

CJIS—Criminal Justice Information System

CTCSS—Continuous Tone Controlled Squelch System

D

dB—decibel

dBm—decibel reference to 1 mW.

dBu—decibel referenced to 1 mV/m

dBv—decibel referenced to 1 V

dBW—decibel referenced to 1 W

DC—direct current

DCS—Division of Computer Services

DDD—direct distance dialing

DID—direct inward dialing

dod—direct outward dialing

DOD —US Department of Defense

DOT—US Department of Transportation

DRG—diagnosis related grouping

DP—double pole

DPDT—double pole double throw

DTMF—dual-tone multi-frequency

DPST—double pole single throw

E

EACOM—emergency and administrative communications system

EAS—extended area service

E & M-–the receive and transmit leads of a signaling system

EAX—electronic automatic exchange

ECC—emergency communications center

EDP—electronic data processing

EIA—Electronic Industries Association

EMD—emergency medical dispatcher

EMF—electromotive force

EKG—electrocardiogram

EMDPRS—emergency medical dispatch priority reference system

EMS—emergency medical service

EMSS—emergency medical service system

EMT—emergency medical technician

EMT-B—emergency medical technician-basic

EMT-D—emergency medical technician-defibrillator

EMT-I—emergency medical technician-intermediate

EMT-P—emergency medical technician-paramedic

EOC—emergency operations center

EOM—end of message

ERCC—emergency resource coordination center

ERP—effective radiated power

ESS—electronic switching system

EST—Eastern Standard Time

ETA—Estimated Time of Arrival

ETV—Educational Television

F

F—Fahrenheit

FCC—US Federal Communications Commission

FCCA—Forestry Conservation Communications Association

FEMA—Federal Emergency Management Agency

FET—field-effect transistor

FM—frequency modulation

Freq.—frequency

FORTRAN —formula translation (computer language)

FSK—frequency-shift keying

FX—foreign exchange

G

GE—General Electric

GESS—General Electric Service Station

GFW—ground fault warning

GHZ—gigahertz (1000 MHz)

GIGO—garbage in, garbage out

GMT—Greenwich Mean Time (Zulu)

GSA—General Services Administration

GT&E—General Telephone and Electronics

H

HEAT—hospital emergency administrative radio

HF—high frequency

HYSIS—highway safety information system

HV—high voltage

Hz—hertz

I

I—current in amperes

IAFC—International Association of Fire Chiefs

IACP—International Association of Chiefs of Police

IC—integrated circuit

ICO—individual channel oscillator

ICOM—integrated circuit oscillator module

ICU—intensive care unit

ICX—intercity exchange link

IEEE—Institute of Electrical and Electronic Engineers

IF—intermediate frequency

IMSA—International Municipal Signal Association

IMTS—improved mobile telephone service

IRAC—Interdepartmental Radio Advisory Committee

ISPERN—Illinois State Police Emergency Radio Network

IT&T—International Telephone and

Telegraph Corporation

ITU—International Telecommunication Union

J

JAN—Joint Army-Navy Specifications

JETEC—Joint Electron Tube Engineering Council

JFET—junction field-effect transistor

UPS—uninterruptible power supply

USIT—US Independent Telephone Association

USFS—US Forest Service

Journal of Emergency Medical Services

K

UPS—uninterruptible power supply

USIT—US Independent Telephone Association

USFS—US Forest Service

kbps—kilobits per second

kHz—kilohertz (1000hertz)

L

LATA—local access transport area

LMR—land mobile radio

LEAA—Law Enforcement Assistance Administration

LETS—Law Enforcement Teletypewriter Service

LORAN—long range navigation

LSI—large scale integration

LOS—line of sight

LRO—lead regional organization

LSU—life support unit

M

MAST—Military Assistance to Safety and Traffic

MCCU—mobile coronary care unit

MF—medium frequency

MHz—Megahertz

MICT—Mobile Intensive Care Technician

MICU —Mobile Intensive Care Unit

MRCC—Medical Resource Coordination Center

N

NABER—National Association of Business and E Radio, Inc.

NCIC—National Crime Information Center

NCMCN —North Carolina Medical Communications Network

NEAR—national emergency aid radio

NHTSA—National Highway Traffic Safety Administration

NLETS—national law enforcement telecommunications system

NPA—Number Plan Area

O

O-D—origin-destination

ONI—operator number identification

OTP—Office of Telecommunications Policy

P

UPS—uninterruptible power supply

USIT—US Independent Telephone Association

USFS—US Forest Service

PABX—Private Automatic Branch Exchange

PBX—Private Branch Exchange

PL—Private Line(r) Trademark of Motorola

PM—Pulse Modulation

PSAP—public safety answering point

PSCC—Public Safety Communications Council

PTT—Press to Transmit or Push to Talk

Q

QEI—quantifiable evaluation indicator

R

RCU—remote control unit

RF—radio frequency

Rx—receive

S

SERS-Special Emergency Radio Service

SIRSA—Special Industrial Radio Service Association

SMR—Specialized Mobile Radio

SMSA—standard metropolitan statistical area

SPA—State Planning Agency

SWR—Standing Wave Radio

T

TASI—time assignment speech

interpolation

TCAM—telecommunications access method

TLOF – Touchdown Liftoff Area

Telco—telephone company

TPL—terminal per line

TPS—terminal per station

Tx—transmit

U

UHF—ultra high frequency

UL—Underwriters Laboratories, Inc.

UPS—uninterruptible power supply

USIT—US Independent Telephone Association

USFS—US Forest Service

V

V—volts

VAC—volts, alternating current

VDC—volts, direct current

VHF—very high frequency

VOM—volt-ohm meter

VOR—voice operated relay

VOX—voice operated switch

VSWR—voltage standing wave ratio

VTVM—vacuum tube voltmeter

VU—Volume Unit

W

WATS—Wide Area Telephone Service

WECO—Western Electric Company

WPM—words per minute

X

Xcvr.—transceiver

Xfmr.—transformer

Xmit.—transmit

Xmtr—transmitter

Xtal—crystal

Z

Z—impedance

ZULU —time zone at Greenwich, England

# FCC CODES AND NAMES OF RADIO SERVICES

industrial:

IB—business

IF—forest products

IM—motion picture

IP—petroleum

IS—special industrial

IT—telephone maintenance

IW—power

IX—manufacturers

IY—relay press

Motor Carrier:

LI—interurban passenger

LJ—interurban property

LU—interurban passenger

LV—urban property

Land Transportation:

LA—automobile emergency

LR—railroad

LX—taxicab

Public Safety:

PF—fire

PH—highway maintenance

PL—local government

PP—police

PO—forestry conservation

PS—special emergency

RS—radio location

ZA—general mobile

Classes of Radio Stations (FCC):

FB—base

FB2—mobile relay

FB4—community repeater

FX1—control

MO—mobile

MO3—mobile/vehicular repeater

FXO—operational fixed

FX2—fixed relay

FX—fixed

FLT—auxiliary test

FXY—interzone

FXZ—zone

LR—radio location

MR—radio location mobile

806-821/851-866 MHz Bands:

Conventional              Category     Trunked

GB     business                                        YB

GO    industrial/land transportation        YO

GP     public safety/special emergency   YP

GX     commercial (SMRS)                    YX

292-930 MHz Band:

GS—private carrier paging systems

# GLOSSARY

A

acoustic feedback—The transfer of sound waves from a loud speaker or end terminal to any previous component within an audio system.

activity—The expenditure of time and resources.

adapter—A device used for changing the terminal connections of a circuit or part to connect to another circuit or part with unlike connections.

alphabet, phonetic—A method of passing alphabetic information substitution over a poor communication path with word substitution for letters. One phonetic alphabet is: Alfa, Bravo, Charlie, Delta,

Echo, Foxtrot, Golf, Hotel, India, Juliett, Kilo, Lima, Mike, November, Oscar, Papa, Quebec, Romeo, Sierra, Tango Uniform, Victor, Whiskey, X-ray, Yankee, Zulu.

American Standard Code for Information Interchange (ASCII)—An eight-level code for data transfer adopted by the American Standards Association to achieve compatibility between data devices.

amplitude compandored single-sideband—A form of sideband modulation used for narrow channel transmission that

incorporates a pilot tone.

amplitude modulation(AM)—Modulation in which the amplitude of the carrier-frequency current is varied above and below its normal value in accordance with the audio, picture, or other intelligence signal to be transmitted.

analog—Physical representation of information such that the representation bears an exact relationship to the original information. Pertaining to data in the form of continuously variable physical qualities

analog communication—System of telecommunications used to transmit information other than voice which

is sometimes used in telemetry.

antenna—A system of wires or electrical conductors employed for reception or transmission of radio waves. Specifically, a radiator that couples the transmission line or lead-in to space for transmission or

receptions of electromagnetic radio waves. It

changes electrical currents into

electromagnetic radio waves and vice versa.

antenna, isotropic—A theoretical antenna with identical radiation in every direction.

antenna, parabolic—A directional antenna with a radiating(or receiving) element, and a parabolic reflector that concentrates the power in a beam.

antenna polarization—The direction of the radiated electrical field in relation to the surface of the earth. Generally vertical in mobile radio use.

arc—A discharge of electricity.

arrester, lightning—A device designed to protect electrical equipment or property from damage by lightening.

assigned frequency—The frequency appearing on a station authorization from which the carrier frequency may deviate by an amount not to exceed that permitted by the frequency tolerance.

Associated Public-Safety Communications Officers (APCO)—A non-profit public safety radio users group composed of administrators and communications technical, operations, and command personnel.

ASTM—A scientific and technical organization formed for the development of standards on characteristics and performance of materials, products, systems, and services.

attack time—The interval required after a sudden increase in input signal to a transducer (transmitter, receiver, etc.) to attain a percentage of final output level due

to this increase.

attenuation—The decrease in amplitude of a signal during its transmission from one point to another. It may be expressed as a ratio or, by extension of the term, in decibels.

attenuator—A device for reducing the energy of a wave without introducing distortion. Also called a pad, gain control, level adjustor, volume control, etc.

audible signal—A buzzer, bell, or other audible sound device that indicates an incoming call.

audio—Pertaining to frequencies corresponding to normally audible sound waves. These frequencies range from 15 to 20,000 Hz.

aural—Pertaining to the ear or sound.

automatic gain control (AGC)—A receiver circuit that maintains the output constant with wide variations in the in the receiver input level.

automatic volume control (AVC)—A self-acting gain control which maintains the output of a receiver constant despite variations in received signal strength.

automatic number identification (ANI)—Equipment for recording the calling party’s number without operator intervention.

B

back bone—A point-to-point

communications system utilizing several stations.

back-to-back repeater—A repeater consisting of a receiver and transmitter with the output of the receiver connected directly to the input of the transmitter.

band (radio frequency)—A range of frequencies between two definite limits. By international agreement, the radio spectrum is divided into nine bands. For example, the very high frequency (VHF) band

extends from 30 MHz to 300 MHz.

bandpass filter—Passes frequencies within a specified band, and attenuates all frequencies outside that band.

bandwith—(1) The width of a band of frequencies used for a particular purpose, (2) the range of frequencies within which a performance characteristic of a device is above specified limits. For filters, attenuators, and amplifiers these limits are generally taken to be 3 dB (half-power) below the average level.

baseband—For microwave systems, the available frequency band that the RF equipment is capable of transmitting.

base station—An item of fixed radio hardware consisting of a transmitter and receiver.

baud—Used to define the operating speed of a printing telegraph of data system. It is

the total number of discrete conditions or signal events per second.

baudot code—A five-unit code used for teletypewriter signals.

beacon—A radio transmitter or lights designed to indicate exact geographical location or direction.

beam—A configuration of radiated energy whose rays are sharply directional and parallel.

beat—A regularly recurring pulsation from the combination of two-tone or frequency waves of different frequencies.

beat frequency—the frequency produced when signals of two different frequencies are combined and refracted. The beat frequency is equal in value to the difference between the original frequencies.

bel—A unit of relative power, named after Alexander Graham Bell, and used to express differences in power.

beeper—a pocket paging receiver that emits a beeping sound upon receiving a page specifically directed to it.

biomedical telemetry (biotelemetry)—The technique of monitoring or measuring vital biological parameters and transmitting data to a receiving point at a remote location.

Biophone—Trade name of Biocom, Inc. for portable telemetry devices.

bit—A unit of digital information (abbreviation of “binary digit”).

boom microphone—A microphone arranged on an arm type mechanical support to permit better placement of the microphone.

braid—A group of fibrous or metal filaments or threads woven into a cylindrical shape to form a covering over one or more wires.

broadcast—Radio or television transmission intended for general reception.

Business Radio Service—A subpart of the Industrial Radio Services section of the FCC rules.

busy indicator—An indicator provided at a control point to indicate the in-use condition of a circuit or channel.

C

cable—One or more insulated or noninsulated wires used to conduct electrical current or impulses. Grouped insulated wires are called a multi-conductor cable.

calibrate—To determine error by

comparison with a known standard.

call, all—The alerting of all decoder equipped units in a system by the transmission of a single coded signal.

call, group—The alerting of subdivided selective call groups by function, type of vehicle, location, etc. by sending a single coded signal.

call, individual—The alerting of a specific coded decoder unit by sending a single coded signal.

call answer—The initial answer of a call for assistance whether by 9-1-1 or other telephone method.

call sign—Federal Communications Commission assigned identifying letters and numbers used for identification of a radio station, transmitter, or transmission.

call referral method—The calling party is referred to a secondary number

call relay method—The call is answered at the PSAP where the pertinent information is gathered and then the interrogator relays the information to the proper public safety agency for their action. This can be accomplished by radio, intercom, telephone,

etc.

call transfer method—The PSAP

interrogator determines the proper responding agency and connects the user

to that agency which then performs the

necessary dispatching in accordance with prearranged plans with cooperating agencies.

call party hold—Enables the public safety answering point to control the connection for confirmation and tracing of a call.

capture effect—An effect occurring in FM reception when the stronger of two signals on the same frequency suppresses the weaker signal.

cardioid microphone—A microphone having a heart-shaped space response pattern of 180° in front, and

minimum response in the rear.

carrier—A radio signal generally without voice or other information.

carrier control timer (CCT)—A device that limits the length of time that the transmitter carrier is on.

carrier frequency—The frequency of an unmodulated electromagnetic wave produced by the transmitter.

cavity resonator—A space enclosed by a metal conductor in which oscillating electromagnetic energy is stored and whose resonant frequency is determined by the

geometry of the enclosure.

cellular radio—A commercially available mobile or portable radio telephone service.

Celsius—The metric scale of temperature in which water freezes at zero degrees and boils at 100°C. To convert a Celsius

temperature to Fahrenheit, multiply by 9/5 and add 32.

central medical emergency dispatch(CMED)—See command and control center.

central office—Sometimes called a wire center; the smallest subdivision within the telephone system which has relatively permanent geographic boundaries.

change out—To replace.

channel element—A temperature compensated crystal oscillator

channel guard—General Electric’s trademark for continuous tone coded squelch system (CTCSS).

channel, point-to-point—A radio channel used for radio communications between two definite fixed stations.

channel, radio—An assigned band of radio frequencies of sufficient width to permit its use for radio communication. The necessary width of a channel depends on the type of transmission and the tolerance for the frequency of emission.

channel, television—A band of radio frequencies 6 MHz wide used for television broadcast

channelization—The assignment of circuits to channels, and the arrangement of those channels into groups.

charge—To replenish the electrical potential in a battery or capacitor.

charge, fast or quick—A method of quickly recharging batteries under controlled conditions.

charge, trickle—The continuous charge of a battery at a slow rate.

chart, 4/3 earth’s radius—A radio profile chart whose horizontal lines are curved to correspond to an earth having a radius 4/3 times larger than actual earth radius.

chassis—The framework on which parts of a radio or other electronic circuits are mounted.

circuit merit—A rating of overall circuit quality. Circuit merit ‘5” is clear circuit. Merit ‘3’ is readable with noise. Any rating below ‘3’ is not readable and generally unacceptable.

class of service—Service order code designation of the combination of telephone service features (equipment, calling area units, dial types) to which business and residence customers subscribe. It is

used for rating, identification, and assignment purposes.

coaxial cable—A transmission line in which one conductor completely surrounds the other, the two being coaxial and separated by a continuos solid dielectric or by dielectric spacers.

code dialing—A method of signaling or encoding and decoding address codes by the use of standard telephone dial.

command and control center (central communications center)—A system which is responsible for establishing communications channels and identifying the necessary equipment and facilities to permit immediate management and control of an EMS patient. This operation must provide access and availability to public safety resources essential to the effective and efficient EMS management of the immediate EMS problem.

common mode rejection (CMR)—The ability of differential amplifier to reject unwanted signals.

communications subsystem—Comprises those resources and arrangements for notifying the EMS system of an emergency, for mobilizing and dispatching resources, for exchanging information, for remote monitoring of vital indicators, and for the radio transmission of treatment procedures and directions.

communications system—a collection of individual communication networks, transmission system, relay stations, control and base stations, capable of interconnection and inter-operations that are designed to form an integral whole. The individual

components must serve a common purpose, be technically compatible, employ common

procedures, respond to control and operate in unison.

comparator—A circuit which compares tow or more signals, and selects the strongest or best.

compression—In audio systems, reducing the volume range of the input signal so that the minimum output has less noise, and the maximum output has less distortion.

compressor—A variable gain audio device used to provide a relatively constant output level for a wide range of varying input levels.

cone of silence—The area directly over or under a vertical transmitting antenna in which little or no signal is radiated.

console—A cabinet housing electronic circuitry normally used in controlling other equipment such s transmitters and receivers installed at a remote location.

consolette—(1) Motorola Communications name for a desk top radio station (2) A device for mounting a mobile microphone, control head and speaker.

continuous tone controlled squelch system (CTCSS)—A system wherein radio receiver(s) are equipped with a tone responsive device which allows audio signals to appear at the receiver audio output only when a carrier modulated with a specific tone is received. The tone must be continuously present for continuous audio output. CTCSS functions are sometimes referred to by various trade names such

as private line or PL(Motorola

Communications & Electronics), Channel Guard or CG(General Electric Mobile Radio) or Quiet Channel (RCA).

control console—A desk-mounted, enclosed piece of equipment which contains a number of controls or circuits used to operate a radio station.

control head—A device with appropriate controls, microphone, volume, squelch, on/off, etc., generally mounted in a vehicle, from which control of the radio or mobile unit is performed.

control point—A position from which a radio system is controlled and supervised.

control, remote—A control scheme for a radio system where all control functions are performed remotely via telephone lines.

continuous duty—(1) An unending transmission (2) Operating 100% of the time (3) EIA—full load output under the manufacturers normal loading conditions for the class of service for 24 hours.

control, local—A control system packaged with the control unit mounted directly on the base station.

coordination, frequency—The cooperative selection and allocation of radio frequencies such that all systems can operate with minimum interference.

couple—To connect two circuits so that signals are transferred from one to the other.

coverage—In a radio communications system, the geographic area where reliable communications exist; usually expressed in terms of miles extending radially from a fixed radio station.

crosstalk—The unwanted transfer of energy from one communication circuit to another by means of a mutual coupling.

crystal—A piece of quartz or similar material that has been ground thin and to the proper size to produce vibrations at the desired frequency. Used in radio

transmission to generate, with a high degree of accuracy, the assigned carrier frequency of a station.

cut over—To transfer from one system to another.

cycle—One complete reversal of an alternating current, including a rise to the maximum level in one direction and a return to zero. The number of cycles occurring in one second is the frequency of the current. The word cycle is commonly used to

mean cycles per second (hertz).

D

dBm—Decibels referenced to one milliwatt. Employed in communication work as a measure of absolute power. Zero dBm equals one milliwatt.

dBV—Decibels referenced to 1 V.

dBW—Decibels relative to 1 W (1 dBw = 30 dBm).

decibel (dB)—A unit which expresses the level of power value relative to a reference power value. Specifically, the level of power, value P, relative to a reference value, PR, in decibels is defined as dB = 10*log10(P/PR).

DC control—A remote base station control scheme that requires metallic conductors and currents

decoding—The conversion and recognition by the addressed (receiving) unit of numerical address codes that have been transmitted through a communications system.

dedicated telephone line—A telephone wire pair, originating at one point, and terminating at another point, operating in a closed circuit. Also called private line.

defibrillator—An electrical device used to eliminate fibrillation of the heart muscle, by the application of high voltage impulses.

demodulation—The process of recovering the modulating information from a modulated signal.

deviation ratio—The ratio of the maximum frequency deviation of the RF carrier to the highest frequency contained in the modulating band.

dial tone first—Allowance of a 9-1-1 or ‘0’ operator calls to be completed without the deposit of a coin in a telephone pay station.

digital—Data represented in discrete, discontinuous form, as contrasted with analog data represented in continuous form.

digital dial code—A signaling technique generally used in VHF radio systems to bypass a receiver CTCSS system

diplexer—A device which enables the use of two radio transmitters, operating on different frequencies, on the same antenna simultaneously.

direct—In terms of communications circuits, means a dedicated instant method of communications. A dial telephone is not direct, a radio or a ring down line are direct.

direct dispatch method—A system where all 9-1-1 call answering and radio dispatching is performed by the personnel at the public safety answering point.

direct distance dialing(DDD)—Telephone service which permits subscribers to dial their own long distance calls.

direct leased land lines—Dedicated or designated point-to-point wire circuits telephone) used in transmitting voice or data communications. See dedicated telephone line.

direct trunking—An arrangement where a telephone line connection has no intermediate points before reaching the final destination (called) party.

directional antenna—An antenna which radiates radio waves more effectively in some directions than in others.

directivity—The value of the direction gain of an antenna in the direction of its maximum value.

dish—A type of antenna. A parabolic reflector used in microwave systems.

dispatch point—A position from which a radio system is used but not a supervision or control point. Dispatch points are not usually listed on a station radio license.

distortion—Unfaithful reproduction of audio or video signals due to change occurring in the wave form of the original signal, somewhere in the course of its transmission or reception. The lower the percentage

of distortion, the more distortion free the system is and the more intelligible the message.

diversity—A method of radio transmission, or reception, or both, which counteracts the effects of fading by combining several signals all bearing the same information.

doctor-interrupt—The ability of a physician or hospital-based communicator to interrupt the voice or telemetry transmission from a radio in the field.

dual-tone multi-frequency (DTMF)—The simultaneous generation of two audio tones generally compatible to AT&T’s standard “touch-tone” frequencies. Used for control or signaling purposes. A method of

sending specific pairs of audio tones for each digit, up to a total of 16.

duplex—The operation of transmitting and receiving apparatus at one location in conjunction with associated transmitting and receiving apparatus at another location: the process of transmission and reception being simultaneous. The simultaneous

transmission and reception of information. A

duplexed piece of equipment is capable of

transmitting and receiving simultaneously. Duplex systems generally employ different transmitting and receiving frequencies.

duplexed operation—The operation of associated transmitting and receiving apparatus concurrently as in ordinary telephones without manual switching

between talking and listening periods. For

comparison see simplex operation.

duplexed/multiplexed telemetry unit—A radio device capable of simultaneous transmission and reception and concurrent transmission of both voice and EKG

information.

duplexer—A device which is used in radio equipment to provide simultaneous transmit and receive capabilities on a single antenna.

duplex, half—A system in which communication may be in either direction but only one way at a time. Transmission in one direction at a time over a single channel.

E

E & M signaling—An arrangement by which signaling between two points on a radio or carrier path is accomplished. An M lead is associated with the transmit (or mouth) while the E lead is associated

with the receiver (or ear).

EACOM—Emergency and Administrative Communications for hospitals. Trade name for VHF radio system operating on standard frequencies with a selective calling system between stations. The system is similar to Motorola Communications HEAR radio system.

effective height—The true electrical height of an antenna corresponding to a “perfect” antenna that will produce the same field strength. The height of its center of radiation above the effective ground level.

effective radiated power(ERP)—The calculated power output from an antenna system which incorporates all the gains and losses in the antenna system. ERP is calculated as follows (1) convert power output of transmitter to dB referenced to 1 W(dBw); (2) subtract all transmission line losses including losses in equipment between the transmitter and antenna

(filter, diplexers, circulators, duplexers, etc.)

expressed in dB; (3) add the antenna’s power gain (expressed in dB reference to a half-wave dimple); and (4) convert the results into watts.

effective signal radiated—The rating basis for licensing radio transmitters. Equal to the square root of the effective radiated power times the antenna height in feet aboveground level.

EKG display console—A unit of electronic equipment located in a hospital emergency room, or cardiac care unit, or both, which displays EKG and records voice and data information received from an EMS scene by transmission via radio or telephone path.

A demodulation display console.

electrocardiogram(ECG or EKG)—A visual or hard copy trace of a patient’s electrical heartbeat information.

electrode—(1) Either of the two terminals of an electric source, such as a battery, (2) A conducting element through which electric current enters or leaves an electrolyte, gas, or vacuum, (3) A conducting element, usually metallic (such as silver/silver

chloride), with a conducting medium or electrolyte (such as sodium chloride and water) attached to a patient to obtain the electrical signals of the heart.

electromagnetic radiation—Radiation associated with a periodical varying electric and magnetic field and is traveling at the speed o flight, including radio waves, light waves, X-rays, and gamma radiation.

electromagnetic wave—A wave of electromagnetic radiation, characterized by variations of electric and magnetic fields.

emergency call—A all that requires immediate action.

emergency medical dispatcher (EMD)—a trained public safety telecommunicator with additional training and specific emergency medical knowledge essential for the efficient management of emergency medical communications.

emergency medical dispatching—The reception and management of requests for emergency medical assistance.

emergency medical dispatch priority reference system (EMDPRS)—A medically approved reference system used by a local dispatch agency to dispatch aid to

medical emergencies, which includes: systematized caller interrogation questions, systematized pre-arrival instructions, and protocols matching the dispatcher'’

evaluation of injury or illness severity with vehicle response mode and configuration

Emergency Medical Service (EMS)—The service utilized in responding to the

perceived individual need for immediate medical care in order to prevent loss of

life or aggravation of physiological or psychological illness or injury.

emergency operations center (EOC)—(1) A secure, protected facility designed and

equipped for the use of community officials to manage response of a community in time of emergency, (2) A communications center designed and operated by a community or within a geographic area for a combination of emergency resources, such as police, fire and EMS.

emergency resource coordination center (ERCC)— Generally a facility that has the resources and ability to coordinate all emergency services (police, fire, EMS, etc.) within a given geographic area. ERCC

works in conjunction with a public safety answering point (PSAP) and may be in the same facility or location.

enclosure—A housing such as a case, cabinet, cabinet rack or console which is designed to provide protection and support to equipment.

encoding—The conversion of numerical address codes, such as telephone number or message codes, into a format of tone or on-off pulses of audio tones for transmission over a communications system, usually

for individual or group addressing, such as for paging or selective calling.

exchange—A defined area, served by one or more telephone central offices, within which the telephone company furnishes service.

exciter—The low level stages of a transmitter which normally consists of an oscillator, modulator and multiplier.

extender board—A printed circuit board that plugs into a module’s circuit connector at one end and the module on the other to maintain a circuit so that the module may be conveniently tested out of an inaccessible position.

F

facility—A communications facility is anything used or available for use in the furnishing of communications service.

facsimile—The process by which pictures, images, and other fixed graphic materials are scanned and the information converted into electrical signals for local use or transmission remotely to produce a likeness

of the subject copy.

fading—The variation of radio field strength caused by a gradual change in the transmission medium.

fade margin—The number of decibels of attenuation which can be added to a specified radio frequency propagation path before the signal-to-noise ratio of the channel falls below a specified minimum.

FCC Part 90—The section of the Federal Communications Commissions Rules and Regulations that affects most EMS communications.

Federal Communications Commission (FCC)—A Board of commissioners appointed by the President under the

Communications Act of 1934 to formulate Rules and Regulations and to authorize use of radio communications. The FCC regulates all communications in the United States by radio or wireline, including

television, telephone, radio facsimile and cable systems.

feedback—The act of returning a portion of the output voltage of a circuit which includes amplification to the input of that circuit.

feedback, acoustic—The feeding back of sound waves from a loudspeaker to a microphone in the same audio system.

field strength—The strength of an electric, magnetic or electromagnetic field. Electromagnetic (radio) field strength is expressed in microvolts per metre or

millivolts per metre.

fixed service—A service or radio communication between specified fixed points. Fixed station: (1) a radio station which is not mobile; (2) a station which

is permanently installed; (3) a base station in a mobile radio system.

fixed relay station—An operational fixed station established from the automatic retransmission of radio communications received from either one or more fixed stations or from a combination of fixed

and mobile stations and directed to a specified location.

F-Layers—The upper layers of ionization in the ionosphere. The f-1 layer is about 130 miles above the earth. The f-2 layer height varies from about 250 miles during the day to about 150 miles at night.

float—To operate a storage battery in parallel with a charger and a load at such voltage that the charger supplies the load current and the battery supplies only transient peaks above the normal load.

FM transmitter—A radio transmitter that emits or radiates a frequency modulated wave.

folded dipole—A receiving or transmitting antenna composed of two parallel dimples, connected at the ends. The connection to the receiver or transmitter is made at the center of one of the poles.

forced disconnect—The capability of the 9-1-1 center to disconnect a 9-1-1 call to avoid caller jamming of the incoming phone lines.

four wire operation—Telephone operation in which the inbound audio signal is carried on one pair of wires and the outbound signal on another pair.

free space loss—The theoretical radiation loss that would occur in transmission if all variable factors were disregarded. Free space loss depends only on the frequency and the distance between antennas.

frequency—The number of cycles, repetitions, or oscillations of a periodic process completed during a unit of time. The frequency of waves in the electromagnetic spectrum (radio waves) is designated in hertz (Hz), kilohertz (kHz = 1000 Hz). One hertz is equivalent to one cycle per second.

frequency modulation (FM)—A method of modulating a carrier-frequency signal by causing the frequency to vary above and below the unmodulated value in accordance with the intelligence signal to be

transmitted. The amount of deviation in frequency above and below the resting frequency is at each instant proportional to the amplitude of the intelligence signal being transmitted. The number of complete deviations per second above and below the resting frequency corresponds at each instant to the frequency of the intelligence signal being transmitted.

frequency response—The transmission loss or gain of a system, measured over the useful bandwidths, compared to the loss or gain at some reference frequency (generally 1000 Hz).

fresnel zone—The circular zone about the direct path between a transmitter and a receive at such a radius that the distance from a point on this circle to the

receiving point has a path length that is some multiple of a half wave length longer than the direct path.

fringe area—An area or locality at such a distance from the transmitter that the signals received are weak.

full-duplex operation—A method of operation of a radio system which provides simultaneous two-way communications between two points. In EMS radio

systems, provides for mutual interrupt capabilities between the field technician and the physician or medical direction at a hospital location.

G

gain, of an antenna—The effectiveness of a directional antenna in a particular direction, compared against a standard (usually an isotopic antenna). The radio of standard antenna power to the directional antenna

power that will produce the same field strength in the desired direction.

generator, standby power—A device which develops electrical voltage from mechanical energy. An a-c electrical power source held in reserve and used to supply the necessary a-c power when commercial power fails.

generator, signal—A portable test oscillator which can be adjusted to provide a test signal at some desired frequency, voltage, modulation, or waveform.

geographical assignment—The assignment and use of communications channels on a dedicated used basis within a given geographic area.

GHz—Gigahertz (billion hertz, 1000 MHz)

gin pole—A pole which is used together with ropes and pulleys as a derrick for lifting heavy loads and for erecting poles or towers.

ground—A reference point. Also a connection, intentional or accidental,

between an electrical circuit and the earth or its equivalent.

ground plan antenna—A type of vertical transmitting or receiving antenna used primarily for short wavelength or high band communications. A ground plane antenna consists of a quarter-wave vertical element, and four radial elements spaced 90° apart, and mounted on the base of the vertical

element. Antennas of this type are non-directional and have a low angle of radiation.

ground wire—A conductor leading from the radio equipment to an electrical connection with the ground.

guard band—A narrow band of frequencies provided between adjacent channels in certain portions of the radio spectrum to prevent interference between stations.

guy anchor—The buried weight or mass to which the lower end of a guy wire is attached.

H

half-duplex channel—A communication channel providing duplex operation at one end of the channel, but not the other. Sometimes, the base station is operated in the duplex mode, however, in EMS the portable or mobile radio is often operated

in the duplex mode, and the base station at the hospital operated simplex, to permit the medical direction physician to interrupt transmissions from the field technician. See also Simplex.

half-duplex operation—Generally refers to the ability of directing medical personnel in EMS radio system to interrupt or ‘break in’ on radio transmissions from field personnel to give instructions or ask questions.

Sometimes referred to as “physician interrupt”. Requires duplexed

communications equipment in the field.

half-wave dipole antenna—A straight, ungrounded antenna having an electrical length equal to half the wave length of the signal being transmitted or received. Mounted vertically, it has a donut-shaped

pattern, circular in the horizontal plane.

ham—A term applied to an amateur radio operator, as opposed to business or commercial operators. A person that makes amateur radio operation a hobby.

harmful interference—Any emission, radiation, or induction which endangers the functioning of a radio service or seriously degrades,obstructs, or repeatedly interrupts a radio communication service.

hand microphone—A microphone designed to be held in the hand. Sometimes called a “palm” microphone.

handset—A device similar to a telephone handset used in place of a hand microphone.

hardcopy—A tangible printed copy of a message such as that obtained from a typewriter.

hardware—The screws, nuts, clamps, anchors, connectors, etc. used in the installation and maintenance of communications systems.

hardwire—To wire or cable directly between units of equipment without passing through other media.

harmonic—An integral multiple of a fundamental frequency. The third harmonic of 20 Hz is 60 Hz. The fifth harmonic of 40 Hz is 200 Hz.

hash—Noise signal produced by an electrical or mechanical source.

headphone—A device which can be placed on the head to allow individual listening to messages.

HEAR—Hospital Emergency Administrative Radio— Motorola Communications and Electronics trade name for a VHF radio system operating on

standard frequencies with a selective calling system between stations. The system is similar to General Electric Mobile Radio Department’s EACOM radio system.

helix—A single layer, spiral wound coil usually having air or foamed polyethylene core.

hetrodyne—(1) pertaining to the production of difference in frequencies (beat frequencies) by the combination

of the two frequencies, (2) to shift an incoming radio signal to a different frequency, often to a lower intermediate frequency.

Hetrodyne frequency—The beat frequency, which is the sum or difference between two frequency signals.

hertz(Hz)—International unit of frequency identical to and used instead of the old term cycles. One hertz is equal to one cycle per second.

high band—A portion of the VHF radio frequency spectrum from 150 to 174 MHz in which two-way radio operates.

hollerith code—A twelve-level code which defines the relation between an

alphanumeric character and the punched holes in an 80-column data card.

hookswitch—The device on which a handset or microphone hangs when not in use. The handset operates a switch, or switches, which open the associated circuits.

hop—(1) The number of reflections from the ionosphere encountered by the radio wave in traveling from the transmitter to the receiver (2) the number of radio links required to span a given path.

hot line—Direct circuit between two or more points for immediate use without patching or switching. (See direct leased land lines) The hot line can employ various signaling configurations (ringdown, audio

amplifier, etc.)

hot standby operation—A method of achieving reliable operation by energizing two identical equipments fed by and to a switchable input and output. A sensing device causes transfer of input and output

circuits when a failure is indicated.

hum—Audio frequency interference which is at the frequency of the power supply or its harmonics.

humidity, relative—The ratio of the amount of water vapor the air contains to the maximum amount it could hold at the same temperature and pressure, expressed in percent.

hybrid—(1) Made up of several different components or a mixture of technologies. (2) A circuit required to convert 4-wire operation to 2 wire, while maintaining isolation of the 4-wire circuit.

I

ignition noise—Interference produced by sparks or other ignition discharged in a vehicle.

image—One of the two groups of sidebands generated in the process of modulations, so called because one is the reverse (mirror image) of the other with respect to operating frequency.

image frequency—In hetrodyne frequency converters, an undesired input frequency which can beat with the local oscillator to produce the intermediate frequency and thus appear in the receiver output.

image rejection—The action of a receiver in suppressing the image frequency.

impedance—The total resistance that a circuit offers to the flow of alternating current. Impedance is a combination of resistance and reactance. The ohm is used as a unit of impedance measurement.

impedance match—The condition in which the impedance of one component is the same as the component to which it is connected or attached.

impedance, characteristic—The importance of characteristic impedance lies in the fact that when a transmission line is terminated, as with an antenna, in an impedance matching its own, then all of the

energy or power flowing along the line is radiated by the antenna. If the impedance of the termination (antenna) is not matched to the transmission line, a portion of the energy will be reflected at the mismatch resulting in a lower output from the antenna.

Improved Mobile Telephone Service (IMTS)—A mobile radio telephone offering of a telephone company.

impulse—A surge of electricity having a single polarity.

indicator—A device used to inform of a condition or change in condition.

induced—Produced as a result of exposure to a changing electric or magnetic field.

Industrial Radio Service—An FCC-designated radio service.

in-band signaling—The transmission of signaling tones within the frequency band of the channel.

insertion loss—The loss introduced when a device or line section is interposed between two elements of a circuit.

insulation—Any nonconductive material used to prevent the leakage of electricity from a conductor, such as rubber, glass, mica, etc.

integrated circuit—A complete circuit consisting of transistors, capacitors, resistors, diodes, etc. which is formed on a single semiconductor substrate.

Integrated Circuit Oscillator Module (ICOM)—A frequency determining circuit used in General Electric radios containing a crystal oscillator circuit and other circuits used to generate the oscillator frequency.

interface—A concept involving the specification of the interconnection between two equipments or systems. The

specification includes the type, quantity, and function of the interconnection circuits and the type and form of the signals to be interchanged via these circuits.

interference—Interference in a signal transmission path is either extraneous power which tends to interfere with the reception of the desired signals or the distribution of signals which results in loss of signal or distortion of information.

intermittent—Not continuously present; disappearing and reappearing.

intermittent duty cycle—A duty cycle of 1 minute on 4 minutes off, or 20% per

electronic industries association (EIA).

intermodulation—The combination of two signals beating together to form a third unusable signal which interferes with the reception of the desired signal. In a radio receiver the method of expressing in dB

below the desired signal, the receiver’s rejection of the unwanted signal to its acceptance of correct signals.

intrinsically safe—A laboratory (UL) rating for equipment considered approved to operate in areas in which hazardous concentrations of flammable gases exist.

inverter—(1) Any of several devices used to convert direct current to alternating current (2) a single input, single output device which changes the polarity of (inverts) a signal when passing it from input to output. A negative signal at the input produces a positive signal at the output and vice versa. A differential EKG amplifier has a normal and an inverting input.

ionosphere—The upper portion of the earth’s atmosphere beginning at about 50 miles above the surface of the earth’ the cause of radio signals being bent, and

returned to earth.

isolator—A passive RF device which permits transmission in only one direction, absorbing energy in the opposite direction.

J

jack—A connecting device ordinarily used to make electrical contact with mating contacts of a plug.

jacket—The outer covering on an insulated wire or cable.

jamming—The deliberate radiation, re-radiation or reflection of electromagnetic energy with the object of impairing the use of electronic devices, equipment or systems.

jumper—A short length of conductor used to bridge electrical connections.

junction box—A metal or other container into which wires or cables are led and connected.

K

key—A push-to-operate switch used for operating a transmitting circuit in a radio system

key telephone equipment—An instrument that has the capability of multiple line terminations. Each line is accessed by depressing an association button (key).

keypunch—A machine controlled by a typewriter like keyboard which enables an operator to punch holes in predescribed places in a hollerith code.

kilo—A prefix meaning one thousand.

kbps—Thousands of bits per second.

kilohertz(kHz)—Equal to 1000 cycles per second. Replaces the term kilocycle.

klystron—An electron tube in which the electrons are periodically bunched by electric fields. Used as an RF oscillator for microwave equipment.

knockout—A metal disc punched in the side of a metal terminal junction box or cabinet which can be punched out to allow entry of a cable or conduit.

L

land line—A generic term which refers to the public-switched telephone system.

lag—The difference in phase angle expressed in electrical degrees between the voltage and current which produced it.

land-mobile—An abbreviation for land to mobile communications such as between base stations and mobile radios or from mobile radio to mobile radio.

Land Mobile Radio Service—A mobile radio service defined by the Federal Communications Commission-FCC Rules and Regulations Part 90.

LATA—Local access and transport area boundaries for telephone companies. The geographic area within which the local telephone company provides local and long distance service.

Law Enforcement Assistance Administration (LEAA)—An

administration under the United States Department of Justice established by the Omnibus Crime Control and Safe Streets Act of 1968, restructured by the Justice Improvement Act of 1979 and abolished two years later.

leased line—A pair of wires or a circuit, usually leased or rented from a telephone company, designed for exclusive use between two fixed points for various

communication control functions.

life cycle—A test performed on a material device to determine the length of time before failure.

line—A transmission lien or power line. A system of one or more wires.

linear—Describing a device in which the signal output voltage is directly proportional to the signal input voltage. A straight line relationship.

line, balanced—A two-wire line which has identical impedance from each wire.

line equalizer—A connection in series with a telephone line that will alter the frequency response characteristics of the line.

line, four-wire—A two-way transmission circuit using separate paths for transmit and receive functions.

line, loss—A transmission line, usually a coaxial cable, which is designed to have very high transmission loss per unit length used in tunnels, underground or buildings for radio communications systems.

line of sight—An unobstructed path between two points. Radio waves at those frequencies where signals travel in a straight line and are not reflected by the ionosphere.

line of sight distance—The straight-line distance from a radio station antenna to horizon. This represents the normal transmitting range of FM transmitting

stations.

link—The portion of a radio relay system between adjacent radio stations.

load—(1) A device that receives power from a transmission system (2)The amount of electric power drawn by an electric or electronic device.

load, dummy—A device which can dissipate energy (into heat) without radiating it.

loading, antenna—Insertion of reactance in an antenna circuit to improve its

transmission characteristic in a given frequency band.

loading, ice—The stress imposed on an antenna or antenna structure caused by ice forming on its members.

loading, wind—The stress imposed on an antenna or antenna structure caused by wind.

lobe—One of the three-dimensional petals representing the radiation or reception efficiency of a directional antenna.

local government radio service—A service of radio communication defined by the FCC essential to official activities of states, possessions, and territories, including counties, towns, cities, and similar governmental subdivisions.

local service area—That area that can be called on the telephone without incurring multimessage units or a toll charge.

log—A list of radio stations showing frequency, location, power, and other data. Also a communication record for a station showing calls made, time, date and other data. A detailed record.

loop—(1) A short transmission line that connects a subscriber to a switchboard (2) A closed path in which a signal may circulate. This path may be within a piece of equipment, such as a repeater or carrier terminal, or may be a complete carrier

circuit.

loop resistance—The resistance presented to the signaling portion of the terminating set by the wireline when the far end of the wireline is short circuited.

loss—A decrease in power suffered by a signal as it is transmitted from one point to another, usually expressed in decibels. Energy dissipated without accomplishing useful work.

loss, free space—The theoretical transmission loss between two radio antennas dependent only upon distance and frequency.

loss, path—The theoretical transmission loss between two

radio antennas dependent only upon distance and frequency.

loss, path—The reduction or attenuation of signal strength that occurs between the transmitted strength and the received signal strength.

low band—A section of the VHF radio frequency spectrum from 25 to 50 MHz in which mobile radio equipment is licensed to operate.

low loss—Describing circuits and transmission line in which little energy is lost from the input to the output.

lower sideband—The lower of two frequencies or of two groups of frequencies produced by a modulation process.

lug, spade—A connector which has an open end to slip under a terminating screw.

M

marginal—Operating at the borderline of permissible limits.

matrix—An array of horizontal and vertical input or output leads with cross points at the intersections, used as a means of switching from any input to any output.

mean—The arithmetic middle point of a range of values, obtained by adding the highest and lowest values and dividing by two.

median—The point below which there are as many instances as there are above.

medical communications control console—An installation of communications control equipment, usually located at a hospital, which provides for control of the transmitting and receiving equipment

necessary for the medical communications.

microwave—A term applied to radio waves in the frequency range of 1,000 MHz and upward. Microwave radio generally performs the same functions as telephone cables, and may be used for radio remote control purposes.

mobile—Term used to describe equipment designed for vehicular installation.

mobile relay station—A fixed station established for the automatic re-transmission of mobile service radio communications which originate on the transmitting

frequency of the mobile stations and which are retransmitted on the receiving frequency of the mobile stations.

mobile repeater station—A mobile station in the mobile service authorized to retransmit automatically on a mobile service frequency communications originated by handheld or portable units or by other mobile or base stations directed to such hand-carried units.

mobile service—A service of radio communications between mobile and land stations, or between mobile stations.

mobile station—A two-way radio station in the mobile service intended to be used while in motion or during halts at unspecified

points.

mobile telephone service (MTS)—Telephone service between a fixed mobile radio base station and several vehicles equipped with mobile radios.

mobile transmitter—A radio transmitter designed for installation in a vehicle, vessel, or aircraft and normally operated while in motion.

mobile unit—A two-way radio equipped vehicle or person. Also sometimes the two-way radio itself, when associated with a vehicle or person.

modem—Contraction of modulator-demodulator.

modular—A construction technique incorporating the use of standard size units for interchangeability.

modulate—To vary the amplitude (AM), frequency (FM),

or phase of a high frequency wave or carrier in step with amplitude variations of another wave (the modulating wave). The carrier is usually a sine wave while the modulating wave is often a complex voice or EKG signal.

modulator—The electronic circuit that combines the modulating wave with the carrier wave. In radio transmitters the final audio-frequency stage which mates the audio signal with the carrier signal. In

EKG telemetry, the circuit that combines the

amplified EKG signal with the subcarrier (audio) signal for transmission by radio or telephone.

multi-channel system—A radio system which uses more than one radio channel. Also known as a multifrequency system.

multicoupler, receiver—A device which permits several radio receivers to use the same antenna. Usually a broadband

amplifier with several output ports.

multi-frequency operation—Employing radio equipment capable of operation on two or more frequencies.

multijurisdictional system—A system covering more than one political boundary or agency.

multipath—The propagation phenomenon which results in signals reaching a radio receiving antenna by two or more paths usually resulting in a degradation of

the original signal.

multiplex—Transmitting two or more signals over the same medium. In EKG telemetry equipment, the ability to transmit electrocardiograph(EKG) signals and voice signals concurrently over the same transmitter.

multiplex, frequency division—A multiplex system in which the total transmission bandwidth is divided into narrower bands each used for a single separate channel.

multiplex, time division—A method of multiplexing in which the total frequency spectrum available is used by each channel, but only for part of the time. A sharing of transmission ability, first by one parameter, then by another.

multi-tone—A method of signaling that involves tow or more tone signals produced simultaneously or sequentially.

mute—To silence or reduce sound level.

N

netting—The process of adjusting a system’s transmitters and receivers to the same operating frequencies.

net loss—The algebraic sum of the gains and losses between two terminals of a circuit.

network—An orderly arrangement of stations interconnected through communications channels in

order to form a coordinated entity.

nine-one-one(9-1-1)—A three-digit emergency telephone number accepted and promulgated by the telephone industry as the nationwide emergency number.

Nxx—The first three digits of a local telephone number that uniquely identifies that central office switching location within its area code number for nationwide long distance call routing.

noise—Interference characterized by undesirable random voltages cause by an internal circuit defect or from some external source. Any extraneous signal tending to interfere with the proper and easy perception of those signals which are intended to be

received.

noise blanker—A device used in mobile radio applications which senses the presence of undesired noise on the desired channel and causes the desired signal to be interrupted for the time period that the

undesired noise signal is present. The time period is controlled and measured in milliseconds so that the interruption of the desired signal is not audible.

noise level—Volume of noise usually expressed in decibels.

noise limiter—A circuit that cuts off the noise peaks that are stronger than the highest peak of the desired signal being received.

nomograph—A chart having three or more scales across which a straightedge can be placed to provide a graphical solution for a particular problem. In mobile radio, nomographs may be used to determine frequency spread, estimated radio range,

antenna height, etc.

O

octave—The interval between two frequencies having a ratio of two to one.

ohm—An electrical unit of resistance.

ohm’s law—The current in an electric

circuit is directly proportional to the electromotive force in the circuit. In the form E=I*R, where E is the electromotive force (voltage), I is the current (amperage), and R is the resistance of the circuit (ohms).

omnidirectional—Equally effective in all directions.

open—A break in circuit continuity

outage—A disruption of communications from any cause, whether planned or accidental.

out-of-band signaling—Transmission of signals by frequencies outside of the voice band.

overload—A load greater than a device is designed to handle.

P

paging—A one-way communications service from a base station to mobile or fixed receivers that provide signaling or information transfer by such means as

tone, tone-voice, tactile, optical readout, etc.

pair—Two wires of a signal circuit generally applied to telephone wherein one wire is designated “tip” and the second wire “ring”.

passive—A device which does not contribute energy to the signal it passes.

passive repeater—A device intentionally interposed in a microwave transmission path to redirect or reflect energy.

patch—A means of connecting one system to another. A patch may be between radio systems, or radio to telephone, as in a radio/phone patch.

path, signal—The route by which intelligence is conveyed from transmitter to receiver or through a circuit.

personal radio—A small portable radio intended to be carried by hand or on the person of the user.

PERT—Program Evaluation and Review Technique. A management tool for comparing actual with scheduled program progress.

phase—The position at any instant which the periodic wave occupies in its cycle of 360°

phone patch—An interconnection between radio and telephone communications circuits which permits direct voice interchange between telephone lines and radio system.

pigtail—A splice made by twisting together the bared ends of two conductors.

plug-in—Describing any device having terminals so it can be connected by simply pushing it into a suitable socket or

connector.

portable—An easily transportable radio.

primary power—A reliable source of electrical power normally serving as the principle source of energy to equipment, such as the commercial 120 volt a-c

power main.

private automatic branch exchange-(PBX)—A telephone switchboard with many stations not individually identifiable to the telephone company’s switching network requiring an operator.

private line(PL)—Motorola’s trademarked name for continuous tone controlled squelch system, CTCSS.

propagation, electromagnetic—The travel of electromagnetic waves through a medium, or the travel of a sudden electric disturbance along a transmission line. Also called wave propagation.

protect—To equip with devices for safeguarding from damage by excessive voltages, current, or physical abuse.

public safety agency—A functional division of a public agency which provides fire fighting, police, ambulance, emergency medical, or other emergency services.

public safety answering point (PSAP)—The initial answering location of a 9-1-1 call and other calls for assistance.

public safety telecommunicator—An individual trained to communicate by electronic means with persons seeking emergency assistance and with agencies and

individuals providing such assistance.

pull box—A box with a removable cover installed in a conduit run to facilitate pulling wire or cable into the conduit.

pulse—A signal of short duration.

pulsed tone—A system of selective signaling using a keyed on-off tone signal.

push-to-talk or press-to-talk(PTT)—In radio or telephone systems, that method of communication over a speech circuit in which transmission occurs from only one station at a time, the talker being required

to keep a switch operated while he is talking. The keying button used to operate a radiotelephone transmitter.

Q

quarter-wave antenna—An antenna electrically equal to one-fourth of the wavelength of the signal to be transmitted or receive.

quartz—An element consisting of pure silicon dioxide. The original piezoelectric material widely used to control the frequency of oscillators.

quartz crystal—A thin square or rectangular slice of quartz which will vibrate at a frequency determined by its thickness.

quiet channel—The RCA Corporation’s trademarked name for continuous tone controlled squelch system (CTCSS).

quieting—Reduction of system noise.

quick-call—Motorola communications Company trademarked name for a system of selective calling, normally using two pairs of two tones each in sequence. Quick Call II uses a pair of sequential tones similar to General Electric’s Type 99 tone system.

R

rack mounting—A method of mounting equipment in which metal panels supporting the equipment are attached to pre-drilled steel channel rails or racks. The dimensions of the panels, the spacing of the rails and the size of the mounting screws are

standardized.

rack unit—In mobile radio generally a rack mounting 19 in. between rails and a height of 1.75 in. per unit.

radio—The transmission and reception of signals by means of electromagnetic waves without a connecting wire.

radio-frequency power—The power associated with any signal consisting of electromagnetic radiation which is used for telecommunications.

radio interference—Undesired disturbance of radio reception. Man-made interference is generated by electric devices, with the resulting interference signals either being radiated through space as electromagnetic waves or traveling over power lines or other conducting media. Radio interference is also due to natural sources such as atmospheric phenomena, such as lightning. Radio transmitters themselves may additionally interfere with each other.

radio network—A number of radio stations, fixed and mobile, in a given geographical area which are jointly administered or which communicate with each other by sharing the same radio channel or channels.

radio common carrier (RCC) —An enterprise that is licensed by the FCC and the Public Utilities Commission to provide radio communications service to the public.

radio receiver—An instrument which amplifies radio frequency signals, separates the intelligence signals from the rf carrier, amplifies the intelligence signal

additionally, and converts the intelligence signal to its original form.

radio relay system (radio relay) —A point-to-point radio transmission system in which the signals are received and retransmitted by one or more intermediate radio stations.

radio transmitter—A radio-frequency power source which generates radio waves for transmission through space.

radome—A dome shaped cover for a parabolic antenna which protects the antenna from the elements and their attenuating effects.

range—Distance over which a radio signal can be transmitted for effective reception or the distance at which a usable signal can be received.

receiver—An electronic device used to detect and amplify transmitted radio signals.

receiver, paging—A small, light, pocket sized receiver used for alerting individuals when they are away from their normal communication instruments.

referral methods—The calling party to a public safety answering point is referred to a secondary telephone number.

refraction—The change of direction experienced by a wave of any form of radiated energy when passing from one medium to another having a different

dielectric constant or index of refraction.

regional EMS system—An emergency medical service area (trade, catchment, market, patient flow, geographic or governmental) that provides essentially all of the definitive emergency medical care for all emergencies and for the most critically ill and injured patients within the area.

relay—Transmission forwarded through an intermediate station.

relay station—Radio stations that rebroadcast signals the instant they are received, so that the signal can be passed on to another station outside the range of the originating transmitter.

reliability—The ability of an item to perform a required function under stated conditions for a stated period of time.

remote base station—A base station located away from the operating console, to take advantage of improved coverage offered by a better geographical location.

remote control—The operation of a device from a distance either electrically or by radio waves.

remote control equipment—The apparatus used for performing monitoring, controlling, supervisory control, or a combination of these functions at a distance by electrical means.

repeater—A combination of apparatus for receiving either one-way or two-way communication signals and delivering corresponding signals which are either

amplified or reshaped or both.

repeater station—An operational fixed station established for the automatic re-transmission of radio communications received from any station in the mobile service.

repeater station, re-modulating—A microwave repeater station in which the signal is demodulated to the original baseband frequencies and re-injected onto

the modulator for transmission to the distant station.

resource management center—A center responsible for the allocation of those resources essential to the most effective and efficient resolution, or management or both, of the immediate problem. In most

communities these resources include police,

fire and emergency medical services. The resource management center is most effective when its responsibilities encompass the whole of public safety response.

ringback—In a public safety answering center, permits the answering point to ring the hung-up telephone on a held circuit. The feature is useful when calling a party has failed to provide all necessary information to the answering point before hanging up.

ringdown—A type of signaling employed in manual operation telephone (as compared to dial) which utilizes a continuos or pulsing a-c signal transmitted over the line.

S

schematic diagram—A diagram or drawing which shows electrical connections of a radio or other electrical device by means of symbols which are used to represent the components.

search lock monitor—A receiving channel scanning scheme which lock the receiver on the first channel received.

selective call—A system for alerting individual or groups of stations by means of coded signals.

selectivity—The ability to select one particular signal from other signals at nearby frequencies. This specification is important in urban areas where radio spectrum congestion exists. The more negative the

dB rating, the better the specification.

selective routing—A routing of telephone call to terminate at a PSAP determined by the location of the calling telephone. This is accomplished by using a computer to process the calling telephone number.

sensitivity—The characteristic of a radio receiver which determines the minimum input signal strength required for a given signal output. In FM, sensitivity is the signal level required to produce e a given ratio

of signal to noise. The more sensitive a receiver is, the weaker the signal it can receive.

service channel—In a microwave system, a voice channel fused for maintenance and fault location. Also called order wire.

service life—The life expectancy of equipment under normal conditions of use.

side tone—The signal that reaches a telephone receiver from the transmitter of the same set by way of a local path within the set.

Signal—The form of a radio wave in relation to the frequency serving to convey intelligence in communication.

signal-to-noise ratio—The ratio of the intensity of the desired signal to that of the undesired noise signal, usually expressed in decibels.

signal strength—A measure of the field intensity caused by a radio transmitter at a particular location within its operating range. Usually expressed as microvolts, or

millivolts of signal.

simplex—1) —single frequency operation whereby all base stations and mobiles operate on one common frequency, (2) operation on two different frequencies in a system that can communicate in two directions, but not simultaneously, such as when a base station and a mobile radio operate on reversed pairs of frequencies without duplexing.

simplex channel—a communication channel providing transmission in one direction only at any given time. For comparison see duplex channel.

simplex operation—A method of radio operation in which communication between two stations takes place in only one

direction at a time. This includes ordinary

transmit-receive operation, press-to-talk operation, voice-operated transmit, and other forms of manual or automatic switching from transmit to receive. Also called simplex.

SINAD —The ratio of signal plus noise plus distortion to the noise plus distortion; expressed in decibels. An EIA standard method of measuring receiver sensitivity. Basically a measure of RF signal strength

that will result in a readable signal.

siren—An acoustical or electromechanical device used as a warning signal on emergency vehicles.

solid state—Denoting the use of semiconductors instead of

vacuum tubes or relays.

Special Emergency Radio Service (SERS) —That portion of radio communications frequency resources authorized by the FCC for use in the alleviation of emergency situations endangering life or property.

See FCC Part 90.

spectrum—A continuous range of frequencies arranged in order of wavelength or frequency within which

waves have some common characteristics, such as audio spectrum, radio spectrum, etc. The entire range of electromagnetic

radiation extending from the longest known radio waves to the shortest known cosmic rays.

spurious response—The response of a radio receiver to an undesired frequency.

squelch—A circuit function that acts to suppress the audio output of a receiver when noise power exceeding a predetermined level is present.

squelch, carrier—A squelch system that responds to the presence of an RF carrier signal.

squelch circuit—A circuit that reduces or lowers the noise that would otherwise be heard in a radio receiver between transmissions.

stability, frequency—The ability of a radio transmitter to maintain any predetermined frequency, such as its assigned frequency. Measured in percent of the carrier. The lower the percentage the better the stability.

standing wave ratio (SWR) —A measure of the amount of lost transmitting power due to impedance differences between the transmission line and the antenna. The ratio of reflected to incident waves that

exists at some particular point on a transmission line.

statewide EMS system—A network of EMS systems, integrated and coordinated at the state level.

strip chart recorder—An electromechanical device used to make paperchart recordings of EKG information. Usually it uses a heat-sensitive paper and a heated stylus.

subcarrier—A frequency sensitive device used to generate a modulated wave which in turn is applied as a modulating wave to modulate another carrier. For EMS telemetry the subcarrier frequency is 1400 Hz.

supergroup—In microwave systems groups of 60 channels each, occupying a particular range of frequencies.

switched network—A complex of diversified channels and equipment that automatically routes communications between the calling and called

person or data equipment. The public telephone system.

synchronization—The process of making the carrier at the receiving end of a line or system match the frequency of the carrier at the transmitting end.

synthesizer, frequency—A highly precise crystal oscillator with frequency dividers used to provide the precise radio frequency. A typical synthesizer can be set to small frequency increments and have an accurate output at the desired output frequency.

system—A combination of two or more stations in such a way as to provide communications.

T

tandem trunking—An arrangement where a telephone-line connection has one or more intermediate points that are required or permitted usually on a controlled dial pulse basis before reaching the final destination (called) party.

tariff—A document filed by a communications company with Public Utilities Commission which lists the

services offered the public and schedule of rates and charges.

tarnish—A discoloration or stain on the surface of metal caused by exposure to chemicals or the atmosphere. To dull or destroy the luster of metal.

tee—A three-way connection in the shape of the letter t.

telecommunications—All forms of electrical transmission of intelligence including: telegraph, telephone, radio, and television. Pertaining to the art and science of communication by these methods.

telemetry—The sensing and measuring of information at some remote location and transmitting the data to a convenient location to be read and recorded.

telpak—An acronym for “telephone package”, a schedule of bulk discount rates for multiple private line telephone services such as AT&T long-lines series 500 tariff offering.

telephone line—A telephone lien from a telephone company central office that is connected to key or non-key telephone equipment.

teletypewriter—An electromechanical device, similar to a typewriter, such that messages typed on the keyboard of the transmitter unit are converted into

electrical signals, which when conveyed to the receiver unit, are printed on paper.

ten signals—A series of coded messages designed to reduce air transmission time and confusion in busy mobile radio systems.

thermal noise—Very small noise voltages that are present in all conductors, caused by the thermal agitation of charged particles within the conductor.

third harmonic—A frequency wave having three times the fundamental frequency value.

threshold—In an FM receiver, the point at which the peaks of the incoming RF signal exactly equal the peaks of the internally generated thermal noise power or the point above which increasing the input

signal strength provides only a dB for dB

improvement in the output signal-to-noise ration.

tip—The ball-shaped contact on the cord (tip) of a plug. One of a pair of telephone wires (the other of which is called the ring).

tone—An audio or carrier of controlled amplitude and frequency used in a selective signaling system or for equipment control purposes.

tone code—A specified character of transmitted tone signals required to effect a particular selection or function.

tone coded squelch—A system whereby a superimposed tone is transmitted with the radio carrier to protect against nuisance type interference.

tone, Type 90—General Electric’s name for a system of single tone signaling. The tones are generally between 1000 and 2400 Hz in two bands.

tone, Type 99—General Electric’s name for its two-tone sequential selective signaling system. Sometimes called Sel-Call. The tones are generally between 520 and 953 Hz.

topographic map—An accurately scaled map having contour lines which show the elevation above sea level. Used in preparing profiles of radio propagation paths.

touch pad—A method of signaling or encoding and decoding address codes by the use of a simple numerical push-button keyboard.

Touchtone—A Bell System trademark used to describe their method of signaling and use of dual tone multifrequency (DTMF) tones.

tower, antenna—A tall antenna support structure used to support one or more antennas or when an antenna must be mounted high above the ground or other

support formation such as a building.

traffic—Used for messages handling by a radio communications system.

transceiver—The combination of radio transmitting and receiving equipment in a common housing, usually for portable or mobile use, and employing common

circuit components for both transmitting and

receiving.

transformer—An electrical device for voltage current transformation, or impedance matching or both.

transfer method—The PSAP interrogator determines the proper responding agency and connects the user to that agency. To perform the necessary dispatching

in accordance with prearranged plans with cooperating agencies.

transient—A rapid, sometimes violent, fluctuation of voltage or current in a circuit usually of short duration caused by switching or changes in load.

transmitter—Apparatus for the production and modulation of radio frequency energy for the purpose of radio communication.

transmission line—A waveguide, coaxial line, or other system of conductors used to transfer signal energy efficiently from one location to another. In communications systems, the coaxial line between the base station and the antenna.

trunk—A circuit used for connecting a subscriber in a central office to all other services in/out of the switching equipment.

trunk line—A telephone line that terminates at a switchboard rather than a telephone.

TSPS—An electronic operating position system whereby operator-handled traffic is routed to its final destination via a central switching machine.

turret—A section of communications control console, containing switches, controls, meters, etc.

two-way radio—A radio that is able to transmit and to receive.

two-wire operation—Uses a single pair (two wires) for both transmitting and receiving.

U

Ultra High Frequency (UHF)—Frequencies between 300 and 3000 MHz.

ultrasonic—Describing frequencies higher than those which are audible. Generally above 20000 Hz.

unbalanced line—A transmission line in which the voltages on the two conductors are unequal.

Underwriters Laboratories, Inc.—A laboratory sponsored by the National board of Fire Underwriters which examines and tests devices, material and equipment

whose action may affect casualty, fire, and life hazard.

unmodulated—Without modulation; the RF carrier signal alone as it exists during pauses in conversations.

upper sideband—The higher of two frequencies or groups of frequencies produced by a modulation process.

utility—A power, gas, or water service available to the public.

V

Van Allen belts—Radiation belts that surround the earth, consisting of electrons and protons at high energy levels.

varactor—A semiconductor diode used as a variable capacitor. Used as a harmonic generator, frequency multiplier, and amplifier.

vehicular repeater station—A mobile station in the mobile services authorized to retransmit automatically on a mobile service frequency, communications originated by hand carried portable units or by other mobile or base stations directed to such hand-carried units.

Versatone—General Electric company trade name for a solid state tuned tone determining element.

vertical antenna—A vertical steel tower, rod or shaft used as an antenna.

Very High Frequency (VHF)—Frequency between 30 and 300 MHz.

Vibrasponder—Motorola Communications company trade name for a tone determining vibrating reed element.

voice grade—A communications circuit which is nominally 300 to 3000 Hz.

voltage standing wave ratio (VSWR)—The ratio of the

maximum voltage to the minimum voltage along a transmission line. It is the measure of the mismatch between the load and the line.

volume control—A potentiometer voltage divider used to

adjust the loudness of an audio circuit.

volume unit (VU)—A measure of the magnitude of sound

from an electrical wave. Measured in decibels.

voting—Automatic selection of remote radio receiver. Al incoming signals are compared for signal strength and the first signal found that meets or exceeds a

preset level is selected and sent to the audio

amplifier.

W

watt—The unit of power.

wattmeter—A meter to indicate the rate at which electrical energy is being used or produced.

wave—A propagated periodic disturbance such as a radio, light or sound wave.

waveguide—A transmission line comprising a hollow conducting tube within which electromagnetic waves may be propagated. Generally used in microwave communications systems.

wavelength—The distance measured along the direction of propagation between tow points that are in phase on adjacent waves. A wavelength is the distance traveled by a wave in the time of one cycle. Electromagnetic waves included both light and radio waves and travel in space at approximately 300,000,000 m/s. To determine the exact length of a wave, divide 300,000,000 m by the frequency in hertz.

wave, radio—An electro-magnetic wave which travels through space at the speed of light.

wave, refracted—A radio wave that is bent (refracted) as it travels into a second medium of propagation, such as from the atmosphere to the ionized layers of the stratosphere.

weatherproof—So constructed or protected that exposure to the weather elements will not prevent proper operation.

weathertight—So constructed that exposure to a driven rain will not result in the entrance of water.

wire—A single metallic conductor.

# ADDENDUM

| Interoperability Channel Naming |
| --- |
| Names for Channels Coordinated/Managed by CalSIEC |
| April 4, 2008 - Subscriber Programming Shown |
| Yellow = Narrow (12.5 kHz) only with original FCC name shown | N = 12.5 kHz bandwidth | MW = 20 kHz bandwidth |  | W = 25 kHz bandwidth |
| Before Rebanding/Narrowbanding (Legacy Names) |  | Post-Rebanding/Narrowbanding |
| Current Name | Rx FREQ | Rx CTCSS | Tx FREQ | Tx CTCSS | Bandwidth |  | NPSTC Name | Short Name (6 char) | Rx FREQ | Rx CTCSS | Tx FREQ | Tx CTCSS | Bandwidth |
| VHF LOW BAND |  | VHF LOW BAND |
| CLEMARS 7 | 39.4600 | 156.7 | 45.8600 | 156.7 | W |  | LLAW1 | LLAW1 | 39.4600 | 156.7 | 45.8600 | 156.7 | W |
| CLEMARS 6 | 39.4600 | 156.7 | Simplex | 156.7 | W |  | LLAW1D | LLAW1D | 39.4600 | 156.7 | Simplex | 156.7 | W |
| Pending FCC | 39.4800 is used by various agencies in California |  | LFIRE2 (pend) | LFIRE2 | 39.4800 | 156.7 | Simplex | 156.7 | W |
| CLEMARS 7 Input | 45.8600 | 156.7 | Simplex | 156.7 | W |  | LLAW3D | LLAW3D | 45.8600 | 156.7 | Simplex | 156.7 | W |
| None | 45.8800 | 156.7 | Simplex | 156.7 | W |  | LFIRE4 | LFIRE4 | 45.8800 | 156.7 | Simplex | 156.7 | W |
| VHF HIGH BAND |  | VHF HIGH BAND |
| VCALL | 155.7525 | none | Simplex | none | N |  | VCALL10 | VCAL10 | 155.7525 | 156.7 | Simplex | 156.7 | N |
| VTAC1 | 151.1375 | none | Simplex | none | N |  | VTAC11 | VTAC11 | 151.1375 | 156.7 | Simplex | 156.7 | N |
| VTAC2 | 154.4525 | none | Simplex | none | N |  | VTAC12 | VTAC12 | 154.4525 | 156.7 | Simplex | 156.7 | N |
| VTAC3 | 158.7375 | none | Simplex | none | N |  | VTAC13 | VTAC13 | 158.7375 | 156.7 | Simplex | 156.7 | N |
| VTAC4 | 159.4725 | none | Simplex | none | N |  | VTAC14 | VTAC14 | 159.4725 | 156.7 | Simplex | 156.7 | N |
|  |  |  |  |  |  |  | VTAC17 | VTAC17 | 161.8500 | 156.7 | 157.2500 | 156.7 | W |
|  |  |  |  |  |  |  | VTAC17D | TAC17D | 161.8500 | 156.7 | Simplex | 156.7 | W |
|  |  |  |  |  |  |  | VTAC18 | VTAC18 | 161.8250 | 156.7 | 157.2250 | 156.7 | W |
|  |  |  |  |  |  |  | VTAC18D | TAC18D | 161.8250 | 156.7 | Simplex | 156.7 | W |
| WHITE 1 | 154.2800 | none | Simplex | none | W |  | VFIRE21 | VFRE21 | 154.2800 | 156.7 | Simplex | 156.7 | N |
| WHITE 2 | 154.2650 | none | Simplex | none | W |  | VFIRE22 | VFRE22 | 154.2650 | 156.7 | Simplex | 156.7 | N |
| WHITE 3 | 154.2950 | none | Simplex | none | W |  | VFIRE23 | VFRE23 | 154.2950 | 156.7 | Simplex | 156.7 | N |
|  |  |  |  |  |  |  | VFIRE24 | VFRE24 | 154.2725 | 156.7 | Simplex | 156.7 | N |
|  |  |  |  |  |  |  | VFIRE25 | VFRE25 | 154.2875 | 156.7 | Simplex | 156.7 | N |
|  |  |  |  |  |  |  | VFIRE26 | VFRE26 | 154.3025 | 156.7 | Simplex | 156.7 | N |
|  |  |  |  |  |  |  | VMED28 | VMED28 | 155.3400 | 156.7 | Simplex | 156.7 | N |
|  |  |  |  |  |  |  | VMED29 | VMED29 | 155.3475 | 156.7 | Simplex | 156.7 | N |
| NLEMARS | 155.4750 | none | Simplex | none | W |  | VLAW31 | VLAW31 | 155.4750 | 156.7 | Simplex | 156.7 | N |
|  |  |  |  |  |  |  | VLAW32 | VLAW32 | 155.4825 | 156.7 | Simplex | 156.7 | N |
| Current Name | Rx FREQ | Rx CTCSS | Tx FREQ | Tx CTCSS | Bandwidth |  | NPSTC Name | Short Name (6 char) | Rx FREQ | Rx CTCSS | Tx FREQ | Tx CTCSS | Bandwidth |
| CLEMARS 1 | 154.9200 | none | Simplex | Varies | W |  | CALAW1 | CALAW1 | 154.9200 | none | Simplex | 156.7 | N |
| CLEMARS 2 | 154.9350 | none | Simplex | Varies | W |  | CALAW2 | CALAW2 | 154.9350 | none | Simplex | 156.7 | N |
| CALCORD | 156.0750 | none | Simplex | none | W |  | CALCORD | CACORD | 156.0750 | none | Simplex | None | N |
| UHF |  | UHF |
| UCALL | 453.2125 | none | 458.2125 | none | N |  | UCALL40 | UCAL40 | 453.2125 | none | 458.2125 | 156.7 | N |
| UCALLD | 453.2125 | none | Simplex | none | N |  | UCALL40D | CAL40D | 453.2125 | none | Simplex | 156.7 | N |
| UTAC1 | 453.4625 | none | 458.4625 | none | N |  | UTAC41 | UTAC41 | 453.4625 | none | 458.4625 | 156.7 | N |
| UTAC1D | 453.4625 | none | Simplex | none | N |  | UTAC41D | TAC41D | 453.4625 | none | Simplex | 156.7 | N |
| UTAC2 | 453.7125 | none | 458.7125 | none | N |  | UTAC42 | UTAC42 | 453.7125 | none | 458.7125 | 156.7 | N |
| UTAC2D | 453.7125 | none | Simplex | none | N |  | UTAC42D | TAC42D | 453.7125 | none | Simplex | 156.7 | N |
| UTAC3 | 453.8625 | none | 458.8625 | none | N |  | UTAC43 | UTAC43 | 453.8625 | none | 458.8625 | 156.7 | N |
| UTAC3D | 453.8625 | none | Simplex | none | N |  | UTAC43D | TAC43D | 453.8625 | none | Simplex | 156.7 | N |
| CLEMARS 5 | 460.0250 | Varies | 465.0250 | Varies | W |  | CALAW4 | CALAW4 | 460.0250 | 156.7 | 465.0250 | Varies | N |
| CLEMARS 4 | 460.0250 | Varies | Simplex | Varies | W |  | CALAW4D | CLAW4D | 460.0250 | 156.7 | Simplex | Varies | N |
| SCMA C | 484.2125 | 167.9 | 487.2125 | 146.2 | W |  | SCMA C | SCMA C | 484.2125 | 167.9 | 487.2125 | 146.2 | N |
| SCMA E | 484.2125 | 167.9 | 487.2125 | 167.9 | W |  | SCMA E | SCMA E | 484.2125 | 167.9 | 487.2125 | 167.9 | N |
| SCMA N | 484.2125 | 167.9 | 487.2125 | 156.7 | W |  | SCMA N | SCMA N | 484.2125 | 167.9 | 487.2125 | 156.7 | N |
| SCMA W | 484.2125 | 167.9 | 487.2125 | 173.8 | W |  | SCMA W | SCMA W | 484.2125 | 167.9 | 487.2125 | 173.8 | N |
| SCMA D | 484.2125 | 167.9 | Simplex | 167.9 | W |  | SCMA D | SCMA D | 484.2125 | 167.9 | Simplex | 167.9 | N |
| CLEMARS 22 | 484.2375 | none | Simplex | 156.7 | W |  | CALAW5D | CLAW5D | 484.2375 | 156.7 | Simplex | 156.7 | N |
| FDUMA | 487.2375 | none | Simplex | 156.7 | W |  | FDUMA | FDUMA | 487.2375 | 156.7 | Simplex | 156.7 | N |
| 800 MHz |  | 800 MHz |
| ICALL | 866.0125 | 156.7 | 821.0125 | 156.7 | MW |  | 8CALL90 | CAL90 | 851.0125 | 156.7 | 806.0125 | 156.7 | MW |
| ICALLD | 866.0125 | 156.7 | Simplex | 156.7 | MW |  | 8CALL90D | CAL90D | 851.0125 | 156.7 | Simplex | 156.7 | MW |
| ITAC 1 | 866.5125 | 156.7 | 821.5125 | 156.7 | MW |  | 8TAC91 | TAC91 | 851.5125 | 156.7 | 806.5125 | 156.7 | MW |
| ITAC 1D | 866.5125 | 156.7 | Simplex | 156.7 | MW |  | 8TAC91D | TAC91D | 851.5125 | 156.7 | Simplex | 156.7 | MW |
| ITAC 2 | 867.0125 | 156.7 | 822.0125 | 156.7 | MW |  | 8TAC92 | TAC92 | 852.0125 | 156.7 | 807.0125 | 156.7 | MW |
| ITAC 2D | 867.0125 | 156.7 | Simplex | 156.7 | MW |  | 8TAC92D | TAC92D | 852.0125 | 156.7 | Simplex | 156.7 | MW |
| ITAC 3 | 867.5125 | 156.7 | 822.5125 | 156.7 | MW |  | 8TAC93 | TAC93 | 852.5125 | 156.7 | 807.5125 | 156.7 | MW |
| ITAC 3D | 867.5125 | 156.7 | Simplex | 156.7 | MW |  | 8TAC93D | TAC93D | 852.5125 | 156.7 | Simplex | 156.7 | MW |
| ITAC 4 | 868.0125 | 156.7 | 823.0125 | 156.7 | MW |  | 8TAC94 | TAC94 | 853.0125 | 156.7 | 808.0125 | 156.7 | MW |
| ITAC 4D | 868.0125 | 156.7 | Simplex | 156.7 | MW |  | 8TAC94D | TAC94D | 853.0125 | 156.7 | Simplex | 156.7 | MW |
| CLEMARS 9 | 868.5125 | none | 823.5125 | 156.7 | MW |  | CALAW8 | CALAW8 | 853.5125 | 156.7 | 808.5125 | 156.7 | MW |
| CLEMARS 8 | 868.5125 | none | Simplex | 156.7 | MW |  | CALAW8D | CLAW8D | 853.5125 | 156.7 | Simplex | 156.7 | MW |
| Current Name | Rx FREQ | Rx CTCSS | Tx FREQ | Tx CTCSS | Bandwidth |  | NPSTC Name | Short Name (6 char) | Rx FREQ | Rx CTCSS | Tx FREQ | Tx CTCSS | Bandwidth |
| CLEMARS 21 | 866.2000 | none | 821.2000 | 156.7 | MW |  | CALAW9 | CALAW9 | 851.2000 | 156.7 | 806.2000 | 156.7 | MW |
| CLEMARS 20 | 866.2000 | none | Simplex | 156.7 | MW |  | CALAW9D | CLAW9D | 851.2000 | 156.7 | Simplex | 156.7 | MW |
| FIREMARS | 868.9875 | 156.7 | 823.9875 | 156.7 | MW |  | CAFIRE1 | CFIRE1 | 853.9875 | 156.7 | 808.9875 | 156.7 | MW |
| FIREMARSD | 868.9875 | 156.7 | Simplex | 156.7 | MW |  | CAFIRE1D | CFRE1D | 853.9875 | 156.7 | Simplex | 156.7 | MW |
| FIREMARS2 | 866.9125 | 156.7 | 821.9125 | 156.7 | MW |  | CAFIRE2 | CFIRE2 | 851.9125 | 156.7 | 806.9125 | 156.7 | MW |
| FIREMARS2D | 866.9125 | 156.7 | Simplex | 156.7 | MW |  | CAFIRE2D | CFRE2D | 851.9125 | 156.7 | Simplex | 156.7 | MW |
| Permitted Use Only: Reno VHF Public Coast Service Area #34, including California counties of Alpine, Inyo, Lassen, Mono, Plumas and Sierra. |
| Permitted Use Only: Southern California UHF TV-Band sharing area (primarily LA County). |
| Permitted Use Only: NPSPAC Region 6 (48 Northern California counties). |